## Slide 1
Telemetry and Telecommand Packet Utilization
The ECSS-E-ST-70-41C
-------
Training Material
Arnaud Bourdoux – ESA/TEC-SWF
Serge Valera – ESA/TEC-SWT

## Slide 2: ECSS-E-ST-70-41C Training
Part 1
The Packet Utilisation Standard and its place in space engineering
What is PUS?
Its relationship with EGSE & Mission Control Systems
Its use on-board
  the EarthCare example
  the Spacebel OBSW architecture example
Its place in ECSS
Its relationship with CCSDS
Space to Ground exchanges:
  multiplexing
  protocol stack
  space packets & transfer frames

## Slide 3: ECSS-E-ST-70-41C Training
Part 2
The Standardized Service Types
Background & History
The PUS Foundation Model
  the service type abstraction level
  the service type deployment abstraction level
The PUS standardized service types
  including per service type:
  important concepts
  message types – requests & reports
  tailoring & deployment
  implementation guidelines
  foundation model
  PUS-A to PUS-C evolution

## Slide 4
1:
The Packet Utilisation Standard and its place in the Space Engineering

## Slide 5: What is PUS?
The PUS complements the CCSDS space packet protocol standard by defining the application-level interface between ground and space
It covers nominal, contingency and troubleshooting operations for both AIV and mission operations
It provides operational concepts and a set of on-board services meeting them
It defines TM & TC packets (including structures) to exploit the on-board services
It promotes the selection and tailoring of the on-board services according to the needs of a given mission
It allows mission-specific extensions
Notes: ESA has developed standards for packet telemetry and telecommand, which are derived from the recommendations of the Inter-Agency Consultative Committee for Space Data Systems (CCSDS). These standards are now mandatory for future ESA programs as well as for many programs currently under development. However, while these packet standards address the end-to-end transfer of telemetry and telecommand data between applications on the ground and application processes on-board, they leave open the internal structure or content of the packets.

## Slide 6
The PUS:
its relationship with EGSE & Mission Control Systems

## Slide 7: What are EGSE and MCS ?
EGSE (Electrical Ground Support Equipment)
 system used to support all stages of assembly, integration and verification (AIV) of the satellite and its components
MCS (Mission Control System)
 system used to monitor and control both the space and ground segments after launch

## Slide 8: A typical AIV configuration

## Slide 9: A typical operations configuration

## Slide 10: What do Monitoring and Control imply?
For AIT:
requests to and reports from the unit under test
requests to and reports from the SCOEs (special checkout equipment)
For operations:
requests to and reports from the spacecraft
requests to and reports from the ground segment equipment
Notes: Example of ground segment equipment : the ground stations

## Slide 11: A typical commanding sequence
The user reacts to the verification reports as necessary
(e.g. rectifies malfunction)
The user requests the initiation of an activity
The request is routed to its final
destination e.g. Spacecraft or SCOE
The Destination e.g. Spacecraft or SCOE
verifies that the request has not been corrupted
generates the acceptance verification notification and relevant verification report
forward the request to the service responsible of its execution
The Service:
executes the request
generates the execution verification notifications and relevant verification reports
The EGSE:
interprets the verification reports
react to the verification reports
routes the verification reports to the source of the request
The verification reports are routed to the source of the request
The EGSE:
verifies that the request’s arguments are within the expected ranges
verifies that the preconditions are met prior to releasing the command
encodes the request into a TC Packet or a SCOE command

## Slide 12: A typical commanding sequence
The EGSE distributes the reporting data to the users.
The Spacecraft (or SCOE) generates
reports i.e. telemetry (or observations)
The EGSE:
verifies the integrity of the report (i.e. no corruption during routing)
extracts raw values of the data contained within the report , i.e. the ECSS-E-70 reporting data
interprets (e.g. calibrates) the raw values to engineering values
checks the engineering values against predefined health criteria
reacts to out of limits
The reports are routed to the EGSE

## Slide 13
The PUS:
its use on-board

## Slide 14: An example: the EarthCARE mission
Base Platform: Astrium Limited
Launcher:
Vega-C (Kourou)
Alt. Falcon-9 (Cape Canaveral)
Satellite Prime Contractor: Astrium GmbH
ESA Kiruna Ground Station
Star Tracker: Jena-Optronik GmbH
Multispectral Imager: SSTL
Broadband Radiometer: SEA Ltd.
Flight Operation Segment: ESOC
Backscatter Lidar: Astrium-SAS
Cloud Profiling Radar: JAXA
Onboard Computer: RUAG Aerospace
Payload Data Segments:
ESRIN
JAXA for CPR
Notes: Slide updated for launcher since 2018…

## Slide 15: The EarthCARE spacecraft, 1

## Slide 16: The EarthCARE spacecraft, 2
Mission Duration:
  3 years (including 6-month commissioning)
Orbit:
  LEO – Frozen Orbit – SSO
  Mean spherical altitude: 393 km (Routine) / 394.4 km (Cal/Val)
  Attitude control: 3-axis stabilised, yaw-steering control
Dry Launch Mass: approx. 2000 kg
Payload
  2 active instruments: ATLID & CPR
  2 passive instruments: BBR & MSI
Power Sub-system
  Deployable solar array, GaAs triple junction cells, 21 m2
  Average Power consumption: 1645 W
Communication Links
  Average: <15 kbps (housekeeping) & <2.5 Mbps (science)
  S-Band:
    Uplink: 64kbps (max 10 TCs/s)
    Downlink (with/without ranging): 128 kbps/1 Mbps
  X-Band downlink (for science data & stored HKTM): 150 Mbps

## Slide 17: EarthCARE – the S/C architecture
ATLID
BBR
CPR
MSI
MMFU
X-Band link
ESRIN
uni-directional
S-Band Transponder
S-Bandlink
ESOC
bi-directional
PCDU
P/F Thermal Control
Thermistors & heaters
Li-Ion Battery
Solar Array
HDRM
SADM
SADE
CESS
AAD
Magneto meter
Star tracker
RMU
GPS
RCS system
Reaction Wheel
Magneto torquer
GPS sync.
1 Hz
System
synchronization
On-board computer
Remote interface unit
downlink
uplink
T
T
MIL-STD 1553 P/F
Measurement data I/F
Discrete & serial I/O
MIL-STD 1553 P/L
T
T

## Slide 18: EarthCARE – the redundancies
ATLID
BBR
CPR
MSI
MMFU
X-Band link
ESRIN
uni-directional
S-Band Transponder
S-Bandlink
ESOC
bi-directional
PCDU
P/F Thermal Control
Thermistors & heaters
Li-Ion Battery
Solar Array
HDRM
SADM
SADE
CESS
AAD
Magneto meter
Star tracker
RMU
GPS
RCS system
Reaction Wheel
Magneto torquer
GPS sync.
1 Hz
System
synchronization
On-board computer
Remote interface unit
downlink
uplink
T
T
MIL-STD 1553 P/F
Measurement data I/F
Discrete & serial I/O
MIL-STD 1553 P/L
T
T
Redundancy:
cR
hR
hR
iR
iR
iR
iR
iR
iR
iR
iR
iR
iR
iR
cR
cR
cR
cR
cold
iR
internal
hR
hot

## Slide 19: EarthCARE – a PUS A compliant S/C
ATLID
BBR
CPR
MSI
MMFU
X-Band link
ESRIN
uni-directional
S-Band Transponder
S-Bandlink
ESOC
bi-directional
PCDU
P/F Thermal Control
Thermistors & heaters
Li-Ion Battery
Solar Array
HDRM
SADM
SADE
CESS
AAD
Magneto meter
Star tracker
RMU
GPS
RCS system
Reaction Wheel
Magneto torquer
T
T
T
T
System
synchronization
GPS sync.
1 Hz
On-board computer
Remote interface unit
downlink
uplink
MIL-STD 1553 P/L
MIL-STD 1553 P/F
Measurement data I/F
Discrete & serial I/O
PUS
PUS
PUS
PUS
PUS
PUS
PUS
1,2,3,5,8,12,17,19
140,145
1,2,3,5,6,8,9,11,12,14,15,17,19 140,142,145,148,149,151
1,2,3,5,6,8,9,12,15,17,19
140
1,3,5,8,9,17
140
1,3,5,17
140  Parameter management
142  functional monitoring
145  S/C state vector distribution
148  OBCP
149  thermal control
151  on-board position scheduler
PUS

## Slide 20
An example:
A compliant software architecture

## Slide 21: An example: PUS in OBSW
Notes: This slide presents the Spacebel On-board Software overall architecture, and illustrates the PUS as a component of the generic software component, i.e. present on all missions, whatever the platform or application
[TBD] Move this slide next to the EarthCare space segment presentation

## Slide 22
The PUS:
its place in ECSS

## Slide 24: EGSE & ECSS
E-70-01
Satellite On-board Control Procedures
E-70-21
EGSE and Mission Control System
E-70-32
Test and Operations Procedure Language
E-70-31
Monitoring and Control Data Definition
E-70-41
Telemetry and Telecommand Packet Utilisation
E-70
Ground Systems and Operations: Principles and Requirements
E-50-04
Telecommand protocols, sychronization and channel coding
E-50-03
Telemetry transfer frame protocol
E-70-11
Space Segment Operability

## Slide 25: MCS & ECSS
E-70-01
Satellite On-board Control Procedures
E-70-21
EGSE and Mission Control System
E-70-42
Space Link Extension
E-70-32
Test and Operations Procedure Language
E-70-31
Monitoring and Control Data Definition
E-70-41
Telemetry and Telecommand Packet Utilisation
E-70
Ground Systems and Operations: Principles and Requirements
E-70-11
Space Segment Operability
E-50-04
Telecommand protocols, sychronization and channel coding
E-50-03
Telemetry transfer frame protocol

## Slide 26: Standards status (June 2022)
E-70-01
Satellite On-board Control Procedures
E-70-21
EGSE and Mission Control System
E-70-42
Space Link Extension
E-70-32
Test and Operations Procedure Language
E-70-31
Monitoring and Control Data Definition
E-70-41
Telemetry and Telecommand Packet Utilisation
E-70
Ground Systems and Operations: Principles and Requirements
E-70-11
Space Segment Operability
E-50-04
Telecommand protocols, sychronization and channel coding
E-50-03
Telemetry transfer frame protocol
N.W.I.P.
N.W.I.P.
N.W.I.P.
Not released
some rework needed
Not released
C rev1 WG
C rev1 WG
Notes: This slide aims at providing the current status of the E-70 branch (and relevant E-50) standards. The presented situation is as of May 2018.
E-70-01 (OBCP) and E-70-41 (PUS) have both been published in their C version.
E-70-11 (Operability), E-70-31 (M&C data) and E-70-32 (Procedures) have been published in their C version, but are impacted by the up-issue of the PUS. Work is in progress for the update of these standards (lessons learned & related projects).
E-70-21 (MCS) needs to be reassessed
E-50-03 (TC) and E-50-04 (TM) may require an update and need to be assessed for full coverage against the previous ESA standards (Packet Telemetry & Packet Telecommand)
E-70-42 (SLE) has not been published yet and is not foreseen to be published in the near future.

## Slide 27
The PUS:
its relationship with CCSDS

## Slide 28: CCSDS
  Reports:
    Blue Recommended Standards
    Magenta Recommended Practices
    Green Informational Reports
    Orange Experimental or ongoing research
    Yellow Record, but not Historical
    Silver Historical
Consultative Committee for Space Data Systems
CCSDS blue books of direct relevance:
CCSDS 133.0-B-1: Space Packet Protocol (incl. 2 errata)
CCSDS 727.0-B-4: CCSDS File Delivery Protocol

## Slide 29
Space to Ground Exchanges

## Slide 30
... Multiplexing

## Slide 31: Why multiplexing?
Physical Layer
Network Layer
Space Packet Protocol
Data Link Layer Data Link Protocol Sublayer
Data Link Layer Sync & Coding Sublayer
spacelink
space multiplexing
sync & coding
time multiplexing
physical channel
PhC
continuous
symbol stream
synchronous
transmission
continuous
frames stream
master channel
SCID
MC
asynchronous
transmission
asynchronous
transmission
virtual channels
VCID
fixed length transfer frames
VC
VC
VC
variable length
source packets
packet channels
APID
asynchronous
production
Data
Data
Data
Notes: From
asynchronous production
of variable length data packets
by the applications
To
Synchronous/continuous transmission
of fixed length frames
over the spacelink

## Slide 32: Flow multiplexing
APIDs/MAPIDs
VCIDs
Another is the mapping
of Virtual Channels
on Physical Channels
(Time Multiplexing)
Aggregates data flows from different source into a single transmission channel (on the sending side)
… and dispatch these aggregated data flows to their respective destinations (on the receiving side)
Need to add some routing or
adressing information
and to perform some encapsulation and
extraction
Directly linked with
Space multiplexing and
Time multiplexing
Example is the mapping
of Packet Channels
on Virtual Channels
(Space Multiplexing)

## Slide 33: Space multiplexing
Fill Packet
Asynchronous Variable Length Source Packets
Asynchronous Fixed Length Transfer Frames
Aggregation of
Several Packets in a One Frame
Segmentation of One Packet in Several Frames
Move from variable length data unit (packets) to fixed length data unit (frames) in view of transmission (sending side)
… and rebuild the variable length packets from the fixed length frames (receiving side)
Gapless or Non Gapless Mode
Blocking or Non Blocking
Transmission Time Out
Fill Packet
First Header Pointer
Packet Length
Sequence Flags

## Slide 34: Time multiplexing
Idle Frame
Asynchronous Fixed Length Transfer Frames
Synchronous (Continuous) Bit Stream
Various possible Multiplexing Schemes
  Fixed Assignement
  Round Robin
  Priority Based
  Hybrid
  …
Move from asynchronous generation of fixed length data unit
to synchronous transmission of these fixed length data unit
in view of robust continuous emission (sending side)
Synchronisation Pattern
no need for specific processing on the receiving side
(apart dispacthing of the multiplexed flows – see previous)

## Slide 35
... Protocol stack

## Slide 36
ECSS
CCSDS
IETF
AOS space data link
protocol
RF & modulation systems
TM synchronisation &
channel coding
TC synchronisation &
channel coding
TM space data link
protocol
TC space data link
protocol
space packet
protocol
SCPS-NP
SCPS-SP
SCPS-TP/FTP
SCPS-FP/FTP
Proximity-1
data link layer
Proximity-1
coding & sync layer
proximity-1
physical layer
lossless
data compression
image
data compression
application
specific
protocols
CCSDS
file
delivery
protocol
CFDP
physical layer
data link layer
network layer
transport layer
application layer
The
PUS
IP V4
IP V6
IPSec
TCP
UDP
FTP
HTTP
data link protocol sublayer
sync & coding sublayer
no presentation layer
/
no session layer
PUS & OSI open systems interconnection

## Slide 37
... Space packets and transfer frames

## Slide 38: Space Packet
PUS TC Packet Data Field
TM Data Field
Space Packet Secondary Header
Variable (1 to 65536 bytes)
TM and TC Space Packets are Identical
PUS TM Packet Data Field
TM Data Field
Space Packet Secondary Header
Variable (1 to 65536 bytes)
Space Packet
Variable (7 to 65542 bytes)
Packet Primary Header
Packet Data Field
TC Transfer Frame
Transfer Frame Primary Header
Transfer Frame Trailer
Transfer Frame Data Field
TM Transfer Frame
Transfer Frame Primary Header
Transfer Frame Trailer
Transfer Frame Data Field
TM and TC Transfer Frames are Different
TM and TC PUS Packets
are Similar
Notes: This set of slides presents the way PUS packets are transferred over the physical link, down to the transmission frames.
TM and TC space packets are identical in terms of structure. They both have the same packet primary header format.
A PUS packet is the complete space packet, including the packet primary header and the instantiated packet data field
Space packets are transferred over TC and TM transfer frames, which are completely different from each other. These packets are explicited in the next few slides.

## Slide 39: TC Space packet
Space Packet
Variable (7 to 65542 bytes)
Packet Primary Header
6 bytes
Packet Identification
2 bytes
Packet
Sequence
Control
2 bytes
Packet Version Number
3 bits
Packet Type
1 bits
Secondary Header
Flag
1 bits
Application Process Id
11 bits
Sequence Flags
2 bits
Packet Sequence
Count
14 bits
Packet Data Length
2 bytes
16 bits
Packet Data Field
Variable (1 to 65536 bytes)
Packet Secondary
Header
(Data
Field
Header)
variable
User
Data
Field
variable
Packet
Error
Control
16 bits
Time Code Field
Var.
Ancillary Data
Field
Var.
Application
Data
Var.
Spare
Var.
Notes: The TC space packet is composed of a primary header and a packet data field.
The primary header contains a packet identification, essentially made of the application ID and several flags; a packet sequence control, with a sequence count used to identify the packet and sequence flags which are not used by the PUS standard (always “stand alone”).
In terms of secondary header, the space packet protocol only requires a time code field and an ancillary data field. These are populated according to the PUS definitions. The same goes for the end for the packet containing the application data and the CRC.

## Slide 40: TC Transfer frame
Transfer Frame
Variable (up to 1024 bytes)
Transfer Frame Trailer
16 bits
Frame
Error Control Field
Transfer Frame Data Field
Variable (up to 1019 bytes)
Transfer Frame Primary Header
5 bytes
TC Transfer Frame are Variable Length
(TM Transfer Frames are Fixed Length)
Space Packet
Space Packet Data Field
Space Packet Primary Header
Segment Header
Sequence
Flags
Multiplexer
Access
Point
Id
2 bits
6 bits
Segment
Data
Field
Variable (up to 1018 bytes)
1 byte
Variable (up to 65542 bytes)
TC Multiplexing is based on additional Segment Header
In Transfer Frame Data Field
(TM Multiplexing is based on standard First Header Pointer in Transfer Frame Primary Header)
Transfer
Frame Version Number
« 00 »
2 bits
Bypass
Flag
Ctrl
Cmd
Flag
1 bits
1 bits
10 bits
Virtual
Channel Id
Spacecraft Id
6 bits
Rsvd.
Spare
2 bits
Frame
length
Frame
Sequence
Number
10 bits
8 bits
Notes: This slide presents the structure of the TC transfer frame.
Important characteristics of the TC transfer frame:
Is of variable length
Contains a segment (a TC packet can be split into mutliple segments)
Has three levels of “addressing”: Spacecraft ID, Virtual Channel ID, MAP Id

## Slide 41: TC Transfer frame & Authentication
Transfer Frame
Variable (up to 1024 bytes)
Transfer Frame Trailer
16 bits
Frame
Error Control Field
Transfer Frame Data Field
Variable (up to 1019 bytes)
Transfer Frame Primary Header
5 bytes
Space Packet
Space Packet Data Field
Space Packet Primary Header
Segment Header
Sequence
Flags
Multiplexer
Access
Point
Id
2 bits
6 bits
Segment
Data
Field
Variable (up to 1018 bytes)
1 byte
Variable (up to 65542 bytes)
Authentication is mentioned in ECSS-E-ST-50-04C (TC synchronisation & coding), referring to PSS-04-107 (old ESA packet telecommand standard)
Process located in the segmentation sublayer
Data is not encrypted, a signature is appended
The authenticated data structure is the TC segment including:
Its header
Its data field
Its Logical Authentication Channel, which includes a counter
Transfer
Frame Version Number
« 00 »
2 bits
Bypass
Flag
Ctrl
Cmd
Flag
1 bits
1 bits
10 bits
Virtual
Channel Id
Spacecraft Id
6 bits
Rsvd.
Spare
2 bits
Frame
length
Frame
Sequence
Number
10 bits
8 bits
Segment Trailer
LAC (ID+count)
Signature
4 bytes
n bytes
Notes: This slide presents the authentication process as defined by ESA PSS-04-107, through ECSS-E-ST-50-04C. This is not the only way to perform TC authentication, but this is the one currently supported by the ECSS standards.
The choice of the TC Segment as the authenticated data structure is linked to that of the Sequence-Controlled Service of COP-I. These two choices are conveniently compatible with the synchronisation requirements of the authentication count number. Thus the signature is placed at the end of the TC Segment structure, which effectively means placing an Authentication Sublayer between the Transfer Layer and the Segmentation Layer.
For operational flexibility, three counters are selectable. These three counters effectively provide three “Logical Authentication Channels” (LACs). The first two LAC counters (“Principal LAC” and “Auxiliary LAC”) make it possible to multiplex two independent streams of authenticated data on two independent sets of MAP connections without discontinuities (one LAC for each set of MAPS). The third LAC counter is foreseen for recovery (“Recovery LAC”): its contents are nonvolatile.

## Slide 42: TC Transmission unit
TC Communication Link Transmission Unit
Start
Sequence
11101011
10010000
16 bits
Encoded Data
Tail
Sequence
11000101
11000101
…
11000101
01111001
1 BCH Codeblock Length
Transfer Frame
Transfer Frame Primary Header
Transfer Frame Trailer
Transfer Frame Data Field
Variable (up to 19 BCh Codeblocks)
BCH
Codeblock
BCH
Codeblock
BCH
Codeblock
…
BCH Codeblock
Information
(possibly randomized)
Parity Check
56 bits
7 bits
Fill
« 0 »
1 bits
8 bytes
BCH Codeblock
Information
(possibly randomized)
Parity Check
56 bits
7 bits
Fill
« 0 »
1 bits
8 bytes
Bose, Ray-Chaudhuri, Hocquenghem
Preamble
« 10101 .. »
Idle
« 1010101 … »
Notes: Once the frame is assembled, it is then encoded into fixed-size BCH code blocks (possibly randomized) and encapsulated into a start and tail sequence to form the CLTU (Communication Link Transmission Unit), which is the signal exchanged on the physical link.

## Slide 43: TM Space packet
Space Packet
Variable (7 to 65542 bytes)
Packet Primary Header
6 bytes
Packet Identification
2 bytes
Packet
Sequence
Control
2 bytes
Packet Version Number
3 bits
Packet Type
1 bits
Secondary Header
Flag
1 bits
Application Process Id
11 bits
Sequence Flags
2 bits
Packet Sequence
Count
14 bits
Packet Data Length
2 bytes
16 bits
Packet Data Field
Variable (1 to 65536 bytes)
Packet Secondary
Header
(Data
Field
Header)
variable
User
Data
Field
variable
Packet
Error
Control
16 bits
Time Code Field
Var.
Ancillary Data
Field
Var.
Application
Data
Var.
Spare
Var.
Notes: In its ‘space packet’ definition, the TM space packet is a verbatim copy of the TC space packet.
The primary header contains a packet identification, essentially made of the application ID and several flags; a packet sequence control, with a sequence count used to identify the packet and sequence flags which are not used by the PUS standard (always “stand alone”).
In terms of secondary header, the space packet protocol only requires a time code field and an ancillary data field. These are populated according to the PUS definitions. The same goes for the end for the packet containing the application data and the CRC.

## Slide 44: TM Transfer frame
Transfer Frame
TM Tranfser Frame length depends on the subsequent coding options (max 2048 bytes)
Transfer Frame Primary Header
6 bytes
8bits
8 bits
Master
Channel Frame
Count
Virtual
Channel Frame
Count
Transfer Frame Data Field
variable
Global Virtual Channel Id
2 bits
10 bits
Virtual
Channel Id
Master Channel Id
Transfer
Frame Version Number
Spacecraft Id
3 bits
6 bytes
Transfer Frame Trailer
16 bits
Frame
Error Control Field
(opt.)
Operational Control Field
(opt.)
32 bits
1 bits
Op
Ctrl
Field
Flag
1 bits
Transfer Frame Data Field Status
Synch
Flag
Pkt
Order
Flag
Seg
Len
Id
1 bits
2 bits
First
Header
Pointer
11 bits
TM Transfer Frames are Fixed Length
(TC Transfer Frame are Variable Length)
TM Multiplexing is based on standard First Header Pointer in Transfer Frame Primary Header
(TC Multiplexing is based on additional Segment Header
In Transfer Frame Data Field)
Space Packet
Space Packet Data Field
Space Packet Primary Header
Variable (up to 65542 bytes)
2 bits
Up to 64 bytes
Sec Hdr Id
Sec
Hdr
Ver
Nbr
Sec
Hdr
Length
6 bits
Xfer
Frm
Sec
Hdr
Data
Field
Transfer Frame Sec Hdr
(opt.)
Xfer
Frm
Sec
Hdr
Flag
1 bits
Notes: This slide presents the structure of the TM transfer frame.
Important characteristics of the TM transfer frame:
Is of fixed length
Contains a continuous flux of TM packets, the first of which is pointed by the first header pointer
Has two levels of “addressing”: Master channel ID and Virtual Channel ID.

## Slide 45
2:
The Packet Utilisation Standard

## Slide 46
The PUS:
Background and History

## Slide 47: Background and history
Origin and evolution
Issue A
Issue C
Operational experience
Operational experience
Issues 1 to 5
Compatibility
1994
2003
2016

## Slide 48: Background and history
Issue A
Issue C
Operational experience
Operational experience
Issues 1 to 5
Compatibility
2003
2016
First Implementations
Generic OIRD
Issue C
Rev 1
2024 ?

## Slide 49: COES PUS - 1994
1994  Standardized Service Types |  |  | 
ST[01] | telecommand verification | ST[13] | large data transfer
ST[02] | device command distribution | ST[14] | packet transmission control
ST[03] | HK and diagnostic data reporting | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[16] | on-board traffic management
ST[05] | event reporting | ST[17] | test
ST[06] | memory management |  | 
ST[07] | task management |  | 
ST[08] | function management |  | 
ST[09] | time management |  | 
ST[10] | time reporting |  | 
ST[11] | on-board scheduling |  | 
ST[12] | on-board monitoring |  | 

## Slide 50: ECSS PUS-A – 2003
2003  Standardized Service Types |  |  | 
ST[01] | telecommand verification | ST[13] | large data transfer
ST[02] | device command distribution | ST[14] | packet forwarding control
ST[03] | HK and diagnostic data reporting | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[16] | reserved
ST[05] | event reporting | ST[17] | test
ST[06] | memory management | ST[18] | on-board operations procedure
ST[07] | reserved | ST[19] | event-action
ST[08] | function management |  | 
ST[09] | time management |  | 
ST[10] | reserved |  | 
ST[11] | on-board operations scheduling |  | 
ST[12] | on-board monitoring |  | 
removed part
new part
modified part
Notes: Point to the fact that if e.g. a service type is depreciated in newer version, it does not mean that existing software need to be updated….

## Slide 51: ECSS PUS-C – 2016
2016  Standardized Service Types |  |  | 
ST[01] | request verification | ST[13] | large packet transfer
ST[02] | device access | ST[14] | real-time forwarding control
ST[03] | housekeeping | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[16] | reserved
ST[05] | event reporting | ST[17] | test
ST[06] | memory management | ST[18] | on-board control procedure
ST[07] | reserved | ST[19] | event-action
ST[08] | function management | ST[20] | parameter management
ST[09] | time management | ST[21] | request sequencing
ST[10] | reserved | ST[22] | position-based scheduling
ST[11] | time-based scheduling | ST[23] | file management
ST[12] | on-board monitoring |  | 
removed part
new part
modified part
Notes: ST[08] is kept but with statement that it is mainly kept for backward compatibility but should not be used anymore...

## Slide 52: ECSS PUS-C revision 1 – 2024 ?
2016  Standardized Service Types |  |  | 
ST[01] | request verification | ST[13] | large packet transfer
ST[02] | device access | ST[14] | real-time forwarding control
ST[03] | housekeeping | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[16] | reserved
ST[05] | event reporting | ST[17] | test
ST[06] | memory management | ST[18] | on-board control procedure
ST[07] | reserved | ST[19] | event-action
ST[08] | function management | ST[20] | parameter management
ST[09] | time management | ST[21] | request sequencing
ST[10] | reserved | ST[22] | position-based scheduling
ST[11] | time-based scheduling | ST[23] | file management
ST[12] | on-board monitoring |  | 
removed part
new part
modified part
REVISION 1 :
Correction and consolidation of foundation model and existing services
Creation of additional services for:
  File Based Operations
  Data sources management
  Critical event Log
  Parameter extraction
Notes: ST[08] is kept but with statement that it is mainly kept for backward compatibility but should not be used anymore...

## Slide 53: ECSS-E-ST-70-41C WG – Main Purpose
The Main Purpose of the PUS-A to PUS-C upgrade was:
  removing the PUS-A deficiencies and injecting lessons learned
  improving the standard to meet the need for future missions
  acknowledging the existence of new ECSS and CCSDS standards and ensuring consistency
  implementing the ECSS drafting rules that apply to any ECSS Standards [e.g. naming each requirement to facilitate tailoring, traceability]
  maintaining backward compatibility when possible
The C version of the PUS has been developed by the major stakeholders including Space Agencies and Industry, with representatives of both the Space Segments and the Ground Segments
Notes: The PUS-C working group started in 2011, involving 17 persons from Agencies (CNES, DLR, Eumetsat, ESA) and Industry (Airbus, Spacebel, Thales)
190 change requests to process.
One of the most used standard, and in its C version, the largest in number of requirements.
Complete reverse engineering has been required, with many decisional conflicts between keeping backward compatibility with existing tools and removal of inconsistencies

## Slide 54: PUS-C – A new document structure
Scope
Normative references
Terms, definitions and abbreviated terms
Context and background
PUS foundation model
Service type system specification
Space/ground interface requirements
  Space packet overview
  Packet data field for TM packet
  Packet data field for TC packet
  Packet Field Code (PTC/PFC)
Service type interface specification
Context and background
Annexes
informative IEEE and MILBUS real formats
informative CRC and ISO checksum
informative Request type & report type summary
informative System and interface specification index
ECSS-E-ST-70-41C | 656 pages
Generic Foundation Model | 121 requirements
system specification | 2216 requirements
interface specification | 850 requirements
Notes: This slide presents the contents of the PUS. While presenting it, it is also interesting to present what it does not contain. In particular, it should be highlighted that the PUS covers all Space Segment requirements but no Ground Segment requirements. In extenso, tailoring is an issue of Operations and Space Segment, but not of Ground Segment.

## Slide 55
The PUS Foundation Model...

## Slide 56: The PUS Foundation Model
Service Type
Deployment
Mission-specific Service Types
Standard Service Types
PUS
Foundation
Model
The PUS Foundation Model defines the model (including vocabulary) that:
has been used to produce the “standard service types”;
shall be used to produce the “mission-specific service types”, i.e.:
  adding new service types, subservice types, message types, …
  adding capabilities to the ”standard service types”;
shall be used to produce the “mission services”, i.e.:
  creating the required services by:
    “realising the service types”, and
    inheriting all mandatory subservices and minimum capabilities;
  selecting, for each service, the additional capabilities, the optional subservices, etc;
  creating the service specific definitions.

## Slide 57: The Service Type System Requirements
Service Type
Deployment
Mission-specific Service Types
Standard Service Types
PUS
Foundation
Model
The ST System Requirements
addresses the “Semantic” of each service type including:
the service type concept and related architecture
the message type concept and related architecture
the overall service type topology (focusing on message exchange between service users and service providers)

## Slide 58: The Service Type Interface Requirements
Service Type
Deployment
Mission-specific Service Types
Standard Service Types
PUS
Foundation
Model
The ST System Requirements
addresses the “Semantic” of each service type including:
the service type concept and related architecture
the message type concept and related architecture
the overall service type topology (focusing on message exchange between service users and service providers)
The service type interface requirements
specifies the Ground/Space Link message exchange protocol i.e.:
how requests are transported within CCSDS SPP & PUS telecommand packets;
how reports are transported within CCSDS SPP & PUS telemetry packets.

## Slide 59: PUS Foundation – some concepts
APID
APID
ground application process
service
Space Segment
Ground Segment
report
TM packet
TC packet
request
subservice
subservice provider
subservice user
subservice
subservice provider
subservice user
sending
entity
receiving
entity
subservice
entities

## Slide 60: PUS Foundation – Instruction ≈ Request
t3  executing the schedule, the time-based schedule service generates the “on/off device command” instruction (request)
APID B
S2
subservice provider
APID A
S11
subservice provider
ground application process
S11
subservice user
S2
subservice user
time-based
scheduling
subservice
device
access
subservice
out of scope
out of scope
instruction
t1  instructs the time-based scheduling service to insert into the time-based schedule, an “on/off device command” instruction (request)
request
TC Packet
t2  the “on/off device command” instruction is inserted within a “insert into time-based schedule” request that is transported within a [11,4] TC packet
instruction
time-based
scheduling
service
device
access
service
Space Segment
Ground Segment
Notes: Unsure the contents of this slide are actually correct…

## Slide 61: The PUS request...
an instruction
instructionID(requestID, relative name)
instructionType defined by that messageType
0 or more{request argument}
0 or more{instruction argument}
others such as execution verification reporting needs
a request
  requestID (source, destination, relative name)
  messageType defined by a subserviceType of a serviceType
  0 or more{request argument}
  1 or more{instruction} of instructionType defined by that messageType
  others such as acceptance verification reporting needs,…
request
destination
source
the WHAT
Notes: a request has:
0 or more request argument
1 or more instructions
an instruction has
the request arguments
0 or more instruction argument

## Slide 62: ... transported in a CCSDS/PUS TC packet
request
destination
source
TC packet PUS version number | acknowledgement flags | message type ID |  | source ID | spare
 |  | service type ID | message subtype ID |  | 
enumerated (4 bits) | enumerated (4 bits) | enumerated (8 bits) | enumerated (8 bits) | enumerated (16 bits) | fixed-size bit-string
 |  |  |  |  | optional
packet primary header |  |  |  |  |  |  | packet data field | 
packet version number | packet ID |  |  | packet sequence control |  | packet data length | packet secondary header | user data field
 | packet type | secondary header flag | application process ID | sequence flags | packet sequence count or packet name |  |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | variable | variable
2 octets |  |  |  | 2 octets |  | 2 octets | 1 to 65536 octets | 
= 2
the HOW
TC packet
Notes: Service: Set of on-board functions offered to a service user that can be controlled and monitored through a well-defined set of service requests and reports
Optionality and tailoring: Multiple levels of optionality exists in the PUS standards, depending on selected functionality:
At header level (secondary headers only – optionality reduced in issue C)
At service level
At subservice level
At request/report level
« Change log » slides are spread across this presentation to highlight the changes brought by the issue C of the PUS standard with respect to issue A. A dedicated « transition from PUS-A to PUS-C » slide show can be created for audiences which are mainly interested in this topic – this would be the case for engineers or operators who are very familiar with issue A and are not interested in the detailed presentation of most of the standard services.
The evolution of secondary headers is limited and does not break backward compatibility. The main change is a suppression of the variability of such headers. Indeed, they are often interpreted by hardware systems, and having a fixed header is seen as a plus in this context.

## Slide 63: The PUS report...
report
source
destination
a notification
notificationID(reportID, relative name)
notificationType defined by that messageType
0 or more{report argument}
0 or more{notification argument}
others
a report
  reportID (source, destination, sequence count)
  messageType defined by a subserviceType of a serviceType
  0 or more{report argument}
  1 or more{notification} of notificationType defined by that messageType
  others
the WHAT
Notes: Service: Set of on-board functions offered to a service user that can be controlled and monitored through a well-defined set of service requests and reports
Optionality and tailoring: Multiple levels of optionality exists in the PUS standards, depending on selected functionality:
At header level (secondary headers only – optionality reduced in issue C)
At service level
At subservice level
At request/report level
« Change log » slides are spread across this presentation to highlight the changes brought by the issue C of the PUS standard with respect to issue A. A dedicated « transition from PUS-A to PUS-C » slide show can be created for audiences which are mainly interested in this topic – this would be the case for engineers or operators who are very familiar with issue A and are not interested in the detailed presentation of most of the standard services.
The evolution of secondary headers is limited and does not break backward compatibility. The main change is a suppression of the variability of such headers. Indeed, they are often interpreted by hardware systems, and having a fixed header is seen as a plus in this context.

## Slide 64: ... transported in a CCSDS/PUS TM packet
packet primary header |  |  |  |  |  |  | packet data field | 
packet version number | packet ID |  |  | packet sequence control |  | packet data length | packet secondary header | user data field
 | packet type | secondary header flag | application process ID | sequence flags | packet sequence count or packet name |  |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | variable | variable
2 octets |  |  |  | 2 octets |  | 2 octets | 1 to 65536 octets | 
TM packet PUS version number | spacecraft time reference status | message type ID |  | message type counter | destination ID | time | spare
 |  | service type ID | message subtype ID |  |  |  | 
enumerated (4 bits) | enumerated (4 bits) | enumerated (8 bits) | enumerated (8 bits) | unsigned integer (16 bits) | enumerated (16 bits) | absolute time | fixed-size bit-string
 |  |  |  |  |  |  | optional
= 2
report
source
destination
TM packet
the HOW
Notes: Service: Set of on-board functions offered to a service user that can be controlled and monitored through a well-defined set of service requests and reports
Optionality and tailoring: Multiple levels of optionality exists in the PUS standards, depending on selected functionality:
At header level (secondary headers only – optionality reduced in issue C)
At service level
At subservice level
At request/report level
« Change log » slides are spread across this presentation to highlight the changes brought by the issue C of the PUS standard with respect to issue A. A dedicated « transition from PUS-A to PUS-C » slide show can be created for audiences which are mainly interested in this topic – this would be the case for engineers or operators who are very familiar with issue A and are not interested in the detailed presentation of most of the standard services.
The evolution of secondary headers is limited and does not break backward compatibility. The main change is a suppression of the variability of such headers. Indeed, they are often interpreted by hardware systems, and having a fixed header is seen as a plus in this context.

## Slide 65: Verifying TM packets continuity
Using the CCSDS header sequence count & the PUS secondary header message type counter to identify missing TM packets due to e.g. signal loss
SRC | DST | Service type ID | Message Subtype ID | Sequence count | Message type count | event
APID_2 | Ground | 3 | 25 | 1 | 1 | real-time download
APID_2 | Ground | 5 | 3 | 2 | 1 | real-time download
APID_2 | Ground | 3 | 25 | 3 | 2 | real-time download
APID_2 | Ground | (5) | (3) | (4) | (2) | real-time lost
APID_2 | Ground | 3 | 25 | 5 | 3 | real-time download
APID_2 | Ground | 5 | 3 | 6 | 3 | real-time download
Notes: The detection of a lost packet can only be seen

## Slide 66: Verifying TM packets continuity
Using the CCSDS header sequence count & the PUS secondary header message type counter to identify missing TM packets due to e.g. real-time forwarding selection
SRC | DST | Service type ID | Message Subtype ID | Sequence count | Message type count | event
APID_2 | Ground | 3 | 25 | 1 | 1 | real-time download
APID_2 | Ground | 5 | 3 | 2 | 1 | real-time download
APID_2 | Ground | 3 | 25 | 3 | 2 | real-time download
APID_2 | Ground | (5) | (3) | (4) | (2) | real-time lost
APID_2 | Ground | 3 | 25 | 5 | 3 | real-time download
APID_2 | Ground | 5 | 3 | 6 | 3 | real-time download
request to stop forwarding the TM[5,3] of APID_2 received on-board |  |  |  |  |  | 
APID_2 | Ground | (5) | (3) | (7) | (4) | not forwarded in real-time
APID_2 | Ground | 3 | 25 | 8 | 4 | real-time download

## Slide 67: Verifying TM continuity – PUS-A Work around
packet primary header |  |  |  |  |  |  | packet data field | 
packet version number | packet ID |  |  | packet sequence control |  | packet data length | packet secondary header | user data field
 | packet type | secondary header flag | application process ID | sequence flags | packet sequence count or packet name |  |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | variable | variable
2 octets |  |  |  | 2 octets |  | 2 octets | 1 to 65536 octets | 
report
source
destination
TM packet
Application Process ID:
Uniquely identifies the source
Drives sequence count (1 count for each APID)
Sometimes split into Process ID (PRID) and Packet Category (PCAT)
  This implies having multiple APIDs and associated sequence counts for the same Application Process identified by its PRID
PUS-C
FOUNDATION
VIOLATION
Notes: Many missions use the concept of PRID (7 bits) and PCAT (4 bits) to further split the APID. In that case, the source is identified by its Process ID; each process can use 16 packet categories to further refine the packet description. This is useful to ensure packet sequence count continuity by grouping together packets that are expected to be transmitted together. For example, packet categories 1 & 2 would go to real-time, while packet categories 3, 4 and 5 would only be stored into mass memory.
A packet category can contain multiple message types or some message types (e.g. for Housekeeping where a third ID is used to further identify) can be spread over multiple categories!!!
Another approach (not playing with the APID) was discussed in the ECSS PUS-C working group that consisted in adding another field in the PUS Secondary Header called Group ID which would have carried the same information as the PCAT but for which the associations of which message types belong to which category/group would have been configurable using dedicated message subtypes of services 14 and 15. Such approach did not find consensus in the WG.

## Slide 68: Verifying TM continuity – PUS-A Work around
packet primary header |  |  |  |  |  |  | packet data field | 
packet version number | packet ID |  |  | packet sequence control |  | packet data length | packet secondary header | user data field
 | packet type | secondary header flag | application process ID | sequence flags | packet sequence count or packet name |  |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | variable | variable
2 octets |  |  |  | 2 octets |  | 2 octets | 1 to 65536 octets | 
report
source
destination
TM packet
Sometimes split into Process ID (PRID) and Packet Category (PCAT)
Some APIDs become telemetry sources only
Several services reference APIDs in their requests:
  Time & position based scheduling
  Real time forwarding, on-board storage
  Event action
Violates the PUS foundation: each subservice provider is hosted by exactly one application process.
PUS-C
FOUNDATION
VIOLATION
Notes: Many missions use the concept of PRID (7 bits) and PCAT (4 bits) to further split the APID. In that case, the source is identified by its Process ID; each process can use 16 packet categories to further refine the packet description. This is useful to ensure packet sequence count continuity by grouping together packets that are expected to be transmitted together. For example, packet categories 1 & 2 would go to real-time, while packet categories 3, 4 and 5 would only be stored into mass memory.
A packet category can contain multiple message types or some message types (e.g. for Housekeeping where a third ID is used to further identify) can be spread over multiple categories!!!
Another approach (not playing with the APID) was discussed in the ECSS PUS-C working group that consisted in adding another field in the PUS Secondary Header called Group ID which would have carried the same information as the PCAT but for which the associations of which message types belong to which category/group would have been configurable using dedicated message subtypes of services 14 and 15. Such approach did not find consensus in the WG.

## Slide 69
The PUS standardized service types...

## Slide 70: PUS-C - standardized service types
Standardized Service Types |  |  | 
ST[01] | request verification | ST[13] | large packet transfer
ST[02] | device access | ST[14] | real-time forwarding control
ST[03] | housekeeping | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[16] | reserved
ST[05] | event reporting | ST[17] | test
ST[06] | memory management | ST[18] | on-board control procedure
ST[07] | reserved | ST[19] | event-action
ST[08] | function management | ST[20] | parameter management
ST[09] | time management | ST[21] | request sequencing
ST[10] | reserved | ST[22] | position-based scheduling
ST[11] | time-based scheduling | ST[23] | file management
ST[12] | on-board monitoring |  | 

## Slide 71: Operations – Use cases
What capabilities do all missions share ?
verifying
high level commanding
managing telemetry and data
on-board parameters
FDIR and asynchronous events
hardware and software functions
...
Notes: For this training, the decision is taken to present the service types according to an operational view made of groups of services.

## Slide 72
PUS for 
Verifying

## Slide 73: SET – verifying
Verifying
The standard service types gathered in this set provide means to verify the uplink of requests.
This set also closes the command loop by including the capability to test the connectivity to command destination, as well as to verify their execution.
ST[01] | request verification | 
ST[17] | test | 

## Slide 74: ST[17] - Test
ST[17] scope
The test service provides the capability to perform a set of end-to-end test functions which can be exercised under ground control (e.g. an are-you-alive function).
Verifying |  | 
ST[01] | request verification | 
ST[17] | test | √

## Slide 75: ST[17] – Standardized subservice type
Test subservice
The test subservice provides the capability to check that the routes (uplink and downlink) are operational and that the receiving application performs a minimum set of functions (including TC processing)
It also provides the capability to verify the connectivity between two application processes. The criteria for determining that the connection test is successful is mission dependent (and will vary between application processes)
Test service

## Slide 76: ST[17] – Important concepts
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
TC[17,1]
TM[17,2]
TC[17,1]
TM[17,2]
TC[17,1] – Perform an are-you-alive connection test
Notes: These two slides depict the difference between a (17,1) connection test and a (17,3) on-board connection test.
In the (17,1) case, the message is transferred by the on-board computer to its destination transparently, and the (17,2) reply is produced by the destination

## Slide 77: ST[17] – Important concepts
MIL-STD 1553 P/L
T
T
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
TC[17,3]
TM[17,4]
TC[17,3]
TM [17,4]
TC[17,3] – Perform an on-board connection test
Message not standardized
MMFU
X-Band link
ESRIN
uni-directional
Notes: These two slides depict the difference between a (17,1) connection test and a (17,3) on-board connection test.
In the (17,3) case, the message is also transferred by the on-board computer to its destination. The latter then tries to reach the selected other application (in this case, the MMU). If this test is successful, the payload generates the (17,4), which is forwarded back to ground by the on-board computer. The way the process inside the payload communicates with the MMU is out of the scope of the PUS standard, which only defines the space to ground interface.
Note that in our example, MMFU has an APID and is a PUS terminal, but (17,3) can also be used to perform an on-board connection test to something that is not a PUS terminal (as long as it is identified by an APID)

## Slide 78: ST[17] – Message types
system | interface | message type |  |  |  | 
6.17.3 | 8.17.2.1 | TC[17,1] |  |  | perform an are-you-alive connection test | minimum
6.17.3 | 8.17.2.2 |  | TM[17,2] |  | are-you-alive connection test report | TC[17,1] response
6.17.4.2 | 8.17.2.3 | TC[17,3] |  |  | perform an on-board connection test | minimum
6.17.4.2 | 8.17.2.4 |  |  | TM[17,4] | on-board connection test report | TC[17,3] response
Test subservice

## Slide 79: ST[17] – Tailoring & deployment
Each on-board application process shall host at most one test subservice provider
It is generally accepted that supporting this subservice is mandatory for all applications.

## Slide 80: ST[17] – Foundation model
2 requests, 2 reports, but one subservice type ?
With PUS-A: Common confusion between ‘subservice’ and ‘service subtype’
In PUC-C, they are now called ‘subservice type’ and ‘message type’
Subservice type is a functional specification concept.
Message type is an interface specification concept.
system | interface | message type |  |  |  | 
6.17.3 | 8.17.2.1 | TC[17,1] |  |  | perform an are-you-alive connection test | minimum
6.17.3 | 8.17.2.2 |  | TM[17,2] |  | are-you-alive connection test report | TC[17,1] response
6.17.4.2 | 8.17.2.3 | TC[17,3] |  |  | perform an on-board connection test | minimum
6.17.4.2 | 8.17.2.4 |  |  | TM[17,4] | on-board connection test report | TC[17,3] response
Test subservice
Notes: The purpose of this slide (and of the ‘tips and tricks’ slides to follow) is to break some of the most common misconceptions or misunderstandings observed when dealing with customers not so familiar with the PUS. The goal is to build on PUS implementation experience, but also to break the flow of an endless list of services and functionalities. The opportunity can also be taken to ‘activate’ the audience, for example by stopping on the first bullet and asking if there’s anything wrong with that statement.
Note that the concepts highlighted in this slide are previously introduced in the presentation part related to the PUS foundation model.

## Slide 81: ST[17] – PUS-A to PUS-C evolution
Added features
TC[17,3] and TM[17,4] Perform on-board connection test
Deleted features
None
Updated features
None
Notes: Service 17 only saw the introduction of the on-board connection test.

## Slide 82: ST[01] – Request verification
Verifying |  | 
ST[01] | request verification | √
ST[17] | test | 
ST[01] scope
The request verification service concerns:
each application process that is involved in the routing of requests to the application processes responsible for their execution, and
for each request, the application process responsible for its execution, i.e. the application process that hosts the service that executes the request.
The request verification service provides the capability for:
checking that a request received on-board has not been corrupted during the ground to space uplink;
checking the availability of the application process that is the destination for that request;
checking the availability of the service that executes that request;
reporting the success or failure of these checks;
generating the execution request verification reports on behalf of the service that executes that request.

## Slide 83: ST[01] – Verification for all requests
ST[01] – Request verification
a service type that provides the capability to report the routing, acceptance and execution of each request independently of its type
ST[02] | device access | ST[14] | real-time forwarding control
ST[03] | housekeeping | ST[15] | on-board storage and retrieval
ST[04] | parameter statistics reporting | ST[17] | test
ST[05] | event reporting | ST[18] | on-board control procedure
ST[06] | memory management | ST[19] | event-action
ST[08] | function management | ST[20] | parameter management
ST[09] | time management | ST[21] | request sequencing
ST[11] | time-based scheduling | ST[22] | position-based scheduling
ST[12] | on-board monitoring | ST[23] | file management
ST[13] | large packet transfer | + any mission/project/product/... specifics | 

## Slide 84: ST[01] – Standardized subservice types
routing and reporting
The routing and reporting subservice type provides the capability to check that the conditions required to pursue the routing of a request are fulfilled. This includes checking the integrity of the request during its routing to the application process that is responsible for executing it.
acceptance reporting
The acceptance and reporting subservice type provides the capability to check the acceptance of a request prior to its distribution to the service addressed by that request. This subservice type provides the means to report the successful or failed acceptance of each received request.
execution reporting
Each subservice of type "execution reporting" is hosted by an application process that hosts subservice providers responsible for executing requests. It receives the request execution notifications issued by the subservice providers and provides the means to generate the corresponding execution verification reports on behalf of those subservice providers.
Each request execution notification indicates a request execution stage, which can be a start of execution, a progress of execution or a completion of execution. The notification also indicates whether that execution stage succeeded or failed and, in case of failure, the reason for such failure.
Request verification service

## Slide 85: ST[01] – Overview
Processes routing/acceptance/execution notifications, successful or failed, and generates the corresponding reports
Closes the loop at ground level
Provides detailed knowledge of the execution status of a request and failure conditions

## Slide 86: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TM[1,10]
TC[8,1]
Stage: Routing
Why TM[1,10] ?
 Latest addition to this service !
Why no TM[1,9] successful routing ?
 Potentially numerous nodes
 No more selection bit available
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Routing stage: The request is sent to the OBC, and forwarded through the 1553 bus. The remote terminal is not responsible. A failed routing verification report is generated by the OBC. This is the only case where the responding entity is not the destination entity.

## Slide 87: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TC[8,1]
Stage: Acceptance
Existing service ?
TM[1,2]
TM[1,1]
TC Execution Profile
TC[200,1]
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Acceptance stage: The request has successfully been forwarded through the 1553 bus. The payload software checks that the provided mode parameter is correct. Failed acceptance verification report generated if the parameter is incorrect, successful acceptance verification report generated if the parameter is correct.

## Slide 88: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TC[200,1]
Stage: Start of Execution
Existing service ?
Current mode allows transition to new mode ?
TM[1,4]
TM[1,3]
TC Execution Profile
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Start of execution stage: The request has successfully been forwarded through the 1553 bus and accepted by the payload. The payload software checks that its current state allows for switching its camera on. Failed start of execution report generated if the camera is not ready, successful start of execution report generated if the camera is ready. Upon generation of successful start of execution, the request starts being executed.

## Slide 89: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TC[200,1]
Stage: Progress & Completion
Existing service ?
Current mode allows transition to new mode ?
Execution steps:
  Preheat
  Activate imaging subsystem
   error activating, abort execution
TC Execution Profile
TM[1,5] – step 1
TM[1,6] – step 2
TM[1,8]
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Progress stage: The request has successfully been forwarded through the 1553 bus, accepted and started by the payload. The payload software executes the different steps linked to the mode change: Preheat, Activate a subsystem, and load its configuration. In this example, the first and last steps succeed, while the secondfails. Two successful progress of execution verification reports are generated, and a failed progress of execution verification report.
Completion stage: Upon completion of the last step, a failed completion of execution report is generated by the payload, indicating that the mode change did not fully succeed. This slide also illustrates that a failed progress report does not necessarily stop the execution of the remaining steps of the execution profile.

## Slide 90: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TC[200,1]
Stage: Progress & Completion
Existing service ?
Current mode allows transition to new mode ?
Execution steps:
  Preheat
  Activate imaging subsystem
   error activating but continue
  Configure payload
TC Execution Profile
TM[1,5] – step 3
TM[1,5] – step 1
TM[1,6] – step 2
TM[1,8]
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Progress stage: The request has successfully been forwarded through the 1553 bus, accepted and started by the payload. The payload software executes the different steps linked to the mode change: Preheat, Activate a subsystem, and load its configuration. In this example, the first and last steps succeed, while the secondfails. Two successful progress of execution verification reports are generated, and a failed progress of execution verification report.
Completion stage: Upon completion of the last step, a failed completion of execution report is generated by the payload, indicating that the mode change did not fully succeed. This slide also illustrates that a failed progress report does not necessarily stop the execution of the remaining steps of the execution profile.

## Slide 91: ST[01] – Verification stages
ATLID
BBR
CPR
MSI
S-Band Transponder
S-Bandlink
ESOC
bi-directional
On-board computer
downlink
uplink
MIL-STD 1553 P/L
T
T
Example: “Change payload mode” request
TC[200,1]
Stage: Progress & Completion
Existing service ?
Current mode allows transition to new mode ?
Execution steps:
  Preheat
  Activate subsystem
  Configure payload
TC Execution Profile
TM[1,5] – step 3
TM[1,5] – step 1
TM[1,5] – step 2
TM[1,7]
Notes: The purpose of this group of slides is to illustrate the different levels of verification using a fictional « Change Payload mode » request.
Completion stage: If the third step is also successful, then a successful completion of execution verification report is generated.

## Slide 92: ST[01] – Who is responsible ?
Routing APID
Destination APID
ground application process
Space Segment
Ground Segment
TC packet
request
Routing & Reporting Subservice
subservice user
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
TC packet
request
request
notifications
Routes request to destination APID
Generates TM[1,10] failed routing report

## Slide 93: ST[01] – Who is responsible ?
Routing APID
Destination APID
ground application process
Space Segment
Ground Segment
TC packet
request
Routing & Reporting Subservice
subservice user
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
TC packet
request
request
notifications
Performs acceptance-level checks
If required, generates TM[1,1] successful acceptance reports
Generates TM[1,2] failed acceptance reports

## Slide 94: ST[01] – Who is responsible ?
Routing APID
Destination APID
ground application process
Space Segment
Ground Segment
TC packet
request
Routing & Reporting Subservice
subservice user
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
TC packet
request
request
notifications
Performs start of execution, progress of execution and completion of execution checks
Forwards the corresponding notifications to the execution reporting subservice

## Slide 95: ST[01] – Who is responsible ?
Routing APID
Destination APID
ground application process
Space Segment
Ground Segment
TC packet
request
Routing & Reporting Subservice
subservice user
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
TC packet
request
request
notifications
Receives the start of execution, progress of execution and completion of execution notifications
May aggregate multiple notifications in a single report
Generates corresponding TM[1,3] to TM[1,8] reports

## Slide 96: ST[01] – Message types
Routing and reporting subservice
system | interface | message type |  | 
6.1.3.3 | 8.1.2.9 | TM[1,10] | failed routing verification report | minimum
Acceptance and reporting subservice
system | interface | message type |  | 
6.1.4.2 | 8.1.2.1 | TM[1,1] | successful acceptance verification report | minimum
6.1.4.3 | 8.1.2.2 | TM[1,2] | failed acceptance verification report | minimum
Execution reporting subservice
system | interface | message type |  | 
6.1.5.1.1 | 8.1.2.3 | TM[1,3] | successful start of execution verification report | minimum
6.1.5.1.2 | 8.1.2.4 | TM[1,4] | failed start of execution verification report | minimum
6.1.5.2.1 | 8.1.2.5 | TM[1,5] | successful progress of execution verification report | minimum
6.1.5.2.2 | 8.1.2.6 | TM[1,6] | failed progress of execution verification report | minimum
6.1.5.3.1 | 8.1.2.7 | TM[1,7] | successful completion of execution verification report | minimum
6.1.5.3.2 | 8.1.2.8 | TM[1,8] | failed completion of execution verification report | minimum
Notes: Note that the decision to use progress reports in NOT a system decision (when tailoring), but a request type definition decision whether it makes sense or not to report progress for each particular request type.

## Slide 97: ST[01] – Tailoring & deployment
Tailoring of service 1:
Notifications will always be generated by the subservice providers – errors must be reported.
What can be configured is the way to report failed progress of execution notifications.
  With PUS-A, many missions only implement acceptance & completion
  LISA-PF REX: Routing-level information would have been useful!
All service 1 report types are now listed as minimum capability
 An acceptance and reporting subservice must be deployed on each application process that executes requests;
 An execution reporting subservice must be deployed on each application process that includes at least one subservice provider that generates execution-level notifications.
Notes: Tailoring options for service 1 are very limited in PUS-C. Only the way to report failed progress of execution notifications can be configured per application and per request (either through separate failed progress of execution verification reports, or gathered in a single failed completion of execution report).
In LPF, the question on how to report failed routing was answered by issuing acceptance failure reports, as it was the first available verification step. This posed a few practical issues considering acceptance failure reports could be generated by multiple sources on behalf of the responding application.
Any application that executes requests must provide service 1.

## Slide 98: ST[01] – Implementation guidelines
All services interact with service 1:
  Service 1 specifies how to report the notifications produced by other services;
  Each other subservice specifies, for each request type, its execution and verification profiles;
  The standard only addresses verifications that could be standardized. Nothing precludes from adding additional, mission specific verifications
Service 1 is not a completely applicative service – it steps in the transport layer
  Impacted by and refers to elements of the CCSDS header (TC ID)
On-board condition codes:
  Are unique per application process;
  Determine the structure of the associated auxiliary data
Destination of the service 1 reports is not always the source of the corresponding request

## Slide 99: ST[01] – Implementation guidelines
While specifying service 1, these considerations and trade-offs must be taken into account:
Balance between number of condition codes and auxiliary data for these condition codes
What is completion ?
Need of a « ground telecommand model » to determine which commands to expect:
  Issued by ground
  Issued by on-board scheduler
  Issued by event action
  Issued by request sequencer
Notes: Points to develop in this slide:
First bullet touches the deployment of the service in terms of condition codes. To be as detailed as possible, the natural tendency would be to have as many condition codes as possible, adopting a different one even for very similar failures. Practically, this means maintaining as many packet definitions as there are conditions codes, because the condition code determines the structure of the auxiliary parameters which are provided in the report. On the other hand, too generic condition codes means that in order to carry the complete information of the error report, the auxiliary parameter structure needs to be quite complex. The granularity of codes should be chosen so that no optionality exists in the auxiliary information.
The concept of completion, i.e. at which stage of the request execution the process can be considered as completed (and thus the completion of execution report can be produced) seems simple in natural language, but may not be so trivial in terms of implementation. Indeed, it is not always possible to follow-up the actual execution (for example, if a hardware process is triggered), and practically the completion report may sometimes be generated earlier. In that cases, operations will rely on other observables to assess the status of the request. These cases should be minimized to the maximum extent.
While the handling of service 1 reports by ground for real-time telecommands seems straightforward, one must consider that there are also on-board telecommand sources. In particular, some of these sources are considered « ground proxy », for which related service 1 reports are also forwarded to ground. This applies to telecommands released from an on-board scheduler, a request sequencer, or an event action service. For these commands, the ground station needs to know that they exist, so that it can correctly interpret service 1 report corresponding to the processing of the corresponding requests.

## Slide 100: ST[01] – Implementation guidelines
Request verification (ST[01]) vs. Event reporting (ST[05])
Service 1 is used to report on verification stages of a request
Service 5 is used to report on events of operational significance not explicitly provided by other services
It may happen that event reports are triggered because of the execution of a request
This however does not preclude the corresponding notifications (in particular, progress) to be generated and forwarded.
Notes: This slide has been added after a discussion during the dry run event, where it was argued that the progress reports ([1,5], [1,6]) could be replaced by event reports. While it is true that event reports may provide the same kind of visibility, especially when the reported progress information could also be triggered by another process than a request, using the progress reporting ensures that the reported information can be linked to its specific request.

## Slide 101: ST[01] – Implementation guidelines
Upcoming change in revision 1:
Many services provide requests allowing multiple instructions
PUS-C allowed partial executions for most (do as much as possible, report all errors), but this leads to several issues in the reporting
Revision 1 will simplify the behavior but reduce flexibility:
  All instructions are to be checked for start of execution failure conditions before execution
  Processing stops as soon as an error is encountered, and this error is reported.
Notes: Added

## Slide 102: ST[01] – Implementation guidelines
PUS-C
Revision 1
Example: TC [3,5] Enable Housekeeping – SIDs {5, 7, 9} – Assuming SID 7 does not exist
Acceptance checks
Request level Start of Execution Checks
  Instruction Level Start of Execution Checks
  Instruction Execution
  Instruction Post Execution Checks
Request level Post Execution Checks
TM [1,1]
TM [1,3]
TM [1,8]
TM [1,1]
TM [1,4]
Notes: Added to illustrate the change of logic within multiple instruction requests upon one single failure introduced in rev 1.

## Slide 103: ST[01] – PUS-A to PUS-C evolution
Added features
Routing and reporting subservice
  TM[1,10] failed routing verification report
Deleted features
None
Updated features
All service types now have a functional specification of their request verification profiles

## Slide 104
PUS for 
High level commanding

## Slide 105: SET – High level commanding
High level commanding
The standard service types gathered in this set all provide several ways of loading commands on board. In addition to simply executing commands in real time, the following capabilities are supported:
Loading commands for execution at a later time;
Loading commands for execution at a specific orbital position;
Loading sequences of commands with interleaved delays;
Loading complex procedures capable of releasing commands based on on-board states or decision trees.
ST[01] | request verification | 
ST[11] | time-based scheduling | 
ST[18] | on-board control procedure | 
ST[21] | request sequencing | 
ST[22] | position-based scheduling | 

## Slide 106: ST[11] – Time-based scheduling
ST[11] scope
The time-based scheduling service provides the capability to command on-board application processes using requests pre­loaded on-board the satellite and released at their due time. To achieve this, the service maintains an on-board command time-based schedule and ensures the timely execution of requests contained in the schedule.
High level commanding |  | 
ST[11] | time-based scheduling | √
ST[18] | on-board control procedure | 
ST[21] | request sequencing | 
ST[22] | position-based scheduling | 

## Slide 107: ST[11] – Standardized subservice type
Time-based scheduling
The time-based scheduling subservice type includes the capability to maintain an on-board time-based schedule of requests and to ensure the timely release of those requests.
The time-based scheduling subservice type provides the optional concept of sub-schedules.
  Each request is associated to a sub-schedule. Each sub-schedule reflects a coherent on-board operation. Once that operation is completed, the sub-schedule has no further reason to exist. Therefore, sub-schedules are automatically created when used and deleted when empty. The time-based scheduling subservice type includes the capability for enabling and disabling the execution of each sub-schedule.
  The time-based scheduling subservice type also provides the optional concept of groups.
  Each request in the time-based schedule is associated to a group. The time-based scheduling subservice type includes the capability for enabling and disabling the execution of grouped requests, independently of the application processes they are released to and of the sub-schedules they belong to. Groups are typically related to spacecraft entities (e.g. hardware or software). Groups can be created and deleted by request and can exist even if empty. They are used, for example, to group all requests associated to a specific instrument and disable their release when the conditions for their execution are not fulfilled, while other requests for the same application process are associated to a different group and enabled for release.
Time-based scheduling service
extension of the ground monitoring and control
Notes: The time-based scheduling provides an extension of the ground monitoring and control. As such, the application process that executes a request released by the time-based scheduling subservice directly sends the request verification reports, if any, to the source identified by the source identifier specified in the request. The release of a request by the subservice is not conditional on the successful or unsuccessful execution of earlier requests released by the subservice.

## Slide 108: ST[11] – Overview
Mission timelines containing up to thousands of requests (30000+ for missions in development – typically one week of operations)
Each scheduled activity contains a request and related metadata:
  Release date;
  Sub-schedule;
  Group.
1: SS1/G1
22/08/2014
14:00:12
2: SS1/G2
22/08/2014
14:00:20
900: SS3/G3
28/08/2014
00:34:52
4: SS1/G1
22/08/2014
14:05:00
3: SS2/G3
22/08/2014
14:03:53
Notes: The term "scheduled activity" is used in the time-based scheduling service type to refer to each entry of the time-based schedule. A scheduled activity consists of:
  scheduling data, e.g. the identifier of the sub-schedule, the identifier of the group, the release time;
  the request that is scheduled for later release.
Each scheduled activity is identified by the identifier of the request that is scheduled for later release.
Current generation of missions have the mission timeline size in thousands (4000 for Proba, 2400 for LPF, 4000 TBC for Euclid), tens of thousands is expected for next gen missions (e.g. Juice)

## Slide 109: ST[11] – Overview

## Slide 110: ST[11] – Important concepts
Sub-schedule:
  Optional concept;
  Set of commands part of a coherent on-board operation;
  Created on the fly, deleted when empty.
1: SS1/G1
22/08/2014
14:00:12
2: SS1/G2
22/08/2014
14:00:20
900: SS3/G3
28/08/2014
00:34:52
4: SS1/G1
22/08/2014
14:05:00
3: SS2/G3
22/08/2014
14:03:53
Notes: The time-based scheduling subservice type provides the optional concept of sub-schedules. If the time-based scheduling subservice supports sub-schedules, each request in the time-based schedule is associated to a sub-schedule. Each sub-schedule reflects a coherent on-board operation. Once that operation is completed, the sub-schedule has no further reason to exist. Therefore, sub-schedules are automatically created when used and deleted when empty. The time-based scheduling subservice type includes the capability for enabling and disabling the execution of each sub-schedule.

## Slide 111: ST[11] – Important concepts
Group:
  Optional concept;
  Set of commands related to the same spacecraft entity;
  Generalises role played by destination APID in PUS A;
  Not autonomously generated.
1: SS1/G1
22/08/2014
14:00:12
2: SS1/G2
22/08/2014
14:00:20
900: SS3/G3
28/08/2014
00:34:52
4: SS1/G1
22/08/2014
14:05:00
3: SS2/G3
22/08/2014
14:03:53
Notes: The time-based scheduling subservice type also provides the optional concept of groups. If the time-based scheduling subservice supports groups, each request in the time-based schedule is associated to a group. The time-based scheduling subservice type includes the capability for enabling and disabling the execution of grouped requests, independently of the application processes they are released to and of the sub-schedules they belong to. Groups are typically related to spacecraft entities (e.g. hardware or software). Groups can be created and deleted by request and can exist even if empty. They can be used, for example, to group all requests associated to a specific instrument and disable their release when the conditions for their execution are not fulfilled, while other requests for the same application process are associated to a different group and enabled for release.

## Slide 112: ST[11] – Important concepts
On-board scheduling is the nominal way of operating a spacecraft
Requests to insert, delete, report, timeshift
Requests to enable & disable command release
Identification by release time window or packet id list
Filtering by sub-schedule and/or group
1: SS1/G1
22/08/2014
14:00:12
2: SS1/G2
22/08/2014
14:00:20
900: SS3/G3
28/08/2014
00:34:52
4: SS1/G1
22/08/2014
14:05:00
3: SS2/G3
22/08/2014
14:03:53

## Slide 113: ST[11] – Message types, 1
system | interface | message type |  |  |  |  |  | 
6.11.4.3.2 | 8.11.2.1 | TC[11,1] |  |  |  |  | enable the time-based schedule execution function | minimum
6.11.4.3.3 | 8.11.2.2 |  | TC[11,2] |  |  |  | disable the time-based schedule execution function | minimum
6.11.4.4 | 8.11.2.3 | TC[11,3] |  |  |  |  | reset the time-based schedule | minimum
6.11.4.5 | 8.11.2.4 | TC[11,4] |  |  |  |  | insert activities into the time-based schedule | minimum
6.11.5.2.1 | 8.11.2.20 | TC[11,20] |  |  |  |  | enable time-based sub-schedules | by declaration
6.11.5.2.2 | 8.11.2.21 |  | TC[11,21] |  |  |  | disable time-based sub-schedules | implied by TC[11,20]
6.11.5.2.3 | 8.11.2.18 | TC[11,18] |  |  |  |  | report the status of each time-based sub-schedule | requires TC[11,20]
6.11.5.2.3 | 8.11.2.19 |  | TM[11,19] |  |  |  | time-based sub-schedule status report | TC[11,18] response
6.11.6.2.1 | 8.11.2.22 | TC[11,22] |  |  |  |  | create time-based scheduling groups | by declaration
6.11.6.2.2 | 8.11.2.23 |  |  | TC[11,23] |  |  | delete time-based scheduling groups | implied by TC[11,22]
6.11.6.3.1 | 8.11.2.24 |  |  | TC[11,24] |  |  | enable time-based scheduling groups | implied by TC[11,22]
6.11.6.3.2 | 8.11.2.25 |  |  |  | TC[11,25] |  | disable time-based scheduling groups | implied by TC[11,24]
6.11.6.3.3 | 8.11.2.26 |  |  | TC[11,26] |  |  | report the status of each time-based scheduling group | requires TC[11,22]
6.11.6.3.3 | 8.11.2.27 |  |  |  |  | TM[11,27] | time-based scheduling group status report | TC[11,26] response
6.11.8.1 | 8.11.2.15 | TC[11,15] |  |  |  |  | time-shift all scheduled activities | by declaration
Time-based scheduling subservice ...

## Slide 114: ST[11] – Message types, 2
6.11.8.2 | 8.11.2.17 | TC[11,17] |  |  | summary-report all time-based scheduled activities | by declaration
6.11.7.1 | 8.11.2.13 |  | TM[11,13] |  | time-based schedule summary report | TC[11,17] response
6.11.8.3 | 8.11.2.16 | TC[11,16] |  |  | detail-report all time-based scheduled activities | by declaration
6.11.7.2 | 8.11.2.10 |  | TM[11,10] |  | time-based schedule detail report | TC[11,10] response
6.11.9.2 | 8.11.2.5 | TC[11,5] |  |  | delete time-based scheduled activities identified by request identifier | by declaration
6.11.9.3 | 8.11.2.7 | TC[11,7] |  |  | time-shift scheduled activities identified by request identifier | by declaration
6.11.9.4 | 8.11.2.12 | TC[11,12] |  |  | Summary-report time-based scheduled activities identified by request identifier | by declaration
6.11.7.1 | 8.11.2.13 |  | TM[11,13] |  | time-based schedule summary report | TC[11,12] response
6.11.9.5 | 8.11.2.9 | TC[11,9] |  |  | detail-report time-based scheduled activities identified by request identifier | by declaration
6.11.7.2 | 8.11.2.10 |  | TM[11,10] |  | time-based schedule detail report | TC[11,9] response
6.11.10.3 | 8.11.2.6 | TC[11,6] |  |  | delete the time-based scheduled activities identified by a filter | by declaration
6.11.10.4 | 8.11.2.8 | TC[11,8] |  |  | time-shift the scheduled activities identified by a filter | by declaration
6.11.10.5 | 8.11.2.14 | TC[11,14] |  |  | summary-report the time-based scheduled activities identified by a filter | by declaration
6.11.7.1 | 8.11.2.13 |  | TM[11,13] |  | time-based schedule summary report | TC[11,14] response
6.11.10.6 | 8.11.2.11 | TC[11,11] |  |  | detail-report the time-based scheduled activities identified by a filter | by declaration
6.11.7.2 | 8.11.2.10 |  |  | TM[11,10] | time-based schedule detail report | TC[11,11] response
... time-based scheduling subservice

## Slide 115: ST[11] – Tailoring & deployment
A time-based scheduling service may contain multiple time-based scheduling sub-services, each one deployed on a different on-board application process
Service type 11 common implementations tend to centralise the management of the mission timeline by deploying it only on the central software application process, but nothing precludes from having multiple deployments.
  This could, for example, allow for smaller propagation times from timeline release to execution, which may be significant for payloads behind system buses.

## Slide 116: ST[11] – Implementation guidelines
The time-based schedule shall never contain requests scheduled in the past. Operationally, this requires introducing a margin when inserting into or time-shifting the schedule, under which commands are rejected.
The time-based scheduling service provides capabilities to enable or disable release of requests at service, group and sub-schedule levels. For a specific request to be released, all three levels must be enabled.
Sub-schedules and groups are operated differently:
  A sub-schedule is a high level activity. It exists because activities are inserted into it. It is autonomously created and deleted
  A group represents a spacecraft entity. They can be created and deleted by TC, and exist even if the time-based schedule does not currently contain any request related to that group.
Notes:           The time margin that the time-based scheduling subservice uses when inserting activities in the time-based schedule or time-shifting activities shall be declared when specifying that subservice.

## Slide 117: ST[11] – Implementation guidelines
There exist two ways of reporting the time-based schedule:
  The release time, sub-schedule ID & group ID are provided in all cases
  In detailed reports, the complete request is attached
  In summary report, only the request identifier (APID + SSC) is provided
Some of the operations above (time shifting, reporting) may require very long processing times given the size of timelines. Care must be taken so that the implementation of these long operations do not affect the nominal execution of the timeline.
Notes:           The time margin that the time-based scheduling subservice uses when inserting activities in the time-based schedule or time-shifting activities shall be declared when specifying that subservice.
          The bullet relative to long operations does not have corresponding requirements in the standard, and the question of whether it should be explicited in the standard was asked during the dry run. It was argued that it could be left to common sense for now.

## Slide 118: ST[11] – PUS-A to PUS-C evolution
By far the most complex service in PUS A
Relative timing
Interlocking
Complete PUS A capability never implemented
PUS-C simplifies service 11 – more complex scenarios should be implemented with OBCPs
1: SS1/G1
22/08/2014
14:00:12
2: SS1/G2
22/08/2014
14:00:20
900: SS3/G3
28/08/2014
00:34:52
4: SS1/G1
22/08/2014
14:05:00
3: SS2/G3
22/08/2014
14:03:53
7: SS2/G5
22/08/2014
Enable + 3’
Notes: This slide’s purpose is to show the complexity that was present in PUS A by illustrating the mechanisms of relative timing (in this example, from sub-schedule activation, but the previous version of the standard was foreseeing a lot of on-board events as usable for relative time-tagging) and interlocking (in the example, the arrows indicate conditional execution, with the double arrow from 2->3 and 2->4 to be presented as two possible outcomes depending on the execution status of TC2).

## Slide 119: ST[11] – PUS-A to PUS-C evolution
Added features
Management of new filtering capabilities
  Report, Enable, Disable Sub-schedules TC[11,18] to TC[11,21]
  Create, Delete, Enable, Disable, Report Groups TC[11,22] to TM[11,27]
Deleted features
Interlocks
Relative time-tagging
Updated features
Filtering is now based on group (new) and sub-schedule (unchanged) concepts
  All messages using filters now support the updated scheme
  TC[11,4], TC[11,6], TC[11,8], TM[11,10], TC[11,11],TM[11,13], TC[11,14]
  Enable / Disable are now separated between service level
  (updated TC[11,1], TC[11,2]) and with filter (see added features)
Notes: The sub-schedule concept exists since PUS A but has been augmented with a notion of automatic creation and deletion, see the previous slide dedicated to its definition.
The group concept is new, and replaces the role destination APID was taking in PUS A.
All requests related to filtering the contents of the command schedule have been updated to support these two concepts. STs 1 and 2, which were dedicated to enable / disable release of commands according to a filter, have however been split and moved into new subtypes (see next slide). STs 1 and 2 have been kept for the general enable/disable at service level.

## Slide 120: ST[11] - Foundation Model
Service 11 illustrates the instruction multiplicity and its relation with the presence of repeated fields (“N”) in the corresponding messages.
1) TC[11,5] – Delete time-based scheduled activities identified by request identifier
Each request to delete time-based scheduled activities identified by request identifier shall contain one or more instructions to delete a time-based scheduled activity identified by request identifier.
Each instruction to delete a time-based scheduled activity identified by request identifier shall contain:
  The identifier of the scheduled activity to delete
 | repeated N times |  | 
N | request ID |  | 
 | source ID | application process ID | sequence count
unsigned integer | enumerated | enumerated | unsigned integer
Notes: Service 11 is a good opportunity to teach by example the concepts of requests, instructions, and the notion of multiple instructions within a request. In particular, the translation from functional to interface level shall be illustrated, showing that repeated fields may exist at interface level even if the request does not contain multiple instructions.
The first example is TC[11,5] delete time-based scheduled activities identified by request identifier. This is the simplest case: All instruction-level information is gathered after the n field in the interface specification; the request is assembled by listing all instructions individually.

## Slide 121: ST[11] - Foundation Model
 |  | repeated N times |  | 
time offset | N | request ID |  | 
 |  | source ID | application process ID | sequence count
relative time | unsigned integer | enumerated | enumerated | unsigned integer
2) TC[11,7] – Time-shift scheduled activities identified by request identifier
Each request to time-shift scheduled activities identified by request identifier shall contain:
  A time offset, (…)
  One or more instructions to time-shift a scheduled activity identified by request identifier
Each instruction to time-shift a scheduled activity identified by request identifier shall contain:
  The identifier of the scheduled activity to time-shift
Notes: Service 11 is a good opportunity to teach by example the concepts of requests, instructions, and the notion of multiple instructions within a request. In particular, the translation from functional to interface level shall be illustrated, showing that repeated fields may exist at interface level even if the request does not contain multiple instructions.
The second example is TC[11,7] time shift scheduled activities identified by request identifier. In this case, the N still depicts instruction multiplicity, but some instruction-related information is promoted to the level of the request. The instruction cannot be interpreted ‘stand-alone’, it needs the time offset to be executed. However, since this time offset is the same for the complete request, it is promoted as a request argument.

## Slide 122: ST[11] - Foundation Model
 |  |  |  | repeated N1 times |  | repeated N2 times
time window |  |  | N1 | sub-schedule ID | N2 | group ID
type | time tag 1 | time tag 2 |  |  |  | 
enumerated | absolute time | absolute time | unsigned integer | enumerated | unsigned integer | enumerated
 | deduced presence | deduced presence | optional |  | optional | 
3) TC[11,6] – Delete the time-based scheduled activities identified by a filter
Each request to delete the time-based scheduled activities identified by a filter shall contain exactly one instruction to delete the time-based scheduled activities identified by a filter.
Each instruction to delete the time-based scheduled activities identified by a filter shall contain the filter to identify the scheduled activities to delete consisting of:
  A time window, (…)
  If sub-schedules are supported, zero or more sub-schedules;
  If groups are supported, zero or more groups.
Notes: Service 11 is a good opportunity to teach by example the concepts of requests, instructions, and the notion of multiple instructions within a request. In particular, the translation from functional to interface level shall be illustrated, showing that repeated fields may exist at interface level even if the request does not contain multiple instructions.
The last example is TC[11,6] delete the time-based scheduled activities identified by request identifier. In this case, the request only has one instruction. The instruction-level data is the filter description, which contains, among others, the list of sub-schedules and groups covered by this filter. The repetition fields (N1, N2) which are present in the interface specification are not related to instruction multiplicity, but simply to list lengths.

## Slide 123: ST[11] – Request verification
Destination APID
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
notifications
request
instr.
instr.
instr.
request
instr.
instr.
instr.
Successful/Failed Start of Request execution Notification
Single TM[1,3] Successful Start of Request Execution Report if requested
Single TM[1,4] Failed Start of Request Execution Report

## Slide 124: ST[11] – Request verification
Destination APID
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
notifications
request
instr.
instr.
instr.
request
instr.
instr.
instr.
Successful/Failed Instruction execution Notification
Single TM[1,5] Successful Progress of Request Execution Report if requested
Single TM[1,6] Failed Progress of Request Execution Report
Option 1: Using progress of request execution reports

## Slide 125: ST[11] – Request verification
Destination APID
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
notifications
request
instr.
instr.
instr.
request
instr.
instr.
instr.
Successful/Failed Instruction execution Notification
No processing on successful instruction execution notification
Storage of failed instruction execution notifications for further reporting
Option 2: Aggregating into completion reports

## Slide 126: ST[11] – Request verification
Destination APID
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
notifications
request
instr.
instr.
instr.
request
instr.
instr.
instr.
Successful/Failed Completion of Request execution Notification
Single TM[1,7] Successful Completion of Request Execution Report if requested
Single TM[1,8] Failed Completion of Request Execution Report (potentially carrying failed progress of execution notifications)

## Slide 127: ST[22] – Position-based scheduling
High level commanding |  | 
ST[11] | time-based scheduling | 
ST[18] | on-board control procedure | 
ST[21] | request sequencing | 
ST[22] | position-based scheduling | √
Standard Service Type Model
PUS
Foundation
Model
The (orbit) position-based scheduling service provides the capability to command on-board application processes using requests pre­loaded on-board the satellite and released when the Spacecraft reaches the associated position on the orbit. This Standard service does not specify how the orbit positions are determined; this is done when tailoring the service to the mission.
This service is an extension of the ground monitoring and control. As such, the application processes that execute the requests released by the position-based scheduling service directly send the request verification reports, if any, to the ground.
ST[22] scope

## Slide 128: ST[22] – Standardized subservice type
Position-based scheduling
The position-based scheduling subservice type includes the capability to maintain an on-board position-based schedule of requests and to ensure the release of those requests at the associated orbit positions.
An entry in the position-based schedule is usually deleted once the related request is released. However, the position-based scheduling subservice type provides the optional concept of persistent scheduling, which can be used to retain an entry in the schedule so that it can be reused on a later orbit.
… see next slide
Position-based scheduling service

## Slide 129: ST[22] – Standardized subservice type
Position-based scheduling, cont.
The position-based scheduling subservice type provides the optional concept of sub-schedules.
Each request in the position-based schedule is associated to a sub-schedule. Each sub-schedule consists of a sequence of position-tagged requests that perform a coherent on-board operation. If a sub-schedule has no requests with persistent scheduling status, then once the operation is completed, the sub-schedule has no further reason to exist. Therefore, sub-schedules are automatically created when used and deleted when empty. The position-based scheduling subservice type includes the capability for enabling and disabling the execution of each sub-schedule.
The position-based scheduling subservice type also provides the optional concept of groups.
Each request in the position-based schedule is associated to a group. The position-based scheduling subservice type includes the capability for enabling and disabling the execution of grouped requests, independently of the application processes they are released to and of the sub-schedules they belong to. Groups are typically related to spacecraft entities (e.g. hardware or software). Groups can be created and deleted by request and can exist even if empty. They can be used, for example, to group all requests associated to a specific instrument and disable their release when the conditions for their execution are not fulfilled, while other requests for the same application process are associated to a different group and enabled for release.
Position-based scheduling service
extension of the ground monitoring and control
Notes: Note that the contents of this slide describes the exact same concepts as for the PUS service 11. If the presentation is followed in order, it can simply be stated that the sub-schedule and group concepts have the same meaning as for service 11.

## Slide 130: ST[22] – Overview

## Slide 131: ST[22] – Overview
Initially designed as a verbatim copy of service type 11 (time-based scheduling) with an orbital positioning reference for the release of requests
Timeline replaced by an ever-increasing orbit-number, and a cyclic position tag
All operations available for time-based scheduling are also available for position-based scheduling
In addition, activities can be persistent and repeated every N orbits. Period is a property of each activity

## Slide 132: ST[22] – Important concepts
Orbit position
The position tag used to specify a position consist in:
  An orbit number, which never wraps around during a mission
  The position on that orbit
Position on the orbit is specified as the angle measured in the plane of the osculating inertial orbit starting from the intersection with the Earth Fixed Equatorial Plane (ω+ν)
Notes: The position on the orbit, as defined, corresponds to the sum of the argument of periapsis and the true anomaly of the satellite. It has to be noted that in the current wording, the requirement does not specify whether the reference node should be the ascending or descending one. This slide assumes ascending.

## Slide 133: ST[22] – Important concepts
Persistent scheduling
Optional capability of position-based scheduling
If supported, each activity can be persistent or non-persistent
If persistent, the periodicity of the activity is expressed in number of orbits and configurable per activity
When a periodic activity is processed for release, the orbit number of the activity is increased by its periodicity, and therefore rescheduled automatically

## Slide 134: ST[22] – Message types, 1
system | interface | message type |  |  |  |  |  | 
6.22.6.3.2 | 8.22.2.1 | TC[22,1] |  |  |  |  | enable the position-based schedule execution function | minimum
6.22.6.3.3 | 8.22.2.2 |  | TC[22,2] |  |  |  | disable the position-based schedule execution function | minimum
6.22.6.4 | 8.22.2.28 | TC[22,28] |  |  |  |  | set the orbit number | by declaration
6.22.6.5 | 8.22.2.3 | TC[22,3] |  |  |  |  | reset the position-based schedule | minimum
6.22.6.6 | 8.22.2.4 | TC[22,4] |  |  |  |  | insert activities into the position-based schedule | minimum
6.22.7.2.1 | 8.22.2.20 | TC[22,20] |  |  |  |  | enable position-based sub-schedules | by declaration
6.22.7.2.2 | 8.22.2.21 |  | TC[22,21] |  |  |  | disable position-based sub-schedules | implied by TC[22,20]
6.22.7.2.3 | 8.22.2.18 | TC[22,18] |  |  |  |  | report the status of each position-based sub-schedule | by declaration
6.22.7.2.3 | 8.22.2.19 |  | TM[22,19] |  |  |  | position-based sub-schedule status report | TC[22,18] response
6.22.8.2.1 | 8.22.2.22 | TC[22,22] |  |  |  |  | create position-based scheduling groups | by declaration
6.22.8.2.2 | 8.22.2.23 |  |  | TC[22,23] |  |  | delete position-based scheduling groups | implied by TC[22,22]
6.22.8.3.1 | 8.22.2.24 |  |  | TC[22,24] |  |  | enable position-based scheduling groups | implied by TC[22,22]
6.22.8.3.2 | 8.22.2.25 |  |  |  | TC[22,25] |  | disable position-based scheduling groups | implied by TC[22,24]
6.22.8.3.3 | 8.22.2.26 |  |  | TC[22,26] |  |  | report the status of each position-based scheduling group | requires TC[22,22]
6.22.8.3.3 | 8.22.2.27 |  |  |  |  | TM[22,27] | position-based scheduling group status report | TC[22,26] response
6.22.10.2 | 8.22.2.15 | TC[22,15] |  |  |  |  | position-shift all scheduled activities | by declaration
Position-based scheduling subservice ...

## Slide 135: ST[22] – Message types, 2
6.22.10.3 | 8.22.2.17 | TC[22,17] |  |  | summary-report all position-based scheduled activities | by declaration
6.22.9.1 | 8.22.2.13 |  | TM[22,13] |  | position-based schedule summary report | TC[22,17] response
6.22.10.4 | 8.22.2.16 | TC[22,16] |  |  | detail-report all position-based scheduled activities | by declaration
6.22.9.2 | 8.22.2.10 |  | TM[22,10] |  | position-based schedule detail report | TC[22,16] response
6.22.11.2 | 8.22.2.5 | TC[22,5] |  |  | delete position-based scheduled activities identified by request identifier | by declaration
6.22.11.3 | 8.22.2.7 | TC[22,7] |  |  | position-shift scheduled activities identified by request identifier | by declaration
6.22.11.4 | 8.22.2.12 | TC[22,12] |  |  | summary-report position-based scheduled activities identified by request identifier | by declaration
6.22.9.1 | 8.22.2.13 |  | TM[22,13] |  | position-based schedule summary report | TC[22,12] response
6.22.11.5 | 8.22.2.9 | TC[22,9] |  |  | detail-report position-based scheduled activities identified by request identifier | by declaration
6.22.9.2 | 8.22.2.10 |  | TM[22,10] |  | position-based schedule detail report | TC[22,9] response
6.22.12.3 | 8.22.2.6 | TC[22,6] |  |  | delete the position-based scheduled activities identified by a filter | by declaration
6.22.12.4 | 8.22.2.8 | TC[22,8] |  |  | position-shift the scheduled activities identified by a filter | by declaration
6.22.12.5 | 8.22.2.14 | TC[22,14] |  |  | summary-report the position-based scheduled activities identified by a filter | by declaration
6.22.9.1 | 8.22.2.13 |  | TM[22,13] |  | position-based schedule summary report | TC[22,14] response
6.22.12.6 | 8.22.2.11 | TC[22,11] |  |  | detail-report the position-based scheduled activities identified by a filter | by declaration
6.22.9.2 | 8.22.2.10 |  |  | TM[22,10] | position-based schedule detail report | TC[22,11] response
... position-based scheduling subservice

## Slide 136: ST[22] – Tailoring & deployment
A position based scheduling service may contain multiple position based scheduling sub-services, each one deployed on a different on-board application process
As for service type 11, it is expected that service type 22 implementations will be centralised by deploying it only on the central software application process, but nothing precludes from having multiple deployments.
How this service accesses the position information, and with which precision, is left for the mission to specify

## Slide 137: ST[22] – Implementation guidelines
ST[22] is ST[11] with a twist, with mostly the same concepts.
As specified, the position on orbit is not a linear function of time (unless the spacecraft flies a circular orbit). This must be taken into account by implementations.
Periodic activities must be assessed even if disabled – A periodic activity, disabled at the moment it should execute, is not discarded. It is simply rescheduled for the next occurrence
The concept of scheduling margin is still present but expressed in position:
  Determine margin knowing that the same difference in position may not be equivalent to the same difference in time depending on the orbit;
  Periodic activities shifted out of margin must be rescheduled for their next occurrence.
Notes: Points to develop in this tips & tricks:
Insist on the fact that the spirit is exactly the same. Only the timeline reference is changed
Position may not immediately be available on reboot, and may be imprecise / display jumps upon AOCS mode modification (i.e. switch from propagated to measured,…). Implementations should be robust to this kind of behaviour

## Slide 138: ST[22] – Implementation guidelines
Implementations should consider the possibility of position unavailability
A command exists to set the orbit number. Why is there no similar function in ST[11] – Time-based scheduling ?
  Orbit number is a concept local to ST[22], while on-board time is widespread across the system – modifying it could lead to unpredictable results
Notes: Points to develop in this tips & tricks:
Insist on the fact that the spirit is exactly the same. Only the timeline reference is changed
Position may not immediately be available on reboot, and may be imprecise / display jumps upon AOCS mode modification (i.e. switch from propagated to measured,…). Implementations should be robust to this kind of behaviour

## Slide 139: ST[18] – On-board control procedure
ST[18] scope
The on-board control procedure service is compliant with and complements the spacecraft on-board control procedures standard (refer to ECSS-E-ST-70-01).
High level commanding |  | 
ST[11] | time-based scheduling | 
ST[18] | on-board control procedure | √
ST[21] | request sequencing | 
ST[22] | position-based scheduling | 

## Slide 140: ST[18] – Standardized subservice types
OBCP management
The OBCP management subservice type provides an interface to the OBCP engine that executes OBCPs. The subservice type therefore provides the capability to control, from ground, the on-board execution of OBCPs.
For OBCP, refer to ECSS-E-ST-70-01
A list of OBCP arguments can be associated to an OBCP, corresponding to the values that it expects to receive at execution initiation time.
A list of OBCP parameters can also be associated to an OBCP, corresponding to the values that it expects to receive during execution.
Refer to ECSS-E-ST-70-31 for OBCP arguments and parameters. The validity of arguments and parameters supplied to an OBCP is checked by the OBCP itself, not by the OBCP management subservice.
OBCP engine management
The OBCP engine management subservice type provides the capability to control the OBCP engine that is responsible for executing the OBCPs.
On-board control procedure service

## Slide 141: ST[18] – Overview
OBCP:
  Procedure to be executed on-board
  Easily loaded or executed
  Can be replaced without modifying the rest of the on-board software
Additional « programs »
  In dedicated language
  Running in an on-board interpreter (OBCP engine)
  Triggered by ground or by on-board software (e.g. in response to on-board events)
  OBCPs can perform complex series of actions, including sending TM, taking logical decisions, etc.
OBCPs have a dedicated ECSS standard (ECSS-E-ST-70-01)

## Slide 142: ST[18] – Overview
Operational uses of OBCP:
  At System Design level – some functionality could be specified as OBCP for isolation, configurability or late accommodation purposes
  At Software Design level – to maintain genericity of OBSW, or to simplify maintenance
  At AIT level – to implement fault injection or complex scenarios which are not easily obtained through the TM/TC interface
  At operations level – to implement corrections without patching the software

## Slide 143: ST[18] – Important concepts
OBCP Execution status
State-transition diagram from ECSS-E-ST-70-01
Most transitions correspond to service 18 requests
Notes: A lot of information is present on this slide, and it is used as support to present most of the concepts of service 18. TBD if it should be extended by a second slide (still displaying the state diagram but indicating the S18 requests & reports).
The following concepts need to be presented:
The OBCP execution status (three sub-states of the “in engine” state)
The possibility to pre-load the OBCP in an on-board store and load by reference, or to direct load
The different transitions, indicating that all of them are actually telecommands, with the exception of the ‘completion’ transition
Skip the fact that « shortcut TCs » exist (such as Load & Activate, Stop & Delete), this will be introduced in this Service Tips & Tricks slide.

## Slide 144: ST[18] – Important concepts
OBCP Step
Smallest operational unit within an OBCP
Each step has its own identifier for OBCP execution control
OBCP Observability
Configures the generation of observability events
Increasing levels:
  None – Observability events are never generated
  Procedure – Execution status changes are reported
  Step – Each step reached is reported
  Detailed – Mission specific additional observability events
Concept of loading policy and the relationship with Files

## Slide 145: ST[18] – Message types, 1
system | interface | message type |  |  |  | 
6.18.4.4.1a |  | at least one of: TC[18,1] TC[18,13] TC[18,19] |  |  |  | minimum
6.18.4.4.2 | 8.18.2.1 | TC[18,1] |  |  | direct-load an OBCP | by declaration
6.18.4.4.3 | 8.18.2.11 | TC[18,13] |  |  | load an OBCP by reference | by declaration
6.18.4.4.4 | 8.18.2.2 |  | TC[18,2] |  | unload an OBCP | implied by TC[18,1] or TC[18,13]
6.18.4.4.5 | 8.18.2.3 | TC[18,3] |  |  | activate an OBCP | minimum
6.18.4.4.6 | 8.18.2.17 | TC[18,19] |  |  | load by reference and activate an OBCP | by declaration
6.18.4.4.7 | 8.18.2.4 | TC[18,4] |  |  | stop an OBCP | minimum
6.18.4.4.8 | 8.18.2.18 | TC[18,20] |  |  | stop and unload an OBCP | by declaration
6.18.4.4.9 | 8.18.2.10 | TC[18,12] |  |  | abort an OBCP | minimum
6.18.4.4.10 | 8.18.2.15 | TC[18,17] |  |  | abort all OBCPs and report | by declaration
6.18.4.4.10 | 8.18.2.16 |  | TM[18,18] |  | aborted OBCP report | TC[18,17] response
6.18.4.5.1 | 8.18.2.8 | TC[18,8] |  |  | report the execution status of each OBCP | minimum
6.18.4.5.1 | 8.18.2.9 |  | TM[18,9] |  | OBCP execution status report | TC[18,8] response
6.18.4.6.1 | 8.18.2.5 | TC[18,5] |  |  | suspend an OBCP | by declaration
6.18.4.6.2 | 8.18.2.6 |  | TC[18,6] |  | resume an OBCP | implied by TC[18,5]
6.18.4.6.3 | 8.18.2.12 | TC[18,14] |  |  | activate and execute one OBCP step | by declaration
6.18.4.6.4 | 8.18.2.13 |  |  | TC[18,15] | resume and execute one OBCP step | implied by TC[18,14]
6.18.4.7.1 | 8.18.2.7 | TC[18,7] |  |  | communicate parameters to an OBCP | by declaration
6.18.4.8.1 | 8.18.2.14 | TC[18,16] |  |  | set the observability level of OBCPs | by declaration
OBCP management subservice

## Slide 146: ST[18] – Message types, 2
system | interface | message type |  |  | 
6.18.5.1.1 | 8.18.2.19 | TC[18,21] |  | start the OBCP engine | minimum
6.18.5.1.2 | 8.18.2.20 |  | TC[18,22] | stop the OBCP engine | minimum
OBCP engine management subservice

## Slide 147: ST[18] – Tailoring & deployment
An on-board control procedure service shall contain exactly one OBCP management subservice, and at most one engine management subservice
It is possible to have two (or more) completely segregated on-board control procedure services (e.g. one OBCP service deployed on the central computer, and another on an intelligent payload)

## Slide 148: ST[18] – Implementation guidelines
The OBCP standard differentiates between:
  OBCP arguments, provided when starting an OBCP
  OBCP parameters, provided during OBCP execution
  They can be the same, but not necessarily. The former are provided in the ‘start’ family of requests (TC [18,3], TC [18,14], TC [18,19]), the latter in the communicate parameters request (TC [18,7]).
Several requests are defined as « Shortcuts », such as « Load & Activate » or « Stop and Unload ». Why ?
  This allows such commands to be registered as Event Actions !
OBCP capabilities are the most complex available in terms of commanding
When specifying a mission, a choice is now given between the OBCP service (very flexible, but complex), and the request sequencing service (less flexible, but offers a simpler ‘macro command’ capability)

## Slide 149: ST[18] – PUS-A to PUS-C evolution
Added features
Load by reference (from file) – TC[18,13]
Activate and execute step - TC[18,14]
Resume and execute step - TC[18,15]
Set observability level - TC[18,16]
Abort all and report - TC[18,17], TM[18,18]
Load by reference and activate - TC[18,19]
Stop and unload - TC[18,20]
Start / Stop OBCP engine TC[18,21], TC[18,22]
Updated features
Direct loading TC[18,1] now supports optional OBCP checksum
OBCP activation TC[18,3] now supports optional observability level
OBCP execution status now merged with the OBCP list TC[18,8], TM[18,9]
Mostly aligned with ECSSE-ST-70-01C
Deleted features
Removed list of active OBCP TC[18,10], TM[18,11] in favor of the above merge and observables

## Slide 150: ST[21] – Request sequencing
ST[21] scope
The request sequencing service type provides the capability to manage the release of an on-board sequence of requests. It also provides capabilities for the loading, control and reporting of on-board sequences.
High level commanding |  | 
ST[11] | time-based scheduling | 
ST[18] | on-board control procedure | 
ST[21] | request sequencing | √
ST[22] | position-based scheduling | 

## Slide 151: ST[21] – Standardized subservice type
Request sequencing
The request sequencing subservice provides the capability to release, one by one, the requests contained in an on-board sequence of requests. Within a request sequence, the delay between the release of a request and the release of the next request can be specified. Several request sequences can be running in parallel.
The service provides the capability to load a request sequence from a file stored on-board or directly from ground. When loading directly from ground, the requests that constitute the request sequence are inside the load request sequence request.
Request sequencing service
extension of the ground monitoring and control
Notes: This service is an extension of the ground monitoring and control. As such, the application processes that execute the requests released by the request sequencing subservice directly send the request verification reports, if any, to the ground.

## Slide 152: ST[21] – Overview
Provides capability to manage the release of a sequence of requests, without the complexity of an OBCP
Users requesting this new service often implemented a specific "Macro Commands" service, i.e. one high level request to gather multiple requests
A request sequence consists of a set of requests and subsequent delays.
Shares concepts with both ST[11] Time-Based Scheduling and ST[18] OBCP, keeping the simplest aspects of both

## Slide 153: ST[21] – Important concepts
Request sequence
Has a unique request sequence identifier
Contains an ordered list of request entries, each one containing:
  A single request
  The delay between the release of this request and the next one in the sequence
Can be inactive or under execution

## Slide 154: ST[21] – Important concepts
Request sequences properties
Properties similar to OBCPs:
  Can be directly loaded by ground, or loaded from a file store
  Are persistent, and can be invoked multiple times
  Cannot have multiple instances running in parallel
  Loading policy also applies
Properties similar to on-board schedule:
  Are executed « blindly », with the execution of requests not conditioned on success of previous ones
  Cannot be suspended (but well aborted – a sequence is either inactive or under execution)

## Slide 155: ST[21] – Message types
system | interface | message type |  |  |  | 
6.21.5.1a |  | at least one of: TC[21,1] TC[21,2] TC[21,8] |  |  |  | minimum
6.21.5.2 | 8.21.2.1 | TC[21,1] |  |  | direct-load a request sequence | by declaration
6.21.5.3 | 8.21.2.2 | TC[21,2] |  |  | load a request sequence by reference | by declaration
6.21.5.4 | 8.21.2.3 |  | TC[21,3] |  | unload a request sequence | implied by TC[21,1] or TC[21,2]
6.21.5.6 | 8.21.2.8 | TC[21,8] |  |  | load by reference and activate a request sequence | by declaration
6.21.5.5 | 8.21.2.4 | TC[21,4] |  |  | activate a request sequence | minimum
6.21.5.7 | 8.21.2.5 | TC[21,5] |  |  | abort a request sequence | minimum
6.21.5.8 | 8.21.2.13 | TC[21,13] |  |  | abort all request sequences and report | by declaration
6.21.5.8 | 8.21.2.14 |  | TM[21,14] |  | aborted request sequence report | TC[21,13] response
6.21.6 | 8.21.2.6 | TC[21,6] |  |  | report the execution status of each request sequence | by declaration
6.21.6 | 8.21.2.7 |  | TM[21,7] |  | request sequence execution status report | TC[21,6] response
6.21.7 | 8.21.2.9 | TC[21,9] |  |  | checksum a request sequence | by declaration
6.21.7 | 8.21.2.10 |  | TM[21,10] |  | request sequence checksum report | TC[21,9] response
6.21.8 | 8.21.2.11 | TC[21,11] |  |  | report the content of a request sequence | by declaration
6.21.8 | 8.21.2.12 |  |  | TM[21,12] | request sequence content report | TC[21,11] response
Request sequencing subservice

## Slide 156: ST[21] – Tailoring & deployment
A request sequencing service may contain multiple request sequencing sub-services deployed on multiple on-board application processes
As for previous commanding services, it is expected that service 21 implementations will be centralised by deploying it only on the central software application process, but nothing precludes from having multiple deployments.
The list of checks to be performed on the requests contained within the request sequences is part of the subservice specification.
  Note that extension of the verification activities can be extended for any command during tailoring !
  This is however explicitly stated for the request to insert activities in the position-based schedule, as the feasible checks may depend on the rest of the tailoring.

## Slide 157: ST[21] – Implementation guidelines
The last delay (after the last request) may be used to delay the completion of the sequence w.r.t. the release of the last telecommand
To what purpose ?
  Introduce a delay before the sequence can be reactivated !
  Ensure this delay is 0 if the last command is an unload for this sequence !
The actual way to checksum a sequence is not specified by the standard, as it is dependent on how the sequence is stored on board, in particular the inter-request delays
Notes: Complexity of service 21 is not so high, and most relevant subjects for in-depth inspection of this service will have already been covered in service 18.

## Slide 158: ST[21] – Implementation guidelines
Request sequencer is a ground proxy (as the on-board schedule and the event action)  Ground expects and processes the related ST[1] reports
Request sequences are persistent, but the last command of a request can be to unload the sequence, overriding this behaviour
It is unlikely that a mission will ever require ST[11], ST[22], ST[18] and ST[21], altogether. Assessing the required granularity and intelligence for commanding is part of the system analysis
Notes: Points to develop in this slide:
Point 1: The implications of request sequencing being a ground proxy is that the sequences shall be part of the ground telecommand model;
Point 2: In that case, it must be ensured that the final delay is 0, otherwise the unload command will be rejected because the sequence is active !
Point 3: Which services to embark is really an operational tradeoff. With PUS A, some missions had the operational requirement to support ‘macro TCs’ (The request sequencing service was not yet part of PUS-A). To their PUS software subcontractor, some of these missions passed a request to support service 11 with all options (i.e. including relative scheduling, interlocking) as it was the closest in functionality without embarking OBCP. Tailoring shall be performed from an operational need resulting in a more rational approach and solution.

## Slide 159
PUS for 
Downlinking - real-time & archives

## Slide 160: SET – Managing Telemetry and Data
Managing Telemetry and Data
The standard service types gathered in this set are all part of the process to manage the way data is stored on board and retrieved on the space link.
Telemetry can be produced in real-time, but most of the time, it is retrieved through playback capabilities provided by the spacecraft. The PUS standards provide means to configure these two kinds of channels.
When large quantity of data must be downlinked, the standard offers two ways to transport it: the large packet transfer service allows splitting large packets into elements which can be transferred on the space link; the file management service offers the capability to manage files, which can grow orders of magnitude larger than the maximum CCSDS packet size.
Finally, data can be directly accessed through the memory management service, which provides direct access to the on-board memories.
ST[01] | request verification | 
ST[02] | device access | 
ST[03] | housekeeping | 
ST[04] | parameter statistics reporting | 
ST[05] | event reporting | 
ST[06] | memory management | 
ST[08] | function management | 
ST[09] | time management | 
ST[12] | on-board monitoring | 
ST[13] | large packet transfer | 
ST[14] | real-time forwarding control | 
ST[15] | on-board storage and retrieval | 
ST[19] | event-action | 
ST[20] | parameter management | 
ST[23] | file management | 

## Slide 161: ST[14] – Real-time forwarding control
ST[14] scope
The real-time forwarding control service provides the capability to control the forwarding to the ground of reports (verification reports, responses and indications) generated by on-board services. The reports are forwarded to ground within a real-time telemetry channel.
This service can be used to control the reports generated by the application process that hosts the service and also to control reports generated by other application processes.
Managing telemetry and data |  | 
ST[06] | memory management | 
ST[13] | large packet transfer | 
ST[14] | real-time forwarding control | √
ST[15] | on-board storage and retrieval | 
ST[23] | file management | 

## Slide 162: ST[14] – Standardized subservice type
Real-time forwarding control subservice
The real-time forwarding control subservice type can be used to control the forwarding of reports generated by the application process that hosts the subservice and by other application processes.
This subservice type provides means to control the forwarding of reports taking into account their operational use. That control is performed, per application process, by defining application process related forwarding control conditions that when met authorize or not the forwarding of related reports.
This subservice type includes the capability for defining control conditions at application process related report type level i.e.:
conditions for all report types of an application process;
conditions for all report types of a specific service type of an application process;
conditions for a specific report type of an application process.
This subservice type includes optional capabilities for defining control conditions at:
housekeeping parameter report structure level;
diagnostic parameter report structure level;
event definition level.
Real-time forwarding control service

## Slide 163: ST[15] – On-board storage and retrieval
ST[15] - scope
The on-board storage and retrieval service is a supporting service used by other on-board services to selectively store the service reports which they generate in order to give the ground system the capability to request the downlink of the reports.
Managing telemetry and data |  | 
ST[06] | memory management | 
ST[13] | large packet transfer | 
ST[14] | real-time forwarding control | 
ST[15] | on-board storage and retrieval | √
ST[23] | file management | 

## Slide 164: ST[15] – Standardized subservice types
Storage and retrieval
The storage and retrieval subservice type provides the capability for storing the telemetry packets in the packet stores and retrieving them later, on ground request.
Each packet store can be managed according to either:
the ‘circular management’ policy, or
the ‘bounded management’ policy
Two retrieval modes are provided by the storage and retrieval subservice type:
the “open retrieval mode”, or
the "by-time-range mode".
Packet selection
The packet selection subservice type can be used to control the storage into packet stores of reports generated by any application process.
This subservice type provides means to control the storage of reports taking into account their operational use. That control is performed, per packet store, by defining application process related storage control conditions that when met authorize or not the storage of related reports to the corresponding packet store.
This subservice type includes the capability for defining packet store control conditions at application process related report type level.
This subservice type includes optional capabilities for defining control conditions at housekeeping parameter report structure level, diagnostic parameter report structure level and event definition level.
On-board storage and retrieval service
Notes: Each packet store can be managed according to either:
the ‘circular management’ policy: the oldest packets are overwritten when the packet store is full, hence the packet store contains the most recently generated packets, or
the ‘bounded management’ policy: storage terminates when the packet store is full.
Two retrieval modes are provided by the storage and retrieval subservice type:
the "open retrieval mode" that retrieves the packets that are newer than the date of the last transmitted packet before the retrieval stopped;
the "by-time-range mode" that retrieves the packets that are time stamped within two dates. This retrieval model is used to recover from packet loss during the downlink.
This subservice type includes the capability for defining packet store control conditions at application process related report type level i.e.:
conditions for all report types of an application process;
conditions for all report types of a specific service type of an application process;
conditions for a specific report type of an application process.

## Slide 165: ST[14] & ST[15] – Overview
Application
Service 14
Service 15
(Packet selection subservice)
TM flow
TM flow
Packet Stores
Real time downlink
Service 15
(Packet Retrieval Subservice)
TM flow
TM flow
Deferred downlink

## Slide 166: ST[14] – Overview
ST[14] - Real-time forwarding control subservice
Manage selection of reports to forward in real-time:
  Enable / Disable forwarding of reports
  Report forwarding selections
Selection criteria:
  Application process forward control (APID, service type ID, message subtype ID)
  Finer granularity available for housekeeping, diagnostic and event reports.

## Slide 167: ST[15] – Overview
ST[15] - Packet selection subservice
Manage selection of reports to store:
  Enable / Disable storage of reports
  Report storage selections
Selection criteria:
  Application process storage control (APID, service type ID, message subtype ID)
  Finer granularity available for housekeeping, diagnostic and event reports
Notes: The fact that this slide is almost a copy & paste of previous slide is on purpose – during the presentation, presenter is invited to go back and forth between the two slides to highlight the similarities between the two subservices. It can be added that is was actually proposed to generalize service 14, actually making it behave as a particular case of the packet selection subservice (one store value would represent the real-time channel).

## Slide 168: ST[15] – Overview
ST[15] - Storage and Retrieval subservice:
on-board storage is to telemetry downlink what on-board scheduling is to telecommand uplink: the nominal way to retrieve spacecraft telemetry
stores telemetry according to the selection made by the packet selection subservice
provides packet store interfaces for:
  retrieving and downlinking stored packet
  deleting stored packets
manages the configuration of stores:
  enabling/disabling storage
  overriding cyclic behaviour
  maintaining stores

## Slide 169: ST[14] & ST[15] – Important concepts
The ST[14] forward control definitions & ST[15] storage control definitions are now fully specified by the standard...
Forward/Storage control definitions case 1:
First level: Application process forward/storage control definitions
Select all for an APID
Message Subtype
Service Type
APID
A
Notes: This set of slides describes the forward control or storage control definitions. The principle of the packet selection for services 14 and 15 is exactly the same. The first level of selection is the “application process forward/storage control”, which handle selection by APID, type and subtype.

## Slide 170: ST[14] & ST[15] – Important concepts
Forward/Storage control definitions case 2:
First level: Application process forward/storage control definitions
Select all subtypes for one or more service types
Message Subtype
Service Type
APID
A
1
5
Notes: This set of slides describes the forward control or storage control definitions. The principle of the packet selection for services 14 and 15 is exactly the same. The first level of selection is the “application process forward/storage control”, which handle selection by APID, type and subtype.

## Slide 171: ST[14] & ST[15] – Important concepts
Forward/Storage control definitions case 3:
First level: Application process forward/storage control definitions
Select one or more service subtypes for specific service types
Message Subtype
Service Type
APID
A
1
1
7
5
Notes: This set of slides describes the forward control or storage control definitions. The principle of the packet selection for services 14 and 15 is exactly the same. The first level of selection is the “application process forward/storage control”, which handle selection by APID, type and subtype.

## Slide 172: ST[14] & ST[15] – Important concepts
Forward/Storage control definitions case 4:
Second level: Housekeeping, Diagnostic parameter report
Both selection sets must allow forwarding / storing
Msg. Subtype
Service Type
APID
A
1
1
7
3
5
4
A
APID
Structure ID
4
1
2
Main filter
Second-level filter
Notes: This set of slides describes the forward control or storage control definitions. The principle of the packet selection for services 14 and 15 is exactly the same.
The second level of selection allows adding additional criteria for housekeeping reports (based on APID+SID), diagnostic reports (APID+SID) and event reports (APID+EDID). It must be stressed that forwarding/storing must be authorized at both levels. This means that if the mission supports controlling the forwarding of housekeeping packets per housekeeping parameter report structure, if no housekeeping parameter report forward-control configuration is defined, then no housekeeping report will be forwarded.

## Slide 173: ST[14] & ST[15] – Important concepts
Forward/Storage control definitions case 5:
Second level: Event report blocking
Both selection sets must allow forwarding / storing
Msg. Subtype
Service Type
APID
A
1
1
7
3
5
4
A
APID
Event ID
553
798
1125
Main filter
Second-level filter
Notes: This set of slides describes the forward control or storage control definitions. The principle of the packet selection for services 14 and 15 is exactly the same.
The second level of selection allows adding additional criteria for housekeeping reports (based on APID+SID), diagnostic reports (APID+SID) and event reports (APID+EDID). It must be stressed that forwarding/storing must be authorized at both levels.
Specifically for event reports, the second level of configuration has been designed as a blocking table instead of a forwarding table, given that the number of event reports may be significant and only a few may need to be masked.

## Slide 174: ST[15] – Important concepts
Packet store
Memory entity that is identified by a unique packet store ID
Dedicated to storing telemetry packets
Multiple standardized optional configuration options:
  Store overwrite policy: Cyclic (most common approach) or bounded (for critical packets such as event reports)
  Virtual channel for store downlink
Data retrieval from stores
Open retrieval - Downlinks all packets newer than the date of the last transmitted packet during the previous open downlink
Time-ranged retrieval - Downlinks all packets with storage date within two specified dates

## Slide 175: ST[15] – Important concepts
Ground
S/C
Event store
HK store
TC[15,15] Resume open retrieval (priority Evt)
EVT
HK
TC[15,16] Suspend open retrieval (all)
TC[15,9] Start by-time-range retrieval (event store, missing range)
Stored EVT packets
TC[15,15] Resume open retrieval (priority Evt)
HK
Notes: This slide illustrates the new downlink paradigm, with open downlink becoming the nominal way to retrieve packets from a packet store.
In this example, two stores are defined, an event store (high priority downlink) and a hk store (low priority downlink). Greyed out areas represent non-visibility periods.
As the satellite comes in visibility, ground requests to downlink all contents of packet stores, notifying a higher priority on the event store. Event store contents are downlinked first, and as it is transmitted, the position of the last transmitted packet is maintained on board. In this example, a transmission issue causes some of the packets from the event store lost on the telemetry link.
When the event store is fully downlinked, the process continues for the HK store. As the satellite is about to come out of visibility, ground issues a command to suspend all downlinks. Again, the last downlinked packet in the HK store is maintained.
During pass post-processing, the missing packets from event store downlink are identified and tagged for re-downlink in the next pass.
(Note – For simplicity of the example, no packets are added to the stores while satellite is out of visibility – this is clearly unrealistic)
This redownlink is done using the by-time-range retrieval. Notice how this downlink method has no effect on the position of the last downlinked packet. Once the re-downlink is complete, the open downlink is resumed, and the downlink of the HK store carries out from where it last stopped.

## Slide 176: ST[15] – Important concepts
New paradigm in retrieval operations
  Open downlink is now the « nominal downlink », can be suspended, resumed
  Open retrieval operations are started using the « resume open retrieval » operation – there is no « start open retrieval »
  Open does not mean unbounded – Retrieval is suspended at the last packet stored before the start of execution of the request
  Time based downlink can only be aborted
  Specification is worded to avoid the use of the « downlink pointer » words as it would constrain the implementation, but the intention is to map on this commonly used approach

## Slide 177: ST[14] – Message types, 1
system | interface | message type |  |  |  | 
6.14.3.4.1 | 8.14.2.1 | TC[14,1] |  |  | add report types to the application process forward-control configuration | minimum
6.14.3.4.2 | 8.14.2.2 |  | TC[14,2] |  | delete report types from the application process forward-control configuration | minimum
6.14.3.4.3 | 8.14.2.3 |  | TC[14,3] |  | report the content of the application process forward-control configuration | requires TC[14,1]
6.14.3.4.3 | 8.14.2.4 |  |  | TM[14,4] | application process forward-control configuration content report | TC[14,3] response
6.14.3.2.1a |  | capability to control, per housekeeping parameter report structure, the forwarding of housekeeping parameter reports |  |  |  | by declaration
6.14.3.5.1 | 8.14.2.5 | TC[14,5] |  |  | add structure identifiers to the housekeeping parameter report forward-control configuration | implied by 6.14.3.2.1a
6.14.3.5.2 | 8.14.2.6 |  | TC[14,6] |  | delete structure identifiers from the housekeeping parameter report forward-control configuration | implied by 6.14.3.2.1a
6.14.3.5.3 | 8.14.2.7 |  | TC[14,7] |  | report the content of the housekeeping parameter report forward-control configuration | requires TC[14,5]
6.14.3.5.3 | 8.14.2.8 |  |  | TM[14,8] | housekeeping parameter report forward-control configuration content report | TC[14,7] response
6.14.3.2.1b |  | capability to control, per diagnostic parameter report structure, the forwarding of diagnostic parameter reports |  |  |  | by declaration
6.14.3.6.1 | 8.14.2.9 | TC[14,9] |  |  | add structure identifiers to the diagnostic parameter report forward-control configuration | implied by 6.14.3.2.1b
6.14.3.6.2 | 8.14.2.10 |  | TC[14,10] |  | delete structure identifiers from the diagnostic parameter report forward-control configuration | implied by 6.14.3.2.1b
6.14.3.6.3 | 8.14.2.11 |  | TC[14,11] |  | report the content of the diagnostic parameter report forward-control configuration | requires TC[14,9]
6.14.3.6.3 | 8.14.2.12 |  |  | TM[14,12] | diagnostic parameter report forward-control configuration content report | TC[14,11] response
Real-time forwarding control subservice ...

## Slide 178: ST[14] – Message types, 2
6.14.3.2.1c |  | capability to control, per event definition, the forwarding of event reports |  |  |  |  |  | by declaration
6.14.3.7.2 | 8.14.2.14 | TC[14,14] |  |  |  |  | add event definition identifiers to the event report blocking forward-control configuration | implied by 6.14.3.2.1c
6.14.3.7.1 | 8.14.2.13 |  |  |  | TC[14,13] |  | delete event definition identifiers from the event report blocking forward-control configuration | implied by 6.14.3.2.1c
6.14.3.7.3 | 8.14.2.15 |  |  |  | TC[14,15] |  | report the content of the event report blocking forward-control configuration | requires TC[14,14]
6.14.3.7.3 | 8.14.2.16 |  |  |  |  | TM[14,16] | event report blocking forward-control configuration content report | TC[14,15] response
... real-time forwarding control subservice

## Slide 179: ST[15] – Message types, 1
Packet selection subservice…
system | interface | message type |  |  |  | 
6.15.4.4.1 | 8.15.2.3 | TC[15,3] |  |  | add report types to the application process storage-control configuration | minimum
6.15.4.4.2 | 8.15.2.4 |  | TC[15,4] |  | delete report types from the application process storage-control configuration | minimum
6.15.4.4.3 | 8.15.2.5 |  | TC[15,5] |  | report the content of the application process storage-control configuration | requires TC[15,3]
6.15.4.4.3 | 8.15.2.6 |  |  | TM[15,6] | application process storage-control configuration content report | TC[15,5] response
6.15.4.2.1a |  | control, per housekeeping parameter report structure, the storage of housekeeping parameter reports |  |  |  | by declaration
6.15.4.5.1 | 8.15.2.26 | TC[15,29] |  |  | add structure identifiers to the housekeeping parameter report storage-control configuration | implied by 6.15.4.2.1a
6.15.4.5.2 | 8.15.2.27 |  | TC[15,30] |  | delete structure identifiers from the housekeeping parameter report storage-control configuration | implied by 6.15.4.2.1a
6.15.4.5.3 | 8.15.2.32 |  | TC[15,35] |  | report the content of the housekeeping parameter report storage-control configuration | requires TC[15,29]
6.15.4.5.3 | 6.15.4.5.3 |  |  | TM[15,36] | housekeeping parameter report storage-control configuration content report | TC[15,36] response

## Slide 180: ST[15] – Message types, 2
…Packet selection subservice
6.15.4.2.1b |  | control, per diagnostic parameter report structure, the storage of diagnostic parameter reports |  |  |  | by declaration
6.15.4.6.1 | 8.15.2.28 | TC[15,31] |  |  | add structure identifiers to the diagnostic parameter report storage-control configuration | implied by 6.15.4.2.1b
6.15.4.6.2 | 8.15.2.29 |  | TC[15,32] |  | delete structure identifiers from the diagnostic parameter report storage-control configuration | implied by 6.15.4.2.1b
6.15.4.6.3 | 8.15.2.34 |  | TC[15,37] |  | report the content of the diagnostic parameter report storage-control configuration | requires TC[15,31]
6.15.4.6.3 | 8.15.2.35 |  |  | TM[15,38] | diagnostic parameter report storage-control configuration content report | TC[15,37] response
6.15.4.2.1c |  | control, per event definition, the storage of event reports |  |  |  | by declaration
6.15.4.7.1 | 8.15.2.31 | TC[15,34] |  |  | add event definition identifiers to the event report blocking storage-control configuration | implied by 6.15.4.2.1c
6.15.4.7.2 | 8.15.2.30 |  | TC[15,33] |  | delete event definition identifiers from the event report blocking storage-control configuration | implied by 6.15.4.2.1c
6.15.4.7.3 | 8.15.2.36 |  | TC[15,39] |  | report the content of the event report blocking storage-control configuration | requires TC[15,33]
6.15.4.7.3 | 8.15.2.37 |  |  | TM[15,40] | event report blocking storage-control configuration content report | TC[15,39] response

## Slide 181: ST[15] – Message types, 3
Storage and retrieval subservice…
system | interface | message type |  |  | 
6.15.3.3.2 | 8.15.2.1 | TC[15,1] |  | enable the storage function of packet stores | minimum
6.15.3.3.3 | 8.15.2.2 |  | TC[15,2] | disable the storage function of packet stores | minimum
6.15.3.4.2 | 8.15.2.11 | TC[15,14] |  | change the open retrieval start time tag of packet stores | minimum
6.15.3.4.3 | 8.15.2.12 | TC[15,15] |  | resume the open retrieval of packet stores | minimum
6.15.3.4.4 | 8.15.2.13 |  | TC[15,16] | suspend the open retrieval of packet stores | implied by TC[15,15]
6.15.3.5.1a |  | by-time-range retrieval function support |  |  | by declaration
6.15.3.5.2 | 8.15.2.7 | TC[15,9] |  | start the by-time-range retrieval of packet stores | implied by 6.15.3.5.1a
6.15.3.5.3 | 8.15.2.14 |  | TC[15,17] | abort the by-time-range retrieval of packet stores | implied by 6.15.3.5.1a
6.15.3.6 | 8.15.2.15 | TC[15,18] |  | report the status of each packet store | by declaration
6.15.3.6 | 8.15.2.16 |  | TM[15,19] | packet store status report | TC[15,18] response
6.15.3.7.1 | 8.15.2.8 | TC[15,11] |  | delete the content of packet stores up to the specified time | by declaration

## Slide 182: ST[15] – Message types, 4
…Storage and retrieval subservice
6.15.3.8.1 | 8.15.2.17 | TC[15,20] |  |  | create packet stores | by declaration
6.15.3.8.2 | 8.15.2.18 |  | TC[15,21] |  | delete packet stores | implied by TC[15,20]
6.15.3.8.3 | 8.15.2.19 |  | TC[15,22] |  | report the configuration of each packet store | requires TC[15,20]
6.15.3.8.3 | 8.15.2.20 |  |  | TM[15,23] | packet store configuration report | TC[15,22] response
6.15.3.8.4 | 8.15.2.21 |  | TC[15,24] |  | copy the packets contained in a packet store selected by time window | requires TC[15,20]
6.15.3.9.1 | 8.15.2.22 | TC[15,25] |  |  | resize packet stores | by declaration
6.15.3.9.2 | 8.15.2.23 |  | TC[15,26] |  | change a packet store type to circular | implied by TC[15.25]
6.15.3.9.3 | 8.15.2.24 |  | TC[15,27] |  | change a packet store type to bounded | implied by TC[15.25]
6.15.3.9.4 | 8.15.2.25 |  | TC[15,28] |  | change the virtual channel used by a packet store | implied by TC[15.25]
6.15.3.10.1 | 8.15.2.9 | TC[15,12] |  |  | summary-report the content of packet stores | by declaration
6.15.3.10.1 | 8.15.2.10 |  | TM[15,13] |  | packet store content summary report | TC[15,12] response

## Slide 183: ST[14] – Tailoring & deployment
A real-time forwarding control service may contain multiple real-time forwarding control sub-services deployed on multiple on-board application processes
Common implementations centralize the real-time forwarding functionality on the central software directly in charge of the telemetry hardware, but this could realistically be deployed directly on telemetry producers

## Slide 184: ST[15] – Tailoring & deployment
An on-board storage and retrieval service may contain multiple packet selection sub-services deployed on multiple on-board application processes
An on-board storage and retrieval service may only contain a single storage and retrieval subservice.
Common implementations centralize the packet selection subservice on the central software directly in charge of the mass memory hardware, but this could realistically be deployed directly on telemetry producers. In that case, the details of how the store selection established by the packet selection subservice is transmitted to the storage and retrieval subservice is not specified.
The deployment of an on-board storage and retrieval subservice often requires mission specific additions in order to configure or accommodate the specific hardware providing the storage functionality.

## Slide 185: ST[14] & ST[15] – Implementation guidelines
Caution: Behaviour sometimes counterintuitive
TC [14,1] Add all report types of APID A
Msg. Subtype
Service Type
APID
A
APID | Type | Subtype | Fwd ?
A | 1 | 1 | YES
A | 1 | 2 | YES
A | 1 | 7 | YES
A | 3 | 25 | YES
A | 5 | 3 | YES
A | 5 | 4 | YES
Notes: This animated set of slides provides examples on how the application process forward-control configuration evolves when sending some add/remove commands, as well as which telemetry packets from an example set are forwarded in the current state of the configuration. The purpose is to highlight the fact that the results may be somewhat counterintuitive. Nevertheless, the interaction on the different levels (All @APID, all @ service or specific subtypes) was not clearly specified in PUS A and is now completely defined. As showed in the last slide, the current specification has been seen as the best consensus for a system in which the complete knowledge of which packets can be generated on board is not known of the service 14/15 implementation, rendering it unable to convert a list of elements into a logical “all elements” for that level.

## Slide 186: ST[14] & ST[15] – Implementation guidelines
Caution: Behaviour sometimes counterintuitive
TC [14,1]: Add message subtypes 1 and 7 for ST[1], and all message subtypes of ST[5]
Msg. Subtype
Service Type
APID
A
1
1
7
5
APID | Type | Subtype | Fwd ?
A | 1 | 1 | YES
A | 1 | 2 | NO
A | 1 | 7 | YES
A | 3 | 25 | NO
A | 5 | 3 | YES
A | 5 | 4 | YES
Notes: This animated set of slides provides examples on how the application process forward-control configuration evolves when sending some add/remove commands, as well as which telemetry packets from an example set are forwarded in the current state of the configuration. The purpose is to highlight the fact that the results may be somewhat counterintuitive. Nevertheless, the interaction on the different levels (All @APID, all @ service or specific subtypes) was not clearly specified in PUS A and is now completely defined. As showed in the last slide, the current specification has been seen as the best consensus for a system in which the complete knowledge of which packets can be generated on board is not known of the service 14/15 implementation, rendering it unable to convert a list of elements into a logical “all elements” for that level.

## Slide 187: ST[14] & ST[15] – Implementation guidelines
Caution: Behaviour sometimes counterintuitive
TC [14,2]: Remove message subtypes 1 and 7 for ST[1]
Msg. Subtype
Service Type
APID
A
1
1
7
5
APID | Type | Subtype | Fwd ?
A | 1 | 1 | NO
A | 1 | 2 | NO
A | 1 | 7 | NO
A | 3 | 25 | NO
A | 5 | 3 | YES
A | 5 | 4 | YES
Notes: This animated set of slides provides examples on how the application process forward-control configuration evolves when sending some add/remove commands, as well as which telemetry packets from an example set are forwarded in the current state of the configuration. The purpose is to highlight the fact that the results may be somewhat counterintuitive. Nevertheless, the interaction on the different levels (All @APID, all @ service or specific subtypes) was not clearly specified in PUS A and is now completely defined. As showed in the last slide, the current specification has been seen as the best consensus for a system in which the complete knowledge of which packets can be generated on board is not known of the service 14/15 implementation, rendering it unable to convert a list of elements into a logical “all elements” for that level.

## Slide 188: ST[14] & ST[15] – Implementation guidelines
Caution: Behaviour sometimes counterintuitive
TC [14,1]: Add message subtype 3 for ST[5]
Msg. Subtype
Service Type
APID
A
5
APID | Type | Subtype | Fwd ?
A | 1 | 1 | NO
A | 1 | 2 | NO
A | 1 | 7 | NO
A | 3 | 25 | NO
A | 5 | 3 | YES
A | 5 | 4 | NO
3
Notes: This animated set of slides provides examples on how the application process forward-control configuration evolves when sending some add/remove commands, as well as which telemetry packets from an example set are forwarded in the current state of the configuration. The purpose is to highlight the fact that the results may be somewhat counterintuitive. Nevertheless, the interaction on the different levels (All @APID, all @ service or specific subtypes) was not clearly specified in PUS A and is now completely defined. As showed in the last slide, the current specification has been seen as the best consensus for a system in which the complete knowledge of which packets can be generated on board is not known of the service 14/15 implementation, rendering it unable to convert a list of elements into a logical “all elements” for that level.

## Slide 189: ST[14] & ST[15] – Implementation guidelines
Caution: Behaviour sometimes counterintuitive
TC [14,2]: Remove message subtype 3 and for ST[5]
  This specification is based on the principle of non-explicit knowledge of all packets on board: When the last item of a list is removed, the parent level entry is removed. However, adding each item of a list individually is never converted to an “all” at parent level
Msg. Subtype
Service Type
APID
A
5
APID | Type | Subtype | Fwd ?
A | 1 | 1 | NO
A | 1 | 2 | NO
A | 1 | 7 | NO
A | 3 | 25 | NO
A | 5 | 3 | NO
A | 5 | 4 | NO
3
Notes: This animated set of slides provides examples on how the application process forward-control configuration evolves when sending some add/remove commands, as well as which telemetry packets from an example set are forwarded in the current state of the configuration. The purpose is to highlight the fact that the results may be somewhat counterintuitive. Nevertheless, the interaction on the different levels (All @APID, all @ service or specific subtypes) was not clearly specified in PUS A and is now completely defined. As showed in the last slide, the current specification has been seen as the best consensus for a system in which the complete knowledge of which packets can be generated on board is not known of the service 14/15 implementation, rendering it unable to convert a list of elements into a logical “all elements” for that level.
E.g.: adding TM[5,1], TM[5,2], TM[5,3], TM[5,4] one by one does not result in adding all subtypes of report type 5.

## Slide 190: ST[15] – Implementation guidelines
Sensitivity of the ST[15] storage & retrieval subservice to hardware
Given the large memory sizes, processing related to this subservice shifts towards hardware implementations
Private subservices are often needed to address the configuration of the hardware supporting the implementation.
Not a problem: what is standardized is what is expected to be common between all missions
The standard offers provision for implementation dependencies (e.g. resizing packet stores)
This service is memory agnostic (it does not need to know how stores are physically represented)
Store creation, deletion and resizing is standardized, but mapping to the physical memory is not
Access to virtual channels
Time stamping method (storage date, packet date)
Mirroring (multiple redundant copies for the same packet store, as in Galileo FOC or Euclid)
Notes: The behaviour of the storage and retrieval subservice is highly dependant of the way the packet stores are implemented. As this slide indicates, this subservice is now mostly implemented in hardware, which brings higher throughput but also constrains. The standard provisions for implementation specificities in several functions, but it has also to be reminded that mission architects are invited to extend the standard with additional service subtypes when needed (e.g. for configuration), or to add dedicated verification items in existing, standard service subtypes.
Some hardware or mission specific aspects (such as mirroring) may require rewording of some functional requirements or error conditions.

## Slide 191: ST[14] – PUS-A to PUS-C evolution
Added features
None
Deleted features
None
Updated features
Added optional support for sub-sampling housekeeping and diagnostic TC[14,5], TM[14,8], TC[14,9], TM[14,12] (based on SID for selection)
Functional requirements clarify expected behaviour when combining several levels of filtering
Reversed logic for event forwarding – now event blocking
Notes: Interface of service 14 is largely unchanged, however attention needs to be brought on the second and third bullets as they may go unnoticed while browsing the standard. Event report forwarding is now based on a ‘blocking’ list instead of a ‘forwarding’ list, as the event blocking list is expected to be way smaller than the forwarding list, and allows not having a priori knowledge of the generated events.
Also, clear functional requirements have been set up in order to clarify the expected behaviour of the service when enable/disable all commands conflict with enable some/disable some.
The sub-sampling feature for HK/DIAG filtering is based on the SID, and allows service 14 to only transfer one report every N on the real-time channel (allowing the report to be stored at its nominal rate, but forwarded to ground in real time with a lower frequency, without having to define twice the same report with different collection intervals)

## Slide 192: ST[15] – PUS-A to PUS-C evolution
Deleted features
Removed support for filtering by packet range (APID/SSC) – TC[15,7], TC[15,10]
Removed Packet Store Contents Report encapsulation packet – TM[15,8]
Updated features
Retrieval by time range simplified to only between two times – TC[15,9]
Updated contents of Catalogue report:
  Information related to APID/SSC removed;
  New information related to open retrieval
Notes: Service 15 has received a major overhaul. On one hand, it has been simplified by removing the capabilities related to the filtering by APID and SSC for downlinking or deleting packets. Rationale for this change is double: With the ever increasing sizes of mass memories, the probability of this identifier not representing a unique packet increased significantly (SSC wraps around at 16384). In addition, the ability to locate a single packet is resource consuming when dealing with such large amounts of data, where time, supposed to be ever-increasing, can support more performant search methods.
(... Follow on next slide)

## Slide 193: ST[15] – PUS-A to PUS-C evolution
Added features
Open retrieval: downlink pointer management:
  Set start time – TC[15,14]
  Resume Open Retrieval – TC[15,15]
  Suspend Open Retrieval – TC[15,16]
Downlink Statuses:
  Abort downlinks by time range – TC[15,17]
  Report packet store statuses – TC[15,18], TM[15,19)
Notion of downlink priority added – TC[15,9], TC[15,15]
Store management:
  Create / delete packet stores TC[15,20], TC[15,21]
  Report store configuration TC[15,22], TM[15,23]
  Copy store contents – TC[15,24]
  Resize packet stores – TC[15,25]
  Set type to circular / bounded – TC[15,26], TC[15,27]
  Set downlink virtual channel – TC[15,28]
Packet selection enhanced:
  Add, delete, report contents of selection tables
  Based on housekeeping SID, diagnostic SID, event EDID (blocking)
  TC[15,28] to TC[15,40]
ST[15] now mirrors ST[14]
Notes: On the other hand, multiple new service subtypes have been added to support new functionalities. Among these, a very common way to operate mass memories has been standardized: the open retrieval. The principle is to keep track of a « downlink pointer » indicating the first packet not yet downlinked in the store; when open retrieval is active, it downlinks all packets from this pointer, and updates the downlink pointer on the way. This is seen as the nominal way to retrieve store contents, while the retrieval by time range can be used if parts have been missed.

## Slide 194: ST[13]- Large packet transfer
ST[13] scope
The ground to space protocol implementations usually limits the maximum length of the CCSDS telemetry and telecommand packets to transfer. These limitations imply that large telecommand packets sent by ground for on-board services and large telemetry packets generated by the on-board services for ground need a specific protocol to manage their transfer.
The large packet transfer service implements such protocol by splitting a large packet into smaller packets, each containing a part of the large packet. The smaller packets can be transferred between ground and space, and the large packet can be reconstructed from its parts at the receiving end.
Managing telemetry and data |  | 
ST[06] | memory management | 
ST[13] | large packet transfer | √
ST[14] | real-time forwarding control | 
ST[15] | on-board storage and retrieval | 
ST[23] | file management | 

## Slide 195: ST[13] – Standardized subservice types
Large packet uplink
The large packet uplink subservice type is composed of:
a sending entity type which includes the capability, for the ground, to:
receive and decompose a large packet into an ordered sequence of parts;
encapsulate each part within a request, i.e. an "uplink part request";
uplink the part requests.
a receiving entity type which includes the capability, on-board, to:
collect all part requests received from the uplink sending entity for a given large packet;
rebuild the large packet from the parts extracted from the part requests;
deliver the large packet to its destination.
Large packet downlink
The large packet downlink subservice type is composed of:
a sending entity type which includes the capability, on-board, to:
receive and decompose large packets into ordered sequences of parts;
encapsulate each part within a report, i.e. a "downlink part report";
downlink the part reports.
a receiving entity type which includes the capability, for the ground, to:
collect all received part reports for a given large packet;
rebuild the large packet from the parts extracted from these part reports;
deliver the large packet to its destination.
Large packet transfer service
Notes: The uplink part request generated by the large packet uplink takes into account the mission maximum telecommand packet length constraint
The downlink part report generated by the large packet downlink takes into account the mission maximum telemetry packet length constraint

## Slide 196: ST[13] – Overview
Fills a gap between applicative layer and transfer layer for CCSDS TM/TC packets (up to a maximum size of 64 KB)
Usually, missions use maximum uplink/downlink packet sizes that are significantly lower than the CCSDS maximum sizes
Two symmetric subservices
  Large packet uplink
  Large packet downlink
Similar principles in each subservice:
  Messages are split in first part, intermediate parts, and last part
  A transmission timeout limits the time between two successive parts
Notes: Add notes related to reasons why missions use lower that CCSDS maximum size and introduce the frame concept (CLTU and CADU)

## Slide 197: ST[13] – Message types
system | interface | message type |  | 
6.13.3.3.1 | 8.13.2.1 | TM[13,1] | first downlink part report" for the first part | minimum
6.13.3.3.1 | 8.13.2.2 | TM[13,2] | intermediate downlink part report" for the intermediate parts | minimum
6.13.3.3.1 | 8.13.2.3 | TM[13,3] | last downlink part report" for the last part | minimum
Large packet downlink subservice
system | interface | message type |  | 
6.13.4.3.1 | 8.13.2.4 | TC[13,9] | uplink the first part" for the first part | minimum
6.13.4.3.1 | 8.13.2.5 | TC[13,10] | uplink an intermediate part" for the intermediate parts | minimum
6.13.4.3.1 | 8.13.2.6 | TC[13,11] | uplink the last part" for the last part | minimum
6.13.4.3.3 | 8.13.2.7 | TM[13,16] | large packet uplink abortion report | minimum
Large packet uplink subservice

## Slide 198: ST[13] – Tailoring & deployment
A large packet transfer service:
  May contain up to one large packet downlink subservice
  May contain up to one large packet uplink subservice
  Must contain at least one of these two
Each of these subservices is composed of two entities, one on board and one on ground.
If a mission implements both subservices, the two on-board entities must be hosted by the same application process.

## Slide 199: ST[13] – PUS Foundation
APID
ground application process
Large packet transfer service
Space Segment
Ground Segment
Large packet uplink subservice
Large packet uplink subservice provider
Large packet uplink subservice user
Large packet downlink subservice
Large packet downlink subservice provider
Large packet downlink subservice user
sending
entity
APID
subservice
subservice provider
subservice user
TC packet
request
request
TC packet
TC packet
request
TC packet
TC
TC packet
pac
TC packet
ket

## Slide 200: ST[13] – PUS Foundation
APID
ground application process
Large packet transfer service
Space Segment
Ground Segment
Large packet uplink subservice
Large packet uplink subservice provider
Large packet uplink subservice user
Large packet downlink subservice
Large packet downlink subservice provider
Large packet downlink subservice user
APID
subservice
subservice provider
subservice user
report
TM packet
TM packet
TM
TM packet
pac
TM packet
ket
TM packet
report
report
TM packet
sending
entity

## Slide 201: ST[13] – Implementation guidelines
Splitting packets into parts fitting the maximum packet size is this service’s sole purpose:
  No possibility to repeat missing parts
  No confirmation of reception (apart from the effect of the original, split packet)
  Only notification of failed reconstructions
Does not allow transferring raw data
  This service works with packets only
  Transfer of files or large data (>64KB) is not covered by the large packet transfer
If an application needs to transmit more that 64 KB data, the Standard foresees that either:
  the use of files as specified in service type 23, or
  the originating application process splits the data into individual, stand-alone messages (see example in service 6 hereafter).

## Slide 202: ST[13] – PUS-A to PUS-C evolution
Added features
None
Deleted features & Updated features
Previously named « Large Data Transfer »
Reduced scope of service only to large packets (< 64k)
Removal of features suitable for larger transfers:
  Sliding window concept TC[13,5], TM[13,14], TM[13,15]
  Repetition of parts TC[13,6], TM[13,7], TC[13,12]
  Uplink/Downlink manual abort TM[13,4], TC[13,8], TC[13,13]

## Slide 203: ST[06] – Memory management
ST[06] scope
The term "memory" is used to logically refer to any physical or virtual memory area which exists on-board the satellite, e.g. RAM, mass memory unit, file system.
The memory management service provides the capability for loading, dumping and checking the contents of these memories without precluding that the same memory is used by more than one memory management service or that overlapping memories are used on-board.
Managing telemetry and data |  | 
ST[06] | memory management | √
ST[13] | large packet transfer | 
ST[14] | real-time forwarding control | 
ST[15] | on-board storage and retrieval | 
ST[23] | file management | 

## Slide 204: ST[06] – Standardized subservice types
Raw data memory management
The raw data memory management provides the capability to access and manage memories whose type is not implicitly known
Structured data memory management
The structured data memory management provides the capability to access and manage memories whose type is implicitly known
Common memory management
The common memory management provides additional capabilities that are common to both access schemes (raw data and structured data)
Memory configuration
The memory configuration provides the capability to configure memories as a whole, regardless of their contents
Memory management service

## Slide 205: ST[06] – Overview
Manages the accesses to all kind of memories on-board
Access and manage memories whose type is not implicitly known
Access and manage memories whose type is implicitly known
Additional capabilities common to both access schemes
Configure memories as a whole, regardless of their contents

## Slide 206: ST[06] – Important concepts
Memory accessing schemes
123a3d4c6e2348621b65c143514a616de8543621690849510b984009840e984a09840d9840984138713984261c9842621eda57568740f8465f846578621048eada968504895426b87561a21357821590792129e5421621b0597a5c249e21109875123387560a3274f98e4d6b1c984e632846a201568e40d65210786c51a657489854b0198d4089e4026a871068c8d7098045a67ed86c0104861263b4e86d015c60a16e8e10615d8d684c06d840a684e0d6510c968d406a854e06d840c684a68e4d06c840a684e0d684c068a410b68d406a84e563510d3541041987a0354d78a6
Raw:
    Type of data not implicitly known
    Addressing using absolute offset from start of memory
Structured:
    Type of data implicitly known
    Addressing identifying the object, then the offset within the object
    Objects can be elements of a configuration table, files,…
Address: 207
Address: Item 3, offset 55
Address: file2.dat, offset 17

## Slide 207: ST[06] – Important concepts
Both addressing schemes provide the same operations:
  Load
  Dump
  Check
  Load by reference
  Dump to file
One extra request for structured memories:
  Check object (whose length is implicitly known)
One extra request for raw memory:
  Load atomic (read-modify-write)
Notes: Load, check and dump are the core of memory management service since PUS A. The other functionalities have been introduced in PUS-C. Relatively speaking, the memory management service is one of the existing services which received the most additions in the transition towards PUS-C.
Load by reference and dump to file have been added to allow writing or reading large quantities of data without relying on multiple, individual packets. The data to load or to dump is read from or written to a file, so that this file can subsequently be transferred as a whole. This trend to make some services file-aware is emphasized when discussing the file management service in the long version of the PUS training course (introduction to file based operations).
The check object request is a specific request provided by the structured memory management subservice. The reason why the structured memory management subservice supports this additional request is that the size of the objects is implicitly known. It is therefore possible to request the checksum of a complete object, e.g. a file, without having to specify its size.
Finally, the atomic load (in full text: Load a raw memory atomic data in a non-interruptible transaction) is a new capability provided by the raw memory management subservice. It allows performing an non-interruptible read-modify-write cycle on a memory area. This is for example useful to modify specific status bits in a 32-bit word.

## Slide 208: ST[06] – Important concepts
PUS-C introduced two new subservices:
Common memory management – Tools that interact with both management subservices:
  Abort all dumps
  …
  and that’s it.
Memory configuration – Requests acting on memories as a whole:
  Manage scrubbing process
  Manage write protection
Notes: This slide illustrates the fact that a single request needed the creation of a dedicated subservice. Indeed, a need was expressed to have a single request that could stop all ongoing dump processes. Since two different subservices provide the capability to dump (raw & structured), it is the only way to allow acting on both with a single request.
The memory configuration subservice gather requests which act on memories as a whole. Capabilities which have been considered for standardization at this stage are the scrubbing processes (implemented on most missions) and to possibility to write protect memories (which the standard allows doing at the whole memory level – some missions implementing local write protections will still need to define they own commands).

## Slide 209: ST[06] – Message types, 1
system | interface | message type |  |  | 
6.6.3.3.1 | 8.6.2.2 | TC[6,2] |  | load raw memory data areas | minimum
6.6.3.4 | 8.6.2.5 | TC[6,5] |  | dump raw memory data | minimum
6.6.3.4 | 8.6.2.6 |  | TM[6,6] | dumped raw memory data report | TC[6,5] response
6.6.3.5 | 8.6.2.9 | TC[6,9] |  | check raw memory data | by declaration
6.6.3.5 | 8.6.2.10 |  | TM[6,10] | checked raw memory data report | TC[6,9] response
6.6.3.6 | 8.6.2.19 | TC[6,19] |  | load raw memory data areas by reference | by declaration
6.6.3.7 | 8.6.2.20 | TC[6,20] |  | dump raw memory data areas to file | by declaration
6.6.3.3.2 | 8.6.2.11 | TC[6,11] |  | load a raw memory atomic data area in a non-interruptible transaction | by declaration
Raw data memory management subservice

## Slide 210: ST[06] – Message types, 2
system | interface | message type |  |  | 
6.6.4.4 | 8.6.2.1 | TC[6,1] |  | load object memory data | minimum
6.6.4.5 | 8.6.2.3 | TC[6,3] |  | dump object memory data | minimum
6.6.4.5 | 8.6.2.4 |  | TM[6,4] | dumped object memory data report | TC[6,3] response
6.6.4.6 | 8.6.2.7 | TC[6,7] |  | check object memory data | by declaration
6.6.4.6 | 8.6.2.8 |  | TM[6,8] | checked object memory data report | TC[6,7] response
6.6.4.7 | 8.6.2.17 | TC[6,17] |  | check an object memory object | by declaration
6.6.4.7 | 8.6.2.18 |  | TM[6,18] | checked object memory object report | TC[6,17] response
6.6.4.8 | 8.6.2.21 | TC[6,21] |  | load object memory data areas by reference | by declaration
6.6.4.9 | 8.6.2.22 | TC[6,22] |  | dump object memory data areas to file | by declaration
Structured data memory management subservice

## Slide 211: ST[06] – Message types, 3
system | interface | message type |  | 
6.6.5.1 | 8.6.2.12 | TC[6,12] | abort all memory dumps | minimum
Common memory management subservice
system | interface | message type |  |  |  | 
6.6.6.1.1a |  | scrubbing memories support |  |  |  | by declaration
6.6.6.1.4 | 8.6.2.13 | TC[6,13] |  |  | enable the scrubbing of a memory | implied by 6.6.6.1.1a
6.6.6.1.5 | 8.6.2.14 |  |  | TC[6,14] | disable the scrubbing of a memory | implied by 6.6.6.1.1a
6.6.6.2.1a |  | write protecting memories support |  |  |  | by declaration
6.6.6.2.4 | 8.6.2.15 | TC[6,15] |  |  | enable the write protection of a memory | implied by 6.6.6.2.1a
6.6.6.2.5 | 8.6.2.16 |  | TC[6,16] |  | disable the write protection of a memory | implied by 6.6.6.2.1a
Memory configuration subservice

## Slide 212: ST[06] – Tailoring & deployment
A memory management service:
  May contain up to one instance of its four subservices
  Must contain at least one of the raw or the structured data memory management
If a mission implements more than one subservice of the memory management service, all subservices must be deployed on the same on-board application process
It is generally required that all kind of memories on board are accessible through this service (local to the central computer or on remote devices)
  Implementation of access to remote devices is either performed by the central software (in which case the way it communicates with the remote device is not standardised), or within the remote device (in which case it provides its own implementation of a memory management service)

## Slide 213: ST[06] – Implementation guidelines
Service 6 has the potential to rely on very large requests and reports (load & dump respectively)
Packets up to 64 Kbytes can be transmitted using the Large Packet Transfer service (ST[13])
If more than 64 Kbytes of data must be uploaded, ground shall split the operation into multiple maximum size load requests
If more than 64 Kbytes of data must be downloaded, the current version of the standard requires that ground splits the operation into multiple maximum size dump requests
  This behaviour does not correspond to usual operation practices
  In response to a single, very large dump request, multiple memory dump reports are generated, each one being stand-alone (the offset indicates the current offset, the size is the current packet size)
  A change request shall be emitted against these requirements (6.6.3.4.c.3 & 6.6.4.5.c.4)
Notes: Memory dumps correspond to the use case where it is the most common to require the potential generation of packets larger than the maximum CCSDS packet size. This case could however happen in multiple other services which cause the reporting of a large quantity of data to ground (e.g. dumping the mission timeline). Establishment of proper requirements to cover these cases will also be asked for in the change request mentioned in this slide.
It can also be mentioned that some missions have chosen to use the grouping flags (in the CCSDS header) to indicate that packets are related to each other and part of a larger logical block. Each packet is however stand alone and can be decoded without the others.

## Slide 214: ST[06] – PUS-A to PUS-C evolution
Added features
Load & Dump related:
  Load atomic data (read-modify-write using bit masks) – TC[6,11]
  Abort all memory dumps – TC[6,12]
Memory level commands:
  Enable / Disable Scrubbing – TC[6,13] & TC[6,14]
  Enable / Disable Write Protection – TC[6,15] & TC[6,16]
Extension of memory checks:
  Check memory object – TC[6,17] & TM[6,18]
Deleted features
None
Updated features
All lengths are now expressed in octets (but alignment has to be checked !)
Usage of base & offset representation clarified (explicitly expanded to files)
Notes: Not many changes have been introduced to service 6 commands. The only major changes is that all lengths are now expressed in bytes instead of SAU’s. The previous scheme was considered error prone, and prevented the representation of service 6 parameters as variable character strings, since the meaning of the datalength varied from memory ID to memory ID.
The base + offset addressing scheme also has been clarified. There is no functional modification to this part, but usage of this scheme was not always fully understood. As a reminder, this addressing scheme can be used to access table elements, symbols, or even files.
Several commands have been added to extend service 6.
Atomic data load allows modifying single bits of memory areas in an uninterruptible read-modify-write cycle. A command to abort all ongoing dumps has been introduced as these are potentially long processes which may need to be stopped in contingency cases.
Commands have been added to manage properties of memories as a whole. Memory scrubbing activity and write protection status are parameters which are independant of the actual data stored, and affect the complete memory id.
Finally, a new command to check objects has been added. It is only applicable to the base + offset addressing scheme, and uses the implicitly known size of the memory object to compute the checksum.

## Slide 215: ST[06] – Request verification
Destination APID
Acceptance & Reporting Subservice
Subservice Provider
Execution Reporting Subservice
notifications
request
instruction
request
instruction
Successful/Failed Progress of Instruction execution Notification
Single TM[1,5] Successful Progress of Request Execution Report if requested
Single TM[1,6] Failed Progress of Request Execution Report

## Slide 216: ST[23] – File management
ST[23] scope
The file management service provides the capability to manage on-board file systems and files.
This Standard assumes the presence of a dedicated file transfer layer, e.g. the CCSDS file delivery protocol, to copy files between the ground and the space systems but does not standardize the corresponding protocol.
Managing telemetry and data |  | 
ST[06] | memory management | 
ST[13] | large packet transfer | 
ST[14] | real-time forwarding control | 
ST[15] | on-board storage and retrieval | 
ST[23] | file management | √

## Slide 217: ST[23] – Standardized subservice types
File handling
The file handling subservice type provides capabilities for interfacing to the on-board file handling system, for file and directory management operations.
File copy
The file copy subservice type provides capabilities for copying or moving files within a file system or between different systems. For example, the capabilities include:
copying a file from an on-ground file system to an on-board file system;
copying a file from an on-board file system to a ground file system;
controlling a file copy operation by suspending, resuming or aborting it.
File management service

## Slide 218: ST[23] – Overview
Files
ST[23] exposes the on-board file system, and possibly file transfer layer, to the Space-Ground Interface
  the file management service assumes existence of these components
  specification of an on-board file system or a file transfer layer is out of the scope of the PUS standard
Only deals with files as containers – File management service:
  has no knowledge of the data contained in files
  cannot interpret file data
  to be made file-aware, other services need to define their own accessing scheme
Notes: When presenting service 23, it is important to pass the message that the purpose of the PUS is not to specify the functionality of a file system or of a file transfer layer, but rather to expose the capabilities of such an object.
With respect to the last sub-bullet, the in-depth version of the course contains a few slides on the concept of File Based Operations, indicating which services already include file-awareness, and with pointers on how the others could fill the gap.

## Slide 219: ST[23] – Important concepts
File handling subservice
Supports flat or structured file systems
Maps the most common file management requests and reports:
  create, delete, lock or unlock a file
  report file attributes, find a file
  create, delete, rename directories
  list directories

## Slide 220: ST[23] – Important concepts
File copy subservice
Provides request to copy or move files:
  within an on-board file system
  between on-board file systems
  from a remote (e.g. ground) to an on-board file system
  from an on-board to a remote (e.g. ground) file system
Allows controlling ongoing copy operations:
  suspend
  resume
  abort
If remote file-systems are accessible, relies on a file transfer layer (e.g. CFDP)
Notes: While presenting the file copy subservice, it can be highlighted that the physical location is transparent to the high-level request. The copy file request specifies a source file path and a destination file path – the information on where these file paths are actually located is known when interpreting these paths. Depending on the source and destination paths, the kind of operation which is triggered varies:
For a copy within an on-board file system, the operation will be implemented by the file system itself;
For a copy between on-board file systems, the operation may be implemented by the file transfer protocol if supported, or by a process implemented at the file copy subservice level;
For a copy involving a remote file system, the operation will be implemented by the file transfer engine. In the example of CFDP, this means initiating a Put or Get transaction

## Slide 221: ST[23] – Message types, 1
system | interface | message type |  |  |  | 
6.23.4.1.1 | 8.23.2.1 | TC[23,1] |  |  | create a file | minimum
6.23.4.1.2 | 8.23.2.2 |  | TC[23,2] |  | delete a file | minimum
6.23.4.2 | 8.23.2.3 | TC[23,3] |  |  | report the attributes of a file | minimum
6.23.4.2 | 8.23.2.4 |  | TM[23,4] |  | file attribute report | TC[23,3] response
6.23.4.3.1 | 8.23.2.5 | TC[23,5] |  |  | lock a file | by declaration
6.23.4.3.2 | 8.23.2.6 |  | TC[23,6] |  | unlock a file | implied by TC[23,5]
6.23.4.4 | 8.23.2.7 | TC[23,7] |  |  | find files | by declaration
6.23.4.4 | 8.23.2.8 |  | TM[23,8] |  | found files report | TC[23,7] response
6.23.4.5.1 | 8.23.2.9 | TC[23,9] |  |  | create a directory | by declaration
6.23.4.5.2 | 8.23.2.10 |  | TC[23,10] |  | delete a directory | implied by TC[23,9]
6.23.4.5.3 | 8.23.2.11 |  | TC[23,11] |  | rename a directory | implied by TC[23,9]
6.23.4.6 | 8.23.2.12 | TC[23,12] |  |  | summary-report the content of a repository | by declaration
6.23.4.6 | 8.23.2.13 |  |  | TM[23,13] | repository content summary report | TC[23,12] response
File handling subservice

## Slide 222: ST[23] – Message types, 2
system | interface | message type |  |  |  | 
6.23.5.2.2 | 8.23.2.14 | TC[23,14] |  |  | copy a file | minimum
6.23.5.2.3 | 8.23.2.15 | TC[23,15] |  |  | move a file | by declaration
6.23.5.3.1 | 8.23.2.16 | TC[23,16] |  |  | suspend file copy operations | by declaration
6.23.5.3.2 | 8.23.2.17 |  | TC[23,17] |  | resume file copy operations | implied by TC[23,16]
6.23.5.3.3 | 8.23.2.19 | TC[23,19] |  |  | suspend all file copy operations involving a repository path | by declaration
6.23.5.3.4 | 8.23.2.20 |  | TC[23,20] |  | resume all file copy operations involving a repository path | implied by TC[23,19]
6.23.5.4.1 | 8.23.2.18 | TC[23,18] |  |  | abort file copy operations | by declaration
6.23.5.4.2 | 8.23.2.21 | TC[23,21] |  |  | abort all file copy operations involving a repository path | by declaration
6.23.5.5.2 | 8.23.2.22 | TC[23,22] |  |  | enable the periodic reporting of the file copy status | by declaration
6.23.5.5.3 | 8.23.2.24 |  |  | TC[23,24] | disable the periodic reporting of the file copy status | implied by TC[23,22]
6.23.5.5.4 | 8.23.2.23 |  |  | TM[23,23] | file copy status report | TC[23,22] response
File copy subservice

## Slide 223: ST[23] – Tailoring & deployment
A file management service:
  must contain exactly one file handling subservice
  may contain up to one file copy subservice
If a mission implements more than one subservice of the file management service, all subservices must be deployed on the same on-board application process
Similarly to on-board storage, it is expected that the file management service requires mission specific additions to configure the specific on-board file system or file transfer layer

## Slide 224: ST[23] – Implementation guidelines
A CCSDS file transfer engine: CFDP
CFDP is the CCSDS standardised file transfer protocol
Designed for transferring files over space links:
  Limited system resources
  Communication links with varying characteristics (Noise, bandwidth, uni/half/full-duplex, service interruptions, long propagation delays)
  Supports reliable or unreliable (best effort) transfers
  Supports waypoints, with either direct transfers or store & forward
Notes: Although the new service 23 does not directly map on the CFDP, it is however seen as the most natural file transfer protocol to rely on for space missions. The next slides briefly present this protocol without digging too much in the details.

## Slide 225: ST[23] – Implementation guidelines
A CCSDS file transfer engine: CFDP
An example transaction (unreliable)
Notes: This is an example of class 1 (unreliable) file transfer. In this case, the transfer is initiated by ground toward a command to the on-board CFDP user. In the frame of the PUS, this corresponds to a PUS 23,14 copy file request, with a source path corresponding to an on-board file and a destination path corresponding to a ground file. In unreliable mode, a transfer is split in:
A metadata protocol data unit, containing the details of the transfer (file names, size,…)
One to many file data units, containing the actual file segments
An End Of File protocol data unit, indicating the end of the file transfer and carrying the file checksum.

## Slide 226: ST[23] – Implementation guidelines
A CCSDS file transfer engine: CFDP
An example transaction (reliable)
Notes: This is an example of class 2 (reliable) file transfer.
In reliable mode, a transfer is split in:
A metadata protocol data unit, containing the details of the transfer (file names, size,…)
One to many file data units, containing the actual file segments
An End Of File protocol data unit, indicating the end of the file transfer and carrying the file checksum.
The receiving end acknowledges the End of File, then provides a list of missing file segments, if any. Upon reception of such NAK packets, the source retransmits the segments marked as missing.
When the receiving entity has received all packets, it generates a “finished” protocol data unit, which is acknowledged by the source to terminate the transaction.
Multiple NAK patterns exist and are configurable through the MIB. For example, NAKs can be generated as soon as a missing segment is detected, or upon source request.

## Slide 227: ST[23] – Implementation guidelines
File usage
The file management service does not access file contents; other services can be made file-aware.
File Based Operations is a concept where the command and control paradigm is shifted from packets to files
It builds on the possibility to transfer potentially large files using reliable protocols
PUS-C initiates a first step in making some services file-aware
Notes: As explained in the service overview, the file management service manipulates files as containers. They are never read or written, but rather created, moved, or deleted. At operations level, files can have many uses. Several studies into the so called File-Based Operations have highlighted how files could be used as main exchange unit, rather than packets, and how they could be used by the current services.
Some conclusions of FBO have been used in the transition from PUS-A to PUS-C for the services for which file utilisation is the most obvious. These applications are presented on the next slides, as well as more prospective possibilities for the future.

## Slide 228: File usage
Service 6 – Memory Management
Service 18 - OBCP
Service 21 – Request Sequencing
Low level access (read/write)
Load from file (e.g. patches)
Dump to file
Load by reference
Service 23 – File Management
Memory
File System
PUS-C
Notes: This slide lists all file-aware services in the C version of the PUS standard. When following the normal order of the presentation, all these services have already been introduced.

## Slide 229: File usage – as seen in 2018
PUS-C
Service 6 – Memory Management
Service 18 - OBCP
Service 21 – Request Sequencing
Low level access (read/write)
Load from file (e.g. patches)
Dump to file
Load by reference
Service 23 – File Management
Memory
File System
ST[22] Position-based Scheduling
ST[15]
On-board storage
ST[11]
Time-based Scheduling
Any configurable service
Telemetry files
Complete timelines
Complete configuration tables
Future usage ?
Notes: This slide presents possible extensions of the file usage as presented in the FBO studies. This is not part of the PUS-C standardisation, and only provides some perspectives of which other services could be made file-aware in the future.

## Slide 230: File usage – where we are going
PUS-C
Service 6 – Memory Management
Service 18 - OBCP
Service 21 – Request Sequencing
Low level access (read/write)
Load from file (e.g. patches)
Dump to file
Load by reference
Service 23 – File Management
Memory
File System
ST[22] Position-based Scheduling
ST[25]
Data source management
ST[11]
Time-based Scheduling
Mapping of data sources to files (e.g. by Spacewire Logical Address)
Routing of certain packets to files similar to Packet stores
Complete timelines
Revision 1 under drafting
ST[24]
Downlink management
Control of downlink entities
Queue management with prioritization for automatic downlink
Notes: This slide presents work in progress in the revision 1 working group. Dedicated sections of the presentation will be created once the corresponding services are fully drafted; in the meanwhile, this slide highlights the addition of the future Data Source Management and Downlink Management Services

## Slide 231: Wrap-Up
Service 6 Raw
Service 6 Structured
Service 15
Service 23 Handling
Service 23 Copy
Notes: This figure comes from the FMSIS study, performed under the supervision of the SAVOIR MASAIS group, and summarizes data organisation when both files and packet stores are supported. It wraps up the telemetry and data section.
The meaning of the acronyms is the following:
SAU: Smallest Addressable Unit (i.e. the smallest block of memory that can be addressed on the hardware)
BAU: Block Access Unit (i.e. the smallest block of memory that can be accessed through the interface proposed)
FS: File System
FMS: File Management Service
FTS: File Transfer Service
DMS: Data Management Service

## Slide 232
PUS for 
On-board parameters

## Slide 233: SET – On-board parameters
On-board parameters
The standard service types gathered in this set are all involved with the management, observation, modification or monitoring of on board parameters.
The PUS standard defines a “parameter” as the lowest level of elementary data item on-board. Practically, it can represent any on-board item, such as a measurement from a sensor, actuations computed by the GNC, or current state of a software process. They are accessed through a single identifier, named parameter identifier.
Operationally, most, if not all parameters are statically defined. A common implementation is to have a centralized data-pool, but such an implementation cannot be assumed.
The standard links four capabilities to parameters:
Cyclically reporting their value;
Providing statistics on their evolution;
Monitoring their value against provided references;
Directly accessing their value or modifying their definition for increased flexibility in observation.
ST[01] | request verification | 
ST[02] | device access | 
ST[03] | housekeeping | 
ST[04] | parameter statistics reporting | 
ST[05] | event reporting | 
ST[08] | parameter management | 
ST[09] | time management | 
ST[12] | on-board monitoring | 
ST[19] | event-action | 
ST[20] | parameter management | 

## Slide 234: On-board parameters
Monitoring & Control
Displays

## Slide 235: ST[20] – On-board parameter management
ST[20] scope
The parameter management subservice relates to the management of on-board parameters, providing the capability to read their current values and set new values.
The service can also be used to change the definition of some of these parameters. In the context of this service, the parameter definition consists of the mapped on-board memory address and the packet field type code (PTC) and format code (PFC).
On-board parameters |  | 
ST[03] | housekeeping | 
ST[04] | parameter statistics reporting | 
ST[12] | on-board monitoring | 
ST[20] | on-board parameter management | √

## Slide 236: ST[20] – Standardized subservice type
Parameter management
The parameter management subservice type includes the capability to maintain a list of parameter definitions, where each definition consists of the parameter identifier, the mapped on-board memory address and the packet field code.
The parameter identifiers are predefined and unique within the context of the spacecraft.
The packet field code contains a packet field type code (PTC) and format code (PFC).
The parameter management subservice type includes optional capability to create new parameters by associating a new parameter memory location or a new field code to a predefined parameter identifier. For example, a new parameter can be used for an OBCP or for exporting an existing internal variable as a parameter for housekeeping or monitoring.
On-board parameter management service

## Slide 237: ST[20] – Overview
New service introduced in PUS-C
Most missions were already implementing part of this service, which made it obvious for standardization
Two aspects:
Manage parameter values:
  Read parameter value
  Write parameter value (!)
Manage parameter definitions:
  Change definitions (!)
  Report definitions
Notes: The parameter management service is probably the service, among those introduced in PUS-C, for which inclusion was the most obvious. The read/write parameter commands seem to be a natural functionality to provide as soon as the concept of parameter is introduced.
The actual way to define a parameter (or to change its definition) is to map parameter types on memory areas, using either the raw or structured access type. This is further described in the next slide.
The exclamation marks next to the write parameter value and change parameter definitions is there to draw attention that these can be hazardous. Practically, missions may not allow the modification of parameters, or only a subset of them. In a similar approach, only some parameters (e.g. a dedicated parameter id range) will have a configurable definition.

## Slide 238: ST[20] – Important concepts
Parameter definition
Indicate where to find it
    Using one of the addressing schemes allowed for the memory as presented for service 6
    One request exists to define a parameter for each addressing scheme
Indicate how to interpret it
    Address is not enough
    e.g. the size needs to be known
    Parameter types are described using the « packet field code » representation
123a3d4c6e2348621b65c143514a616de8543621690849510b984009840e984a09840d9840984138713984261c9842621eda57568740f8465f846578621048eada968504895426b87561a21357821590792c984e632846a201568e40d65210786c51a657
Unsigned integer ?
IEEE Floating point ?
Signed integer ?
Notes: Defining a parameter consists in indicating where the information to map is located in memory and how it must be interpreted. The address only gives the first byte of the parameter, but at least its size needs to be known for proper utilisation in requests of this service (read parameter, write parameter) and in housekeeping reports; for usage in monitoring, the actual nature of the parameter needs to be known in order to allow comparisons against threshold values.
The PTC/PFC notation is presented in the next slides.

## Slide 239: ST[20] – Important concepts
A standard notation exists to define parameter types:
  the « Packet field Type Code »
    determines the data type of the parameter
PTC | simple type correspondence
1 | Boolean
2 | enumerated
3 | unsigned integer
4 | signed integer
5 | real
6 | bit-string
7 | octet-string
8 | character-string
9 | absolute time
10 | relative time
11 | deduced
12 | packet

## Slide 240: ST[20] – Important concepts
A standard notation exists to define parameter types:
  the « Packet field Type Code »
    determines the data type of the parameter
  the « Packet field Format Code »
    determines the way the parameter is encoded
    depends on the PTC
PTC | simple type correspondence
1 | Boolean
2 | enumerated
3 | unsigned integer
4 | signed integer
5 | real
6 | bit-string
7 | octet-string
8 | character-string
9 | absolute time
10 | relative time
11 | deduced
12 | packet
PFC | format definition | lowest value | highest value
0 to 12 | (PFC + 4) bits, unsigned |  | 
13 | 3 octets, unsigned |  | 
14 | 4 octets, unsigned |  | 
15 | 6 octets, unsigned |  | 
16 | 8 octets, unsigned |  | 
17 | 1 bit, unsigned | 0 | 1
18 | 2 bits, unsigned | 0 | 3
19 | 3 bits, unsigned | 0 | 7
PFC | format definition | lowest value | highest value
0 to 12 | (PFC + 4) bits, unsigned |  | 
13 | 3 octets, unsigned |  | 
14 | 4 octets, unsigned |  | 
15 | 6 octets, unsigned |  | 
16 | 8 octets, unsigned |  | 
17 | 1 bit, unsigned | 0 | 1
18 | 2 bits, unsigned | 0 | 3
19 | 3 bits, unsigned | 0 | 7
PFC | format definition
0 | Variable-length character-string
n > 0 | Fixed-length character-string with a number of characters equal to PFC

## Slide 241: ST[20] – Message types
system | interface | message type |  |  |  |  | 
6.20.4.1 | 8.20.2.1 | TC[20,1] |  |  |  | report parameter values | minimum
6.20.4.1 | 8.20.2.2 |  | TM[20,2] |  |  | parameter value report | TC[20,1] response
6.20.4.2 | 8.20.2.3 | TC[20,3] |  |  |  | set parameter values | by declaration
6.20.5.2 | 8.20.2.4 | TC[20,4] |  |  |  | change raw memory parameter definitions | by declaration
6.20.5.3 | 8.20.2.5 | TC[20,5] |  |  |  | change object memory parameter definitions | by declaration
6.20.5.4 | 8.20.2.6 |  |  | TC[20,6] |  | report parameter definitions | requires TC[20,4] or TC[20,5]
6.20.5.4 | 8.20.2.7 |  |  |  | TM[20,7] | parameter definition report | TC[20,6] response
Parameter management subservice

## Slide 242: ST[20] – Tailoring & deployment
A parameter management service may contain multiple parameter management sub-services deployed on multiple on-board application processes
It is expected that implementations centralize the parameter management functionality on the central software when it implements a datapool to manage parameters.
In all cases, on-board parameter identifiers are requested to be unique within the context of the spacecraft

## Slide 243: ST[20] – Implementation guidelines
Parameters are essential to operations. Changing their value or their definition must be treated with the same caution as when loading memory.
The standard restricts changing parameter definitions to a specific subset of configurable parameters which must be declared upon service specification
Any service relying on parameters (Housekeeping, Monitoring, Statistics, or any mission specific application) is affected by a change of definition
Changing parameter values may also be either hazardous (mission parameters) or ineffective (e.g. parameters cyclically updated through acquisitions)
  Although not standardized, nothing precludes restricting the set parameter values function to a subset of settable parameters if the mission requires it.
  Persistency of changes across reboots is not addressed by the standard (as for any service that may rely on default configurations)
Notes: As hinted in the overview slide, setting parameter values and changing parameter definitions can have unexpected consequences if used freely. This slide explains the safeguards that are required by the standard (only a restricted subset of configurable parameters can be redefined), and recommends an additional protection for setting the value (although not standardized as of today).

## Slide 244: ST[03] – Housekeeping
ST[03] scope
The housekeeping service controls and adapts the spacecraft reporting plan according to the mission phases.
The housekeeping service provides the visibility of any on-board parameters assembled in housekeeping or diagnostic parameter report types as required for the mission. The parameter report types used by the housekeeping service can be predefined on-board or created when needed.
The housekeeping service is composed of three subservices:
the housekeeping reporting subservice,
the diagnostic reporting subservice, and
the parameter reporting configuration subservice.
On-board parameters |  | 
ST[03] | housekeeping | √
ST[04] | parameter statistics reporting | 
ST[12] | on-board monitoring | 
ST[20] | on-board parameter management | 

## Slide 245: ST[03] – Standardized subservice types
Housekeeping reporting
dedicated to nominal operations
parameter reports can be generated periodically or on request
periodic generation can be enabled/disabled
parameter reports are collections of simply commutated parameters and/or super commutated parameters
Diagnostic reporting
dedicated to contingency operations
parameter reports can be generated periodically or on request
periodic generation can be enabled/disabled
parameter reports are collections of simply commutated parameters and/or super commutated parameters
Parameter functional reporting configuration
The parameter functional reporting configuration subservice type provides the capability to control the generation of the parameter reports generated by the housekeeping and the diagnostic reporting subservices e.g. to ease the management of housekeeping configuration on mode transitions.
It operates on sets of parameter reports, of housekeeping or diagnostic nature, e.g. enabling or disabling the generation of such sets. Functional configurations can be applied exclusively, in which case the periodic generation of each report type of the service is disabled before applying the functional configurations.
Housekeeping service
≈
Notes: Parameter functional reporting configuration subservice:
« meta-subservice »
Manages sets of housekeeping and/or diagnostic reports
Nicknamed « TM mode » subservice, it provides a convenient way to reconfigure reporting according to the current spacecraft mode.

## Slide 246: ST[03] – Overview
Defines three subservice types:
Housekeeping reporting subservice type
Diagnostic reporting subservice type
  Management and generation of reports
  Periodic or on request
  Two very similar subservices
Parameter functional reporting configuration subservice type
  « meta-subservice »
  Manages sets of housekeeping and/or diagnostic reports
  Nicknamed « TM mode » subservice, it provides a convenient way to reconfigure reporting according to the current spacecraft mode.
Notes: TBD – maybe remove slide. It is almost redundant with previous slide, but all services currently have an overview slide.

## Slide 247: ST[03] – Important concepts
Housekeeping and Diagnostic
Two operational subservices types with similar functional and interface specifications
Why would we do that ?
Report definition:
  Structure ID
  Collection interval
  List of parameters
Parameters
SID 1:
Every second, sample and report parameters 1,2,3,4,5.

## Slide 248: ST[03] – Important concepts
Housekeeping and Diagnostic
Two operational subservices with similar functional and interface specifications
Why would we do that ?
Report definition:
  Structure ID
  Collection interval
  List of parameters sampled once
  List of super-commutated parameters:
    Number of samples
    List of parameters
Parameters
SID 1:
Every second, sample and report parameters 1,2,3,4,5.
SID 2:
Every minute, generate a report containing one sample of parameter 6, three samples of parameters 7,8,9, and six samples of parameters 3 to 4.

## Slide 249: ST[03] – Important concepts
Housekeeping and diagnostic subservices
  Enable/disable the generation of reports individually
2
1
5
3
4
6
7

## Slide 250: ST[03] – Important concepts
Parameter functional reporting configuration
  groups, for enabling/disabling, housekeeping parameter reports
     allows simple transitions from one spacecraft mode to another
Each configuration
  contains the enable/disable action to perform on selected reports
  can be applied
      inclusively
      exclusively
  can also specify collection intervals for each report
2
1
5
3
4
6
7
2
1
5
3
4
6
7
2
1
5
3
4
6
7

## Slide 251: ST[03] – Message types, 1
system | interface | message type |  |  |  |  | 
6.3.3.3 | 8.3.2.13 | TM[3,25] |  |  |  | housekeeping parameter report | minimum
6.3.3.4.1 | 8.3.2.5 | TC[3,5] |  |  |  | enable the periodic generation of housekeeping parameter reports | by declaration
6.3.3.4.2 | 8.3.2.6 |  |  | TC[3,6] |  | disable the periodic generation of housekeeping parameter reports | implied by TC[3,5]
6.3.3.5.1 | 8.3.2.1 | TC[3,1] |  |  |  | create a housekeeping parameter report structure | by declaration
6.3.3.5.2 | 8.3.2.3 |  | TC[3,3] |  |  | delete housekeeping parameter report structures | implied by TC[3,1]
6.3.3.6 | 8.3.2.9 |  | TC[3,9] |  |  | report housekeeping parameter report structures | requires TC[3,1]
6.3.3.6 | 8.3.2.10 |  |  | TM[3,10] |  | housekeeping parameter report structure report | TC[3,9] response
6.3.3.8 | 8.3.2.17 |  | TC[3,29] |  |  | append parameters to a housekeeping parameter report structure | requires TC[3,1]
6.3.3.9 | 8.3.2.19 | TC[3,31] |  |  |  | modify the collection interval of housekeeping parameter report structures | by declaration
6.3.3.10 | 8.3.2.21 | TC[3,33] |  |  |  | report the periodic generation properties of housekeeping parameter report structures | by declaration
6.3.3.10 | 8.3.2.23 |  | TM[3,35] |  |  | housekeeping parameter report periodic generation properties report | TC[3,33] response
6.3.3.7 | 8.3.2.15 | TC[3,27] |  |  |  | generate a one-shot report for housekeeping parameter report structures | by declaration
6.3.3.3 | 8.3.2.13 |  |  |  | TM[3,25] | housekeeping parameter report | TC[3,27] response
Housekeeping reporting subservice

## Slide 252: ST[03] – Message types, 2
system | interface | message type |  |  |  |  | 
6.3.4.3 | 8.3.2.14 | TM[3,26] |  |  |  | diagnostic parameter report | minimum
6.3.4.4 | 8.3.2.7 | TC[3,7] |  |  |  | enable the periodic generation of diagnostic parameter reports | minimum
6.3.4.5 | 8.3.2.8 |  | TC[3,8] |  |  | disable the periodic generation of diagnostic parameter reports | minimum
6.3.4.6 | 8.3.2.2 | TC[3,2] |  |  |  | create a diagnostic parameter report structure | minimum
6.3.4.7 | 8.3.2.4 |  | TC[3,4] |  |  | delete diagnostic parameter report structures | minimum
6.3.4.8 | 8.3.2.11 |  | TC[3,11] |  |  | report diagnostic parameter report structures | requires TC[3,2]
6.3.4.8 | 8.3.2.12 |  |  | TM[3,12] |  | diagnostic parameter report structure report | TC[3,11] response
6.3.4.10 | 8.3.2.18 |  | TC[3,30] |  |  | append parameters to a diagnostic parameter report structure | requires TC[3,2]
6.3.4.11 | 8.3.2.20 | TC[3,32] |  |  |  | modify the collection interval of diagnostic parameter report structures | by declaration
6.3.4.12 | 8.3.2.22 | TC[3,34] |  |  |  | report the periodic generation properties of diagnostic parameter report structures | by declaration
6.3.4.12 | 8.3.2.24 |  | TM[3,36] |  |  | diagnostic parameter report periodic generation properties report | TC[3,34] response
6.3.4.9 | 8.3.2.16 | TC[3,28] |  |  |  | generate a one-shot report for diagnostic parameter report structures | by declaration
6.3.4.3 | 8.3.2.14 |  |  |  | TM[3,26] | diagnostic parameter report | TC[3,28] response
Diagnostic reporting subservice

## Slide 253: ST[03] – Message types, 3
system | interface | message type |  |  |  |  | 
6.3.5.3 | 8.3.2.25 | TC[3,37] |  |  |  | apply parameter functional reporting configurations | minimum
6.3.5.4.1 | 8.3.2.26 | TC[3,38] |  |  |  | create a parameter functional reporting definition | by declaration
6.3.5.4.2 | 8.3.2.27 |  | TC[3,39] |  |  | delete parameter functional reporting definitions | implied by TC[3,38]
6.3.5.5 | 8.3.2.28 |  | TC[3,40] |  |  | report parameter functional reporting definitions | requires TC[3,38]
6.3.5.5 | 8.3.2.29 |  |  | TM[3,41] |  | parameter functional reporting definition report | TC[3,40] response
6.3.5.6.1 | 8.3.2.30 |  | TC[3,42] |  |  | add parameter report definitions to a parameter functional reporting definition | requires TC[3,38]
6.3.5.6.2 | 8.3.2.31 |  |  |  | TC[3,43] | remove parameter report definitions from a parameter functional reporting definition | implied by TC[3,42]
6.3.5.6.3 | 8.3.2.32 | TC[3,44] |  |  |  | modify the periodic generation properties of parameter report definitions of a parameter functional reporting definition | by declaration
Parameter functional reporting configuration subservice

## Slide 254: ST[03] – Tailoring & deployment
A housekeeping service:
  Must contain at least one housekeeping reporting subservice
  May contain one or more diagnostic reporting subservices
  May contain up to one parameter functional reporting configuration subservice
The way housekeeping and diagnostic reporting subservices are deployed is generally linked to the on-board parameter management:
  Centralised datapool architectures lead to single subservice deployments
  Distributed architectures may lead to deployments where each node is responsible for its own housekeeping/diagnostic reporting
  In all cases, parameter functional reporting configuration subservice must be centralised

## Slide 255: ST[03] – Implementation guidelines
Minimum sampling interval
All collection intervals (time between the generation of two successive reports) are expressed in multiples of the minimum sampling interval
All on-board parameters accessed by an application process must have the same minimum sampling interval
This does not mean all parameters must be sampled at this rate.
Super-commutated parameters
Using super-commutated parameter sets provides increased flexibility on resources usage (e.g. bandwidth)
The presence of these parameters however limits the usage of some functions:
  Generate one-shot report: handling of super-commutated parameters is not specified by the standard (reject/adapt)
  Append parameters: only super-commutated parameter sets can be added to a definition which already contain some
Notes: Note: Watch out for the meaning of “sampling” in the PUS. For the housekeeping service, the sampling time is the moment the parameter is read from where it is made available, i.e. most likely not the actual acquisition from the hardware but rather the reading of its value out of a datapool.

## Slide 256: ST[03] – Implementation guidelines
Report structure
In order:
Structure ID
All simply commutated parameters
For each super-commutated parameter set, the complete sample set repeated as many times as specified
Timestamping
Unless there exists dedicated parameters, one single timestamp is available at report level
The acquisition timing policy must be specified at mission level (i.e. how to deduce timestamps of individual samples from the report timestamp)
SID 2:
Every minute, generate a report containing one sample of parameter 6, three samples of parameters 7,8,9, and six samples of parameters 3 to 4.
6
71
81
91
72
82
92
73
83
93
31
41
32
42
..
..
3n
4n
SID
Notes: An example of timestamping scheme:
Simply commutated parameters are collected at the end of the collection interval
The last sample of the super-commutated parameters sets is collected at the end of the collection interval
Previous samples of the super-commutated parameters sets are collected every (collection interval / NREP).
In this example, it means that if the report has a timestamp of T:
samples 6, 7-3, 8-3, 9-3, 3-6, 4-6 have been collected at time T;
Samples 3-5, 4-5 have been collected at time T-10s
Samples 7-2, 8-2, 3-4, 4-4 have been collected at time T-20s;
…
Samples 3-1, 4-1 have been collected at time T-50s.

## Slide 257: ST[03] – PUS-A to PUS-C evolution
Added features
New commands for housekeeping and diagnostic reporting subservices:
  Generate one-shot report – TC[3,27], TC[3,28]
  Append parameters to structure – TC[3,29], TC[3,30]
  Modify collection interval – TC[3,31], TC[3,32]
  Report generation status – TC[3,33] to TM[3,36]
New parameter functional reporting configuration subservice:
  Apply configuration – TC[3,37]
  Create, delete, report configuration – TC[3,38] to TM[3,41]
  Add/ remove report to/from configuration - TC[3,42], TC[3,43]
  Modify periodic generation status of report in configuration – TC[3,44]
Deleted features
Sampling time offsets – TC[3,13] to TM[3,16]
Filtered mode – TC[3,17] to TM[3,24]
Updated features
None
Notes: A significant bunch of the ‘old’ service 3 has been removed from the standard. All commands related to the sampling time offsets functionality (getting the precise time when parameters are sampled from the hardware) and filtered mode (production of housekeeping reports upon change detection) were scratched because of few / no implementations.
On the other hand, commonly used features for the parameter reporting subservice have been added. The possibility to generate one-shot reports is useful when combined to event action, or to use on-board definitions for on-demand housekeeping. Appending parameters to an existing structure allows quick modifications without having to reload the complete HK definitions, and allows large housekeeping structure even if the TC size is limited in the mission. In the same way, changing the collection interval is now possible without having to redefine the report, as HK packets may be needed at different frequencies at different times in the mission. Finally, additional observability is given on the enabled/disabled status of each houseekeping/diagnostic report, as this information is not suitable as observables (dynamic, and numerous)
In addition, a new subservice, the parameter functional reporting configuration subservice, has been introduced. It allows defining the configuration of HK/DIAG reports and change them completely with a single telecommand. This concept is illustrated in the slides before.

## Slide 258: ST[03] – Implementation guidelines
Possible important revision 1 change to housekeeping
Problem of message type counter continuity when changing the routing of some HK packets
Currently only two such counters for an APID: HK and DIAG packets
Create additional categories? Yes, but inflation of commands
Currently recommended solution: Additional categories with implicit association between SIDs and subtypes
Potential consequence: Generalisation of the service, but also simplification as diagnostic falls in the generalisation (see next slide)
TM | Example of SID ranges | Name | Proposed routing
TM[3,25] | 25.000 – 25.999 | Standard housekeeping parameter report | Real-time and on-board storage for later retrieval
TM[3,26] | 26.000 – 26.999 | Diagnostic housekeeping parameter report | On-board storage only for later retrieval
TM[3,45] | 45.000 – 45.999 | Essential housekeeping parameter report | Real-time only, no on-board storage
TM[3,46] | 46.000 – 46.999 | Troubleshooting housekeeping parameter report | On-board storage only, optional retrieval
TM[3,47] | 47.000 – 47.999 | Spare 1 housekeeping parameter report | 
TM[3,48] | 48.000 – 48.999 | Spare 2 housekeeping parameter report | 
Notes: Table extracted from the WG presentation by I. Clerigo. Proposed routing is for example only and can be changed at any time

## Slide 259: ST[03] – Implementation guidelines
Possible important revision 1 change to housekeeping
TC | Purpose
TC[3,1] | Create HKTM Report
TC[3,2] | Create Diagnostic Report
TC[3,3] | Delete HKTM Report
TC[3,4] | Delete Diagnostic Report
TC[3,5] | Enable HKTM Report
TC[3,6] | Disable HKTM Report
TC[3,7] | Enable Diagnostic Report
TC[3,8] | Disable Diagnostic Report
TC[3,9] | Report HKTM structures
TC[3,11] | Report Diagnostic structures
TC[3,27] | Generate one-shot HKTM Report
TC[3,28] | Generate one-shot Diagnostic Report
TC[3,29] | Append params to HKTM Report
TC[3,30] | Append params to Diagnostic Report
TC[3,31] | Change gen interval HKTM Report
TC[3,32] | Change gen interval Diagnostic Report
TC[3,33] | Report Gen properties HKTM structures
TC[3,34] | Report Gen properties Diagnostic structures
TC | Purpose
TC[3,1] | Create HKTM Report
TC[3,3] | Delete HKTM Report
TC[3,5] | Enable HKTM Report
TC[3,6] | Disable HKTM Report
TC[3,9] | Report HKTM structures
TC[3,27] | Generate one-shot HKTM Report
TC[3,29] | Append params to HKTM Report
TC[3,31] | Change gen interval HKTM Report
TC[3,33] | Report Gen properties HKTM structures
Simplify!
Notes: Tables extracted from the WG presentation by I. Clerigo.

## Slide 260: ST[04] – Parameter statistics reporting
ST[04] scope
The parameter statistics reporting service provides the capability to evaluate statistics on-board for a list of on-board parameters.
This service is especially appropriate for missions with limited ground coverage (e.g. low Earth orbiter), where a statistics report can be used to provide a summary of the behavior of parameters during the previous period of "no contact".
On-board parameters |  | 
ST[03] | housekeeping | 
ST[04] | parameter statistics reporting | √
ST[12] | on-board monitoring | 
ST[20] | on-board parameter management | 

## Slide 261: ST[04] – Standardized subservice type
Parameter statistics reporting
This subservice reports to the ground system the maximum, minimum, mean and standard deviation values of these on-board parameters during a time interval.
This can, for example, be used to reduce the quantity of engineering data that is systematically reported to the ground system.
The parameter statistics reporting subservice type includes optional capability to modify the list of evaluated parameters and their associated time intervals.
Parameter statistics reporting service

## Slide 262: ST[04] – Overview
Parameter statistics
  Minimum & maximum (with time of occurrence) mean, standard deviation
  Collected since start time or last reset
  Periodic or on demand reporting
Commands
  Enable / Disable / Reset
  Add / Remove parameters
  Select periodic/filtered mode
  Report parameter list
Allows reducing bandwidth by down sampling
Allows summarizing data after a period of no contact
Notes: Not often used

## Slide 263: ST[04] – Message types
system | interface | message type |  |  |  |  | 
6.4.4 | 8.4.2.3 | TC[4,3] |  |  |  | reset the parameter statistics | minimum
6.4.5.2 | 8.4.2.1 | TC[4,1] |  |  |  | report the parameter statistics | minimum
6.4.5.3 | 8.4.2.2 |  | TM[4,2] |  |  | parameter statistics report | TC[4,1] response
6.4.6.1a |  | support for the periodic reporting of the results of the parameter statistics evaluation |  |  |  |  | by declaration
6.4.6.2 | 8.4.2.4 | TC[4,4] |  |  |  | enable the periodic parameter statistics reporting | implied by 6.4.6.1a
6.4.6.3 | 8.4.2.5 |  | TC[4,5] |  |  | disable the periodic parameter statistics reporting | implied by 6.4.6.1a
6.4.7.1 | 8.4.2.6 | TC[4,6] |  |  |  | add or update parameter statistics definitions | by declaration
6.4.7.2 | 8.4.2.7 |  |  | TC[4,7] |  | delete parameter statistics definitions | implied by TC[4,6]
6.4.7.3 | 8.4.2.8 |  |  | TC[4,8] |  | report the parameter statistics definitions | requires TC[4,6]
6.4.7.3 | 8.4.2.9 |  |  |  | TM[4,9] | parameter statistics definition report | TC[4,8] response
Parameter statistics reporting subservice

## Slide 264: ST[04] – Tailoring & deployment
A parameter statistics reporting service may contain multiple parameter statistics reporting sub-services deployed on multiple on-board application processes

## Slide 265: ST[04] – Implementation guidelines
Two schemes for resetting the parameter statistics:
Automatically reset upon reporting
Explicitly stated in the request to report statistics
Optional sampling and reporting intervals can be defined:
Sampling interval is defined for each parameter. It should be adjusted to the actual sampling frequency of the parameter. A too high frequency wastes on-board computational resources
Reporting interval is defined at subservice level. It should be adjusted according to the usage made of the statistics. A too high frequency wastes bandwidth.

## Slide 266: ST[04] – PUS-A to PUS-C evolution
Added features
None
Deleted features
None
Updated features
Addition of the end of time range in TM[4,2]
Notes: Service 4 is mainly unchanged. A single parameter, giving the end time of the collection of statistics, has been added to the (4,2) report.

## Slide 267: ST[12] – On-board monitoring
ST[12] scope
The on-board monitoring service provides the capability to monitor on-board parameters or groups of parameters and react to the violations of the related monitoring conditions by raising event reports that can be sent to ground and caught on-board, e.g. by an event-action subservice.
The on-board monitoring service is composed of two subservices, the parameter monitoring subservice and the functional monitoring subservice.
On-board parameters |  | 
ST[03] | housekeeping | 
ST[04] | parameter statistics reporting | 
ST[12] | on-board monitoring | √
ST[20] | on-board parameter management | 

## Slide 268: ST[12] – Standardized subservice types
Parameter monitoring
The parameter monitoring subservice type provides the capability to:
monitor on-board parameters with respect to checks defined by the ground system,
to report any parameter check transitions to the ground, and
when monitoring conditions are violated to raise events.
The types of check depend on the parameter and its type (limit check, expected value, delta change).
Functional monitoring
The functional monitoring subservice type provides the capability to monitor the functional health of on-board elements (e.g. software applications, hardware).
A functional monitoring definition includes a set of one or more parameter monitoring definitions: when a minimum number of these definitions is contemporaneously violated, that functional monitoring definition is considered violated and the associated event is raised.
The behaviour of the functional monitoring subservice type relies on the parameter monitoring subservice type.
On-board monitoring service
Notes: Parameter Monitoring:
For each parameter and associated check, a parameter monitoring definition is specified. This Standard does not introduce any limitation on the number of checks that can be performed on an on-board parameter. A parameter monitoring definition can specify warning limits for an on-board parameter when another definition can specify danger limits for that same parameter. A parameter can be at the same time limit checked and delta checked, using two different parameter monitoring definitions.
The parameter monitoring subservice type provides optional capability to include a conditional check in a parameter monitoring definition. If the conditional check is false, the parameter monitoring check in that definition is not performed. For example, this can be used to disable the monitoring of an on-board parameter when the associated equipment is inactive.

## Slide 269: ST[12] – Overview
Parameter monitoring subservice
Maintains and executes checks at parameter level
Fully configurable (modify existing / create new definitions)
Can be used to implement parameter level FDI
Functional monitoring subservice
Builds upon parameter monitoring subservice
Fully configurable (modify existing / create new definitions)
Can be used to implement functional level FDI (isolation at a functional level, e.g. an instrument)
Requires protection (both at functional and parameter monitoring levels)
Notes: Protecting a functional monitoring definition prevents from:
Deleting this FMON;
Enabling, Disabling, Deleting or Modifying any PMON included in this FMON
FDI stands for Fault Detection and Isolation

## Slide 270: ST[12] – Important concepts
Parameter monitoring definition
Parameter monitoring definition identifier
Monitored on-board parameter identifier
Optional validity condition (parameter/mask/value)
Monitoring interval (time between two evaluations of the monitor)
Check definition
  Number of repetitions needed to establish new checking status
    Expected value check (possibly masked)
    Limit check
    Delta check (differences between successive values)
  Event(s) to generate

## Slide 271: ST[12] – Important concepts
Parameter Monitoring Checking Status
Each parameter check has an associated state-machine
Checked
Invalid
Valid
Expected Value
Unexpected Value
Unchecked
Expected-value Check
Notes: While presenting the state machine, it is also interesting to indicate what happens during the transitions and what causes them:
- All transitions are recorded for reporting in a 12,12 packet;
- All transitions to unexpected value, below low (limit/threshold) and above high (limit/threshold) lead to the generation of the associated event notification, if any.

## Slide 272: ST[12] – Important concepts
Checked
Invalid
Valid
Below Low Limit
Above High Limit
Unchecked
Within Limits
Parameter Monitoring Checking Status
Each parameter check has an associated state-machine
Limit / Delta Check
Notes: While presenting the state machine, it is also interesting to indicate what happens during the transitions and what causes them:
All transitions are recorded for reporting in a 12,12 packet;
All transitions to unexpected value, below low (limit/threshold) and above high (limit/threshold) lead to the generation of the associated event notification, if any.

## Slide 273: ST[12] – Important concepts
Parameter Monitoring Example
Interval: 1s
Check 1:
  17 <= T° <= 22 Warning if out of range #rep = 2
Check 2: 15 <= T° <= 25 Alert if out of range #rep = 3
t = 13s  warning event
t = 17s  alert event
Notes: Some variations on this example scenario can be explained:
If after the generation of the warning event, two samples had been within the limits of check 1, it would have been regenerated one second before the alert event
If a value alternates below low and above high samples, PUS A would assign a new checking status, while PUS-C does not. This change is not intended and will result in a change request towards PUS-C.

## Slide 274: ST[12] – Message types, 1
system | interface | message type |  |  |  |  | 
6.12.3.5.1 | 8.12.2.15 | TC[12,15] |  |  |  | enable the parameter monitoring function | minimum
6.12.3.5.2 | 8.12.2.16 |  | TC[12,16] |  |  | disable the parameter monitoring function | minimum
6.12.3.6.1 | 8.12.2.1 | TC[12,1] |  |  |  | enable parameter monitoring definitions | minimum
6.12.3.6.2 | 8.12.2.2 |  | TC[12,2] |  |  | disable parameter monitoring definitions | minimum
6.12.3.7 | 8.12.2.12 | TM[12,12] |  |  |  | check transition report | minimum
6.12.3.8 | 8.12.2.3 | TC[12,3] |  |  |  | change the maximum transition reporting delay | by declaration
6.12.3.9.1 | 8.12.2.5 | TC[12,5] |  |  |  | add parameter monitoring definitions | by declaration
6.12.3.9.1b |  |  | if TC[12,5], at least one of: TC[12,4] TC[12,5] |  |  |  | implied by TC[12,5]
6.12.3.9.2 | 8.12.2.4 |  |  | TC[12,4] |  | delete all parameter monitoring definitions | by declaration
6.12.3.9.3 | 8.12.2.6 |  |  | TC[12,6] |  | delete parameter monitoring definitions | by declaration
6.12.3.9.4 | 8.12.2.7 | TC[12,7] |  |  |  | modify parameter monitoring definitions | by declaration
6.12.3.10 | 8.12.2.8 |  | TC[12,8] |  |  | report parameter monitoring definitions | requires TC[12,5] or TC[12,7]
6.12.3.10 | 8.12.2.9 |  |  | TM[12,9] |  | parameter monitoring definition report | TC[12,8] response
6.12.3.11 | 8.12.2.13 |  | TC[12,13] |  |  | report the status of each parameter monitoring definition | requires TC[12,1]
6.12.3.11 | 8.12.2.14 |  |  | TM[12,14] |  | parameter monitoring definition status report | TC[12,13] response
6.12.3.12 | 8.12.2.10 | TC[12,10] |  |  |  | report the out-of-limits | by declaration
6.12.3.12 | 8.12.2.11 |  |  |  | TM[12,11] | out-of-limits report | TC[12,10] response
Parameter monitoring subservice

## Slide 275: ST[12] – Implementation guidelines
Monitoring can be enabled or disabled at parameter of function level
  Both levels must be enabled for a monitoring check to be performed
  Enabling/disabling a level does not affect the other
To avoid generating too many reports, check transition notifications are gathered in a single report and sent upon reaching a pre-defined number of transitions or after a configurable maximum reporting delay, whichever comes first
Multiple ways to obtain monitoring status
  Event reports generated upon transitions
  Check transition reports
  Out of limits reports

## Slide 276: ST[12] – Implementation guidelines
What happens if ?
 change request against PUS-C has been raised !
Notes: Figure should show nominal in green, first warning/danger repetition in grey
Arnaud to raise change request vs PUS-C. Refer to PUS-C draft from 20130517 “out of limits oscillating”, see PUS-A page 11, bullet b, 3rd paragraph
in this case, the first warning repetition is “warning too low”, the second is “warning too high”
similar for danger

## Slide 277: ST[12] – Important concepts
Functional monitoring definition
Functional monitoring definition identifier
Optional validity condition (parameter/mask/value)
Identifier of the event definition to raise in case of detection
The minimum number of failed parameter monitoring conditions to trigger the functional monitoring
A set of parameter monitoring definition identifiers

## Slide 278: ST[12] – Important concepts
Functional Monitoring Checking Status
Each functional check also has an associated state-machine
Checked
Invalid
Valid
running
failed
Unchecked
Functional Monitoring Checking Status
Notes: Note that the number of transitions between functional monitoring checking statuses is lower than parameter monitoring checking statuses

## Slide 279: ST[12] – Message types
system | interface | message type |  |  |  |  | 
6.12.4.4.1 | 8.12.2.17 | TC[12,17] |  |  |  | enable the functional monitoring function | minimum
6.12.4.4.2 | 8.12.2.18 |  | TC[12,18] |  |  | disable the functional monitoring function | minimum
6.12.4.5.2 | 8.12.2.19 | TC[12,19] |  |  |  | enable functional monitoring definitions | minimum
6.12.4.5.3 | 8.12.2.20 |  | TC[12,20] |  |  | disable functional monitoring definitions | minimum
6.12.4.6.1 | 8.12.2.21 | TC[12,21] |  |  |  | protect functional monitoring definitions | by declaration
6.12.4.6.2 | 8.12.2.22 |  | TC[12,22] |  |  | unprotect functional monitoring definitions | implied by TC[12,21]
6.12.4.7.1 | 8.12.2.23 | TC[12,23] |  |  |  | add functional monitoring definitions | by declaration
6.12.4.7.2 | 8.12.2.24 |  | TC[12,24] |  |  | delete functional monitoring definitions | implied by TC[12,23]
6.12.4.8 | 8.12.2.25 |  | TC[12,25] |  |  | report functional monitoring definitions | requires TC[12,23]
6.12.4.8 | 8.12.2.26 |  |  | TM[12,26] |  | functional monitoring definition report | TC[12,25] response
6.12.4.9 | 8.12.2.27 | TC[12,27] |  |  |  | report the status of each functional monitoring definition | by declaration
6.12.4.9 | 8.12.2.28 |  |  |  | TM[12,28] | functional monitoring definition status report | TC[12,27] response
Functional monitoring subservice

## Slide 280: ST[12] – Tailoring & deployment
An on-board monitoring service:
  Must contain exactly one parameter monitoring subservice
  May contain up to one functional monitoring subservice
  Must be associated to a single event reporting subservice

## Slide 281: ST[12] – Implementation guidelines
Functional monitoring protection
Functional monitoring can be used to implement subsystem level FDI, and can therefore be critical
Some functional monitoring definitions can therefore be protected
This has implications at functional monitoring and parameter monitoring levels:
  A protected functional monitoring definition cannot be deleted
  Any parameter monitoring definition involved in a protected functional monitoring cannot be:
    Disabled
    Modified
    Deleted

## Slide 282: ST[12] – PUS-A to PUS-C evolution
Added features
New commands for parameter monitoring subservice:
  Report PMON status – TC[12,13], TM[12,14]
  Report subservice status – TC[12,15], TM[12,16]
New functional monitoring subservice:
  Enable/Disable functional monitoring – TC[12,17], TC[12,18]
  Enable/Disable individual FMON – TC[12,19], TC[12,20]
  Protect/Unprotect FMON – TC[12,21], TC[12,22]
  Add/Delete PMON to/from FMON – TC[12,23], TC[12,24]
  Report FMON definition – TC[12,25], TM[12,26]
  Report FMON status – TC[12,27], TM[12,28]
Deleted features
None
Updated features
Main identifier Parameter ID is replaced by Monitoring ID TC[12,1], TC[12,2], TC[12,5] to TC[12,7], TC[1M,9], TC[12,11], TM[12,12]
Restriction on monitoring event severity lifted
Notes: The parameter monitoring subservice is largely unchanged in its spirit. Using a monitoring id to identify monitors was already widespread before standardisation.
The added commands for this subservice provide additional observability in the same way as for housekeeping: PMON status is not appropriate as service observables because of dynamic definition and quantity of parameters. The second is more discutable (it could be a service observable), but the option to use a report has been kept.
The major change to the monitoring service comes from the addition of the functional monitoring subservice, which allows defining logical combinations of parameter monitorings

## Slide 283: ST[26] – Parameter extraction
New service to be introduced in revision 1
Functionality to capture any part of a routed report as a parameter
Can be used e.g. to perform centralised monitoring of parameters coming from different instruments
Uses the same granularity as other routing services (ST 14 and 15), i.e. parameters can be extracted from a specific (APID, type, subtype) combination, or any specific housekeeping or event packet.
Offsets to identify parameter locations in the extracted packet are provided as part of the parameter extraction definition; parameter size and type are implicitly deduced from the target parameter definition used for the extraction

## Slide 284
PUS for 
FDIR – asynchronous events & on-board actions

## Slide 285: SET – FDIR and asynchronous events
FDIR and asynchronous events
The standard service types gathered in this set manage the detection, reporting and autonomous action on asynchronous on-board generated events.
Such asynchronous events can be generated by on-board applications to notify the occurrence of any operationally significant event. The on-board monitoring service, presented in set three, is a producer of such events, and is therefore relisted in this set.
The PUS standard provides capabilities to report these on-board events as well as controlling their reporting. In addition, it allows registering on-board actions which can be executed anytime a specific event is detected.
This set of services provides the tools to implement a first line satellite FDIR (Fault Detection, Isolation and Recovery).
ST[01] | request verification | 
ST[02] | device | 
ST[05] | event reporting | 
ST[08] | function management | 
ST[09] | time management | 
ST[12] | on-board monitoring | 
ST[19] | event-action | 

## Slide 286: FDIR scenario
Service 12 : Monitoring
Event Reporting Service
PUS (5,2) packet
Event-action Service
PUS (5,4) packet
Shutdown TC
Packet Forwarding Service
On-board Storage Service
Event log
Critical event log
Event notification
Event notification

## Slide 287: ST[05] – Event reporting
ST[05] scope
The event reporting service provides the capability to report information of operational significance which is not explicitly provided within the provider-initiated reports of another service.
The service covers the requirements for reporting of events such as:
on-board failures and anomalies, including anomalies detected by a failure detection, isolation and recovery (FDIR) function;
initiation, progress and completion of activities initiated either from ground or autonomously on-board;
hardware device built-in test results;
normal payload events.
FDIR and asynchronous events |  | 
ST[05] | event reporting | √
ST[19] | event-action | 

## Slide 288: ST[05] – Standardized subservice type
Event reporting
Each event that occurrences can be caught by the event reporting subservice and reported is associated to an event report type.
Each event report type specifies the severity level of the event to report (informative, low severity, medium severity or high severity).
To facilitate ground system detection and routing the severity level is indicated by the message type of the generated report.
Each event is also associated to an event definition. An event definition is identified by an event definition identifier that is unique within the application process that generates the corresponding event reports. Auxiliary data can be associated to each event definition to report the context and the cause of the event occurrence.
The event reporting subservice type includes optional capability to selectively enable and disable the generation of its event reports.
Event reporting service

## Slide 289: ST[05] – Overview
Report information of operational significance not explicitly provided in other reports
Uniquely identified by its Event Definition ID (EDID); auxiliary data provides additional context.
4 Severities
  [5,1] Normal/Progress report : Notifies an on-board autonomous action, which does not relate to a fault condition
  [5,2] Anomaly report – low severity: Notifies an anomaly which ground should be aware of, although it does not require an immediate action
  [5,3] Anomaly report – medium severity: Notifies an anomaly which ground should be aware of and take action to restore functionality
  [5,4] Anomaly report – high severity: Notifies a critical anomaly which requires an on-board action (e.g. autonomous reboot)
Notes: Although event reporting is presented in the FDIR section of this course, it has to be noted that service 5 is not stricly limited to FDIR: In addition to on-board anomalies, event reports can be used for reporting any relevant information, such as:
Initiation, progress and completion of activities initiated either from ground or autonomously on-board;
Hardware devices built-in test results
Normal payload events

## Slide 290: ST[05] – Message types
system | interface | message type |  |  |  | 
6.5.4 | 8.5.2.1 | TM[5,1] |  |  | informative event report | minimum
6.5.4 | 8.5.2.2 | TM[5,2] |  |  | low severity anomaly report | minimum
6.5.4 | 8.5.2.3 | TM[5,3] |  |  | medium severity anomaly report | minimum
6.5.4 | 8.5.2.4 | TM[5,4] |  |  | high severity anomaly report | minimum
6.5.5.2 | 8.5.2.5 | TC[5,5] |  |  | enable the report generation of event definitions | by declaration
6.5.5.3 | 8.5.2.6 |  | TC[5,6] |  | disable the report generation of event definitions | implied by TC[5,5]
6.5.5.4 | 8.5.2.7 |  | TC[5,7] |  | report the list of disabled event definitions | requires TC[5,5]
6.5.5.4 | 8.5.2.8 |  |  | TM[5,8] | disabled event definitions list report | TC[5,7] response
Event reporting subservice

## Slide 291: ST[05] – Tailoring & deployment
An event reporting service may contain multiple event reporting sub-services deployed on multiple on-board application processes
In general, the event reporting service follows a distributed approach, which each event source deploying its own event reporting subservices.
In all cases, events must be uniquely identified using the APID, event definition ID couple.

## Slide 292: ST[05] – Implementation guidelines
In most deployments, all applications may generate events; an event report is identified by its (APID,EDID) pair.
Auxiliary data must be fully determined by this identification.
It has been chosen to standardize the reporting of disabled event reports rather than enabled ones, as it is expected that most event reports will always be enabled.

## Slide 293: ST[05] – PUS-A to PUS-C evolution
Added features
Report disabled event definitions – TC[5,7], TM[5,8]
Deleted features
None
Updated features
None
Notes: Service 5 is mainly unchanged. Only one observability functionality has been added.

## Slide 294: ST[19] – Event-action
ST[19] scope
The event-action service provides the capability to define on-board actions that can be autonomously executed when specific on-board events occur.
This service is associated to one or more event reporting services and has the visibility of all event reports generated by these services.
The event-action service can be configured to react to any related event reports, by initiating the execution of the request (i.e. an action) that is associated to that event report. Such requests can, for example, directly reconfigure hardware, start an on-board control procedure or start a request sequence.
This service is an extension of the ground monitoring and control. As such, the application processes that execute the requests issued by the event-action service directly send the request verification reports, if any, to the ground.
Standard Service Types |  | 
ST[05] | event reporting | 
ST[19] | event-action | √

## Slide 295: ST[19] – Standardized subservice type
Event-action
The event-action subservice type includes the capability to maintain a list of event-action definitions.
Each event-action definition relates to an event (by means of the corresponding event definition identifier) and the corresponding request (i.e. the action).
The subservice reacts to any event occurrence by initiating the execution of the associated request. Such requests can, for example, directly reconfigure hardware, start an on-board control procedure or start a request sequence.
Event-action service
extension of the ground monitoring and control

## Slide 296: ST[19] – Overview
On-board actions autonomously executed upon occurrence of specific on-board events
This service monitors event reports generated by the event reporting subservices, and releases the associated requests upon detection
On-board events identified with their (APID,EDID) pair
The action can be any request

## Slide 297: ST[19] – Important concepts
The event action service detects and reacts on event reports
  This implies that if reporting of an event is disabled, any event action that would be associated to this event will not be triggered
The standard specifies that the request that is registered as an action can be any request
  Requests released by the event action subservice are not generated by that subservice, but rather by the source that initiated the “add event-action definition request”
  Requests are released “as is” by the event action – verifications can be implemented as part of the “add event-action definition” request. Otherwise, they will be checked on release as any other telecommand
  Service 1 reports for requests registered as event actions should be expected by ground.
Notes: Some implementations may choose to represent and manipulate events in a dedicated way. While the standard does not preclude such kind of implementation, it is important to clarify that an event action cannot be triggered if the corresponding event is not reported.

## Slide 298: ST[19] – Message types
system | interface | message type |  |  |  | 
6.19.6.1 | 8.19.2.8 | TC[19,8] |  |  | enable the event-action function | minimum
6.19.6.2 | 8.19.2.9 |  | TC[19,9] |  | disable the event-action function | minimum
6.19.7.1 | 8.19.2.4 | TC[19,4] |  |  | enable event-action definitions | minimum
6.19.7.2 | 8.19.2.5 |  | TC[19,5] |  | disable event-action definitions | minimum
6.19.8.1 | 8.19.2.1 | TC[19,1] |  |  | add event-action definitions | minimum
6.19.8.2a |  |  | at least one of: TC[19,2] TC[19,3] |  |  | implied by TC[19,1]
6.19.8.3 | 8.19.2.2 |  | TC[19,2] |  | delete event-action definitions | by declaration
6.19.8.4 | 8.19.2.3 |  | TC[19,3] |  | delete all event-action definitions | by declaration
6.19.8.5 | 8.19.2.6 | TC[19,6] |  |  | report the status of each event-action definition | by declaration
6.19.8.5 | 8.19.2.7 |  | TM[19,7] |  | event-action status report | TC[19,6] response
6.19.8.6 | 8.19.2.10 | TC[19,10] |  |  | report event-action definitions | requires TC[19,1]
6.19.8.6 | 8.19.2.11 |  |  | TM[19,11] | event-action definition report | TC[19,10] response
Event-action subservice

## Slide 299: ST[19] – Tailoring & deployment
An event action service may contain multiple event action sub-services deployed on multiple on-board application processes
It is common to have a centralised event-action service that is able to detect the events produced by multiple event reporting.
The list of checks to be performed on the requests contained within the event actions is part of the subservice specification.

## Slide 300: ST[19] – PUS-A to PUS-C evolution
Added features
New command to enable/disable the overall event action status – ST[19,8], ST[19,9]
Deleted features
None
Updated features
Complete telecommand added to TC[19,7] for increased observability

## Slide 301: ST[19] – Implementation guidelines
Since any request can be recorded as an action, several other services can complement the event-action service for more complex action scenarios:
  Service 21 (Request Sequencing) allows associating more than one request to an event through the execution of a request sequence. The action to register is the activation of that sequence;
  Service 18 (OBCP) allows even more on-board intelligence through the execution of a procedure. The action to register is either the activation of that sequence, or a load & activate command (e.g. if the procedure is kept in a file and not permanently loaded)
Notes: Presenter should take the opportunity of this slide to remind the existence of the « shortcut » commands present in the OBCP service, such as « load & activate », as it illustrates why these commands exist in the first place.

## Slide 302: Overall FDIR – Implementation guidelines
The PUS-C standard offers a comprehensive toolbox for implementing the spacecraft FDIR through parameter and functional monitoring, event reporting, event action, request sequencing and OBCPs. Nevertheless, FDIR is a complex topic, and most missions will not be able to exclusively rely on these services. In particular:
Most very low level FDIR is executed by hardcoded processes, possibly raising flags and/or event reports upon detection
Missions implementing their high-level FDIR using functional monitoring gain in configurability and flexibility, but design solutions needed to be found to avoid multiple recoveries to trigger and possibly conflict
At least two missions implement a safety that will temporarily disable the functional monitoring when an FMON has triggered to avoid conflicting recoveries.

## Slide 303
PUS for 
Commanding – hardware & software functions

## Slide 304: SET – Hardware and software functions
Hardware and software functions
This set of standard service types contain the capabilities to access hardware and software functions provided on-board.
Software and hardware functions fundamentally vary from mission to mission, and the services described in this set are those identified as being common to all of them. It is generally this category of services which will be extended through private service types as presented in the PUS foundation model.
The standard provides a standardized service to access hardware devices at physical and logical level, and another for software functions.
Time management is isolated in a specific service, as time synchronization needs deserve a particular status.
ST[01] | request verification | 
ST[02] | device access | 
ST[08] | function management | 
ST[09] | time management | 

## Slide 305: ST[02] – Device access
ST[02] scope
The device access service provides the capability of distributing commands to and acquiring data from the on-board devices.
An on-board device can be any on-board entity which can be configured by means of commands or which is able to generate data.
Hardware and software functions |  | 
ST[02] | device access | √
ST[08] | function management | 
ST[09] | time management | 

## Slide 306: ST[02] - Standardized subservice type
Device access
The device access subservice type provides capabilities to interact with:
on-board devices such as actuators, sensors, transponders and equipment that have no direct support for PUS services;
equipment during the assembly, integration and test phases or in-flight trouble-shooting, e.g. to validate the basic communication capabilities.
The device access service type supports addressing devices physically or logically. Physically accessing a device implies knowledge of the transmission link and of the communication protocol. Logically accessing a device can be done with a command identifier and its parameters. The on-board software maps this logical information onto the physical link and protocol.
A typical example is the low-level commanding of a Mil-Std-1553B bus remote terminal:
to command it as a ‘physical device’, the command word is specified, containing the address, the transmission direction, the sub-address and the data word count.
On the other hand, to command the same remote terminal as a ‘logical device’, the logical device identifier, the logical command and its associated parameters are specified. It is the task of the service to map such a command onto the right communication protocol and physical link.
Device access service

## Slide 307: ST[02] – Overview
Distribute commands to and acquire data from on-board devices such as:
  Actuators, sensors, transponders or other equipment not providing direct support for PUS services
  Equipment during AIT or for in-flight troubleshooting to validate basic communication capabilities
Low level access: Bypasses the nominal on-board software functions
Type of requests:
  On-off commands for devices
  Register load / dump
  Distribute CPDU commands
  Physical device low level command / acquisition request
  Logical device low level command / acquisition request

## Slide 308: ST[02] – Important concepts
On-off device commands
  Bi-level signals connected to a particular device, and identified by an hardware address
  Addressing the on-off device triggers a pulse on that line
  Examples: Switch on or switch off lines for devices; open or close latch valves; switch a relay.
Registers
  Software or hardware exchange areas identified by their addresses
  Loading a value to or acquiring a value from a register may trigger a hardware process
  Some registers may only support loading or reading
CPDU (Command Pulse Distribution Unit)
  Particular kind of pulses generally related to powering or resetting devices
  Has a specific access point at TC decoder level (« Hardware TCs »)
  Device access subservices implements Software CDPU, i.e. the capability to perform the same actions as direct, hardware-level CPDUs.
Notes: Detailed definitions of each device access type

## Slide 309: ST[02] – Important concepts
Physical device
  Device which can be accessed using explicit knowledge of the transmission link and the transmission protocol
  For example, for a GPS accessed through a MIL-1553B bus, the request has to include the 1553 command word (containing RT address, transaction direction, RT sub-address and word count), and the command to perform (e.g. update configuration) is specified in its raw form, as transmitted on the transmission link.
Logical device
  Device which can be accessed using a higher-level description
  In that case, the mapping to physical is performed by the software implementing the corresponding service
  In the same example, the accessed GPS is only identified through a device ID, and the command to perform is provided as a command identifier and its parameters
These two types of accesses are not mutually exclusive

## Slide 310: ST[02] – Message types
system | interface | message type |  |  |  |  |  |  |  | 
6.2.3a |  | at least one of: TC[2,1] TC[2,2] TC[2,4] TC[2,7] |  |  |  |  |  |  |  | minimum
6.2.4.2 | 8.2.2.1 | TC[2,1] |  |  |  |  |  |  | distribute on/off device commands | by declaration
6.2.5.2 | 8.2.2.2 | TC[2,2] |  |  |  |  |  |  | distribute register load commands | by declaration
6.2.5.3 | 8.2.2.4 |  | TC[2,5] |  |  |  |  |  | distribute register dump commands | requires TC[2,2]
6.2.5.3 | 8.2.2.5 |  |  | TM[2,6] |  |  |  |  | register dump report | TC[2,5] response
6.2.6.2 | 8.2.2.3 | TC[2,4] |  |  |  |  |  |  | distribute CPDU commands | by declaration
6.2.7.1.2 | 8.2.2.6 | TC[2,7] |  |  |  |  |  |  | distribute physical device commands | by declaration
6.2.7.1.3 | 8.2.2.7 |  |  |  | TC[2,8] |  |  |  | acquire data from physical devices | implied by TC[2,7]
6.2.7.1.3 | 8.2.2.8 |  |  |  |  | TM[2,9] |  |  | physical device data report | TC[2,8] response
6.2.7.2.2 | 8.2.2.9 |  |  |  | TC[2,10] |  |  |  | distribute logical device commands | requires TC[2,7]
6.2.7.2.3 | 8.2.2.10 |  |  |  |  |  | TC[2,11] |  | acquire data from logical devices | implied by TC[2,10]
6.2.7.2.3 | 8.2.2.11 |  |  |  |  |  |  | TM[2,12] | logical device data report | TC[2,11] response
Device access subservice

## Slide 311: ST[02] – Tailoring & deployment
A device access service may contain multiple device access sub-services deployed on multiple on-board application processes
In general, the deployment choices will be in accordance with the accessibility of the hardware to be commanded by the corresponding subservice

## Slide 312: ST[02] – Implementation guidelines
Some overlap may exist between service 2 (device access) and service 6 (memory management) with respect to accessing register contents, in particular for memory-mapped devices:
  If registers are mapped to a memory area available through direct memory addressing, service 6 is suitable for accessing them;
  On the contrary, service 2 allow accessing registers that may not otherwise be accessible
  If reading registers may trigger hardware processes, it is recommended that these registers are accessed through the device access service
Notes: For the last bullet, even if required by the standard, using service 2 indicate proximity of the hardware where it is generally known that reading registers may have side effects (e.g. resetting the read value). This is not so obvious for a ‘simple’ memory read operation

## Slide 313: ST[02] – PUS-A to PUS-C evolution
Added features
TC[2,4] introduced for software commanding of CPDU
TC[2,5] and TC[2,6] Register dump commands
TC[2,7] to TC[2,9] Physical device commands & acquisitions
TC[2,10] to TC[2,12] Logical device commands & acquisitions
Deleted features
None
Updated features
TC[2,3] CPDU, interpreted at TC decoder level, has never really been a PUS compliant type of telecommand.
PUS-C still defines TC[2,3] but in a separate clause (Clause 9)
Notes: The only modification of service 2 is a clarification of the CPDU distribution. Having the hardware telecommands in the scope of the PUS was not logical, as the software never sees them. A software counterpart has however been added, as it is common to have the software allowed to trigger the CPDUs in addition to the hardware controller.
In addition, direct communication with devices has been added. Two levels are available. See previous slide for distinction between logical level and physical level commanding.

## Slide 314: ST[09] – Time management
ST[09] scope
All satellites maintain a satellite time reference, which can be downlinked in time reports generated by the time management service. The ground segment can perform a correlation between the reported satellite time and the UTC (coordinated universal time) used by the ground segment.
Service focused on the production of time reports
These time reports are used on ground to synchronize the on-board time with the UTC time
Hardware and software functions |  | 
ST[02] | device access | 
ST[08] | function management | 
ST[09] | time management | √

## Slide 315: ST[09] – Standardized subservice types
Time reporting subservice
Capability to generate the time reports
Two mutually exclusive time formats: CUC or CDS
Rate of generation of time reports tied to the rate of generation of the telemetry frames on VC0
Time reporting control subservice
Allows modifying the rate of production of the time reports
Setting as power of 2
Time management service

## Slide 316: ST[09] – Important concepts
Time formats defined by CCSDS 301.0-B-4
Two supported time representations
CUC (CCSDS Unsegmented Time Code)
  Continuous time counter counter
  Coarse part represents seconds
  Variable size: up to 4 bytes coarse and 3 bytes fine
CDS (CCSDS Day Segmented Time Code)
  Separated into day, ms, µs fields
  µs field is optional
Many other time representations exist (CCS, GPS, …), but only these two are natively supported by PUS
C1 | C2 | C3 | C4 | F1 | F2 | F3
1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet
day | ms of day | µs of ms
2 octets | 4 octets | 2 octets
Notes: CCS refers to CCSDS calendar Segment Time Code: CCSDS 301x0b2.pdf
GPS also has a week field, counting from Jan 6th 1980.

## Slide 317: ST[09] – Message types
system | interface | message type |  | 
6.9.4.1a |  | exactly one of: TM[9,2] TM[9,3] |  | minimum
6.9.4.2 | 8.9.2.2 | TM[9,2] | CUC time report | by declaration
6.9.4.3 | 8.9.2.3 | TM[9,3] | CDS time report | by declaration
Time reporting subservice
Time reporting control subservice
system | interface | message type |  | 
6.9.5.1.1 | 8.9.2.1 | TC[9,1] | set the time report generation rate | minimum

## Slide 318: ST[09] – Tailoring & deployment
A spacecraft shall contain exactly one time management service
The time management service shall contain:
  Exactly one time reporting subservice
  Up to one time reporting control subservice

## Slide 319: ST[09] – Implementation guidelines
Time reports
Time reports use a dedicated APID (0)
They have no secondary header (and therefore, their type and subtype, (9,2) and (9,3), never appear in the corresponding packet)
Time reporting rate
Reporting rates that are set through the time reporting control subservice are exponential (2rate)
These are expressed in the number of telemetry frames between two consecutive time reports. The time between two reports is therefore dependent on the telemetry throughput.

## Slide 320: ST[09] – PUS-A to PUS-C evolution
Added features
CDS time report – TM[9,3]
Deleted features
None
Updated features
None
Notes: Service 9 is unchanged for existing services. Only an additional representation of the time report has been added.

## Slide 321: ST[08] – Function management
ST[08] scope
The function management service provides means to interact with application process related software functions that are not provided by other standardized services.
These functions relate to the specialized role assigned to the application process on-board the spacecraft, for example, responsibility for controlling the operation of a payload instrument or an AOCS subsystem. The nature of this control can vary quite considerably and is not prescribed or constrained in any way by this Standard. It can cover all on-board nominal operations for subsystems and payloads including predefined mode change operations.
-----------------
It is noted that the PUS service type concept addresses the semantics of related services. This is true for all standardized service types except service type 8 that, in fact, only focuses on offering a very generic mean to call a software function on-board, whatever that function is. The standardization obsolescence of that service is announced in PUS-C
Hardware and software functions |  | 
ST[02] | device access | 
ST[08] | function management | √
ST[09] | time management | 
Notes: In some missions, service 8 represents more than 50 % of all available commands.
The function management service is kept in the standard for backward compatibility reasons
It is highly recommended to develop mission specific service types (or mission specific subtypes of standard service types) instead of relying on this service

## Slide 322: ST[08] - Standardized subservice type
Function
provide the capability to execute application process specific function, identified by a function ID
provides a single request type for that purpose. That request type allows arguments to be provided
Function management service

## Slide 323: ST[08] – Message types
system | interface | message type |  | 
6.8.4 | 8.8.2.1 | TC[8,1] | perform a function | minimum
Function management subservice

## Slide 324
PUS for 
Extensions

## Slide 325: PUS Service types - Extensions
The PUS foundation model defines rules for extending the standard
Private service types 
ST[128] to ST[255]
for example for payload commanding, science data handling or AOCS control
Private message types 
TM/TC[n,128] to TM/TC[n,255] with
TM/TC[n,1] to TM/TC[n,255] with
  for example for mission specific packet store handling, specific time management such as GPS synchronization, housekeeping report compression (POCKET)

## Slide 326
Providing Feedback

## Slide 327: PUS – Providing Feedback
  Noticed an error ? Something needs clarification ?
Do not hesitate to register on www.ecss.nl !
  Once registered, open change requests can be viewed at
  http://www.ecss.nl/ecss-change-requests/
  New change requests can be submitted using the form at
  http://www.ecss.nl/standards/change-requests/

## Slide 328: PUS – Providing Feedback

## Slide 329: PUS – Providing Feedback
What to provide in a change request ?
Document number/date: The complete ECSS reference number & date of the document
Organization: The organisation from which you depend (industry is represented by EUROSPACE)
Location: Clause, Table or Figure number
Page: Page number
Description: Description of the proposed change – Identify the improvement, preferably in a from – to approach
Justification: Purpose, reasons and benefits of the proposed change

## Slide 330: PUS – Pending change requests
1. Foundation: On-board condition codes
Impacted requirements: 5.3.5.2.3.g
Problem: The note attached to the requirement says “for each request-specific successful start of execution condition to notify, a code value that refers to that condition”. No such code exists for successful checks, only for failed checks. A similar problem exists for each successful condition in the same note
Recommended update: Remove the reference to successful conditions in this note.

## Slide 331: PUS – Pending change requests
    2. Foundation: Responses not fitting a CCSDS packet
Impacted requirements: 5.4.11.3.2.b and its references (6.6.3.4.c.3, 6.6.4.5.c.4)
Problem: This requirement says that a request which would generate a packet that would exceed the maximum size of a CCSDS space packet must be rejected. While it is agreed that all packets must fit in the CCSDS packet protocol, OIRDs generally require capability for some large data dumps (in particular, for service 6, where it is requested that it is possible to dump the complete memory using a single command). In that case, the service is responsible for generating as many reports as necessary.
Recommended update: Reword 5.4.11.3.2.b to forbid the generation of packets larger than the maximum CCSDS space packet size, but to allow the existence of service-specific mechanisms to handle such requests

## Slide 332: PUS – Pending change requests
    3. Incorrect capability reference in service 2
Impacted requirements: 6.2.3.a.4
Problem: This capability is referred to as “the capability for physical devices commanding access specified in clause 6.2.7”. The capability name is “Physical and logical device access”.
Recommended update: Replace 6.2.3.a.4. with “the capability for accessing physical and logical devices specified in clause 6.2.7”.

## Slide 333: PUS – Pending change requests
    4. Implicit capability types
Impacted requirements: 6.11.9.1.a, 6.11.10.1.a, 6.22.11.1.a, 6.22.12.1.a
Problem: These requirements do not fit in the foundation model, which expresses that a capability type is either an inclusive-or capability type (requiring that at least one of several listed capabilities is implemented) or a transaction-defining capability type (which is directly linked to an associated transaction type). The requirements listed above are not part of those two categories and violate the constraint.
Recommended update: The four requirements mentioned above do not bring any added value in terms of specification, as it is implicitly verified upon selection of the implemented service subtypes. Recommendation is to keep this information, but not as a requirement (informative text)

## Slide 334: PUS – Pending change requests
    5. Monitoring: loss of functionality w.r.t. PUS A
Impacted requirements: 6.12.3.6.3.c.3.b
Problem: In PUS A, when performing a limit check, a new checking status would be established if the current status is within limits and the parameters samples alternatively between below low and above high limits. This behaviour is lost in PUS-C, where a NREP number of consistent samples are required.
Recommended update: Restore this functionality, without trying to create a specific state “oscillating”. Simply assign the new checking status according to the last value that causes the state change, counting all out of range values in the NREP.

## Slide 335: PUS – Pending change requests
    6. Inconsistency in service 22 scope
Impacted requirements: 6.22.1.1, 6.22.4.b
Problem: The service scope says “The service type does not specify how the orbit positions are determined; this is done when tailoring the service to the mission”. However 6.22.4.B defines the angle to use.
Recommended update: Make consistent by either removing this sentence in the scope, or by removing 6.22.4.b so that the orbit position can be freely determined by the mission.

## Slide 336: PUS – Pending change requests
    7. Service 22 position definition
Impacted requirements: 6.22.4.b
Problem: The position within the orbit is defined as “the angle measured in the plane of the osculating inertial orbit starting from the intersection with the Earth Fixed Equatorial Plane”. Two such intersections exist, at the ascending and descending nodes.
Recommended update: Clearly identify the origin by specifying the node.

## Slide 337: PUS – Pending change requests
    8. TM [15,13] repeated parameters
Impacted requirements: 8.15.2.10.b
Problem: The ‘repeated N times’ scope of the requirement does not properly reflect the fact that the packet store id information is given for each store, as required by 6.15.3.10.1.g.1.
Recommended update: Extend the scope of the ‘repeated N times’ on top of the interface definition so that it also covers packet store ID.

## Slide 338: PUS – Pending change requests
    9. TC/TM [15,30] to [15,40] repeated parameters
Impacted requirements: 8.15.2.27.b, 8.15.2.29.b, 8.15.2.30.b, 8.15.2.31.b, 8.15.2.37b
Problem: The ‘repeated N2 times’ scope of the requirement includes the N2 field which is the repetition factor for the following TC/TM: [15,30], [15,32], [15,33], [15,34], [15,40].
Recommended update: Reduce the scope of the ‘repeated N2 times’ on top of the interface definition so that it no longer covers N2.

## Slide 339: PUS – Pending change requests
    10. TC [18,7] parameter names
Impacted requirements: 8.18.2.7.b
Problem: Arguments and parameters are two different concepts for OBCPs. An argument is provided when starting the OBCP, while a parameter can be provided while it runs. The second field of this TC is named ‘argument values’, while the TC is “Communicate parameters to an OBCP”.
Recommended update: Change the second field name to ‘parameter values’ instead of ‘argument values’.

## Slide 340: PUS – Pending change requests
    11. TM [22,13] repeated parameters
Impacted requirements: 8.22.2.13.b
Problem: The ‘repeated N times’ scope of the requirement does not properly reflect the fact that the subschedule ID information is given for each request, as required by 6.22.9.1.b.
Recommended update: Extend the scope of the ‘repeated N times’ on top of the interface definition so that it also covers subschedule ID.

## Slide 341: PUS – Pending change requests
    12. TC [23,1] & TM [23,4] file attributes
Impacted requirements: 8.23.2.1.b, 8.23.2.4.b.
Problem: A ‘repeated N times’ bar is present above the ‘additional file attributes’ field, although no N field is present in the TC [23,1] & TM [23,4] packet structures.
Recommended update: Remove this ‘repeated N times’ bar.

## Slide 342: PUS – Pending change requests
    13. Reference of bit-strings (editorial)
Impacted requirements: Clause 8 - Generic
Problem: Bit strings are sometimes listed as “bit-string” or “fixed length bit-string” when used as a type in field descriptions.
Recommended update: Follow a consistent approach when using bit-strings.

## Slide 343: PUS – Pending change requests
    14. Representation of variable-length strings
Impacted requirements: 8.6.2.1.b, 8.6.2.19.b (examples only – generic concern)
Problem: The way variable strings are represented in clause 8 is not consistent. Strings of variable length, through their type definitions in clause 7, already include a length field. In some places this length field is explicit (e.g. TC[6,1]) while in others it is not (e.g. TC[6,19]).
Recommended update: Follow a consistent approach when using variable string fields.

## Slide 344: PUS – Pending change requests
    15. Capability dependency in service 12
Impacted section: Annex C.2.12.1
Problem: As stated, TC [12,5] implies at least one of TC [12,4] and TC [12,5]. This is obviously a typo.
Recommended update: Update this dependency so that TC [12,5] implies at least one of TC [12,4] and TC [12,6].

## Slide 345: PUS – Pending change requests
    16. Capability dependency in service 15
Impacted section: Annex C.2.15.1
Problem: TC [15,26] Change packet store type to circular, TC [15,27] Change packet store type to bounded, and TC [15,28] Change the virtual channel used by a packet store are indicated as being implied by TC [15,25] Resize packet store. This capability relationship is not correct.
Recommended update: Change capability dependency as follows:
  TC [15,25] by declaration
  TC [15,26] by declaration
  TC [15,27] implied by TC [15,26]
  TC [15,28] by declaration.

## Slide 346: PUS – Pending change requests
    17. Capability dependency in service 17
Impacted section: Annex C.2.17.1
Problem: Typo: TM [17,4] is indicated as being a response to TC[17,4].
Recommended update: Correct to indicate that TM [17,4] is a response to TC [17,3].

## Slide 347: PUS – Pending change requests
    18. Foundation: All subservice providers within same application process
Impacted section: 5.4.6
Problem: Some service types require that all subservice providers within that service are hosted by the same application process (e.g. service 6, as required by 6.6.2.2.a). The foundation model does not foresee anything to require the expression of such constraints
Recommended update: Create a new requirement in section 5.4.6, with a wording such as follows: “Whether all subservice providers of a service must be hosted by the same application process shall be declared when specifying that service type”.

## Slide 348: PUS – Pending change requests
    19. Foundation: Ordering of instructions
Impacted section: 5.4.11.2.1.f
Problem: This requirement imposes that the list of instructions is ordered. Most requests do not require that the instructions are executed in a specific order.
Recommended update: Update requirement 5.4.11.2.1.f so that the list does not need to be ordered, and require the request specification to include whether ordering is required.

## Slide 349: PUS – Pending change requests
    20. Service 13: inconsistency between functional and interface specification
Impacted section: 6.13.3.3.1.c.1.(a), 6.13.4.3.1.b.1.(a)
Problem: The way service 13 is specified is inconsistent with the foundation model. Indeed, a single request type and a single report type (uplink & downlink) are specified; within these request/report, a request argument indicates whether the part is the first, intermediate, or last. At interface level, this is mapped to three different subtypes for both directions.
Recommended update: Make functional and interface specifications consistent. Preferred solution is to keep the functional specification and update the interface (to one subtype per direction). The other possible solution is to update the functional specification so that it describes three different requests and reports.

## Slide 350: PUS – Pending change requests
    21. Service 1: Management of start of execution notifications
Impacted section: 6.1.5.1.1.b, 6.2.4.2.e and all similar
Problem: Requirement 6.1.5.1.1.b states that any received start of execution failure notification shall be reported in a report. 6.2.4.2.e (and all similar) states that a start of execution failure notification is generated for each instruction. This results in the generation of multiple start of execution failure reports (carried in TM[1,4]), which is definitely not the intention.
Recommended update: See attached.

## Slide 351
that’s it for today...

## Slide 352: Still to develop
Impact on SRDB, on EGS-CC, etc. updates of E-70-31, E-70-01, E-70-11, OIRD
System versus subsystems or PUS terminal (e.g. VCD for central software, for Payload) Verification Control Document (VCD requirements are established at PDR, CDR verification mainly at System Satellite CDR)
PUS-C DOORS module
PUS-Gen R&D
Consider PUS cloud, community website where we can find the normalised foundation model e.g. for SRDB development.
Add slide(s) explaining how now tailoring should be made and explain that tailoring the PUS should consist in adding mission specifics, ... resulting in first version on on-board requirements specifications (e.g. OBSW req. spec) and not just a tailored pus (as past and currently the case).

## Slide 353: PUS & OSRA on-board software reference architecture
Placeholder: Need to retrieve the most recent OSRA overall architecture figure and populate it with PUS deployment.
Placeholder: develop dependencies between service types, subservice types,...

## Slide 354: SAVOIR and Generic OIRD
Need to explain what the operators (interacting with EGSE and MCS) needs, i.e. not by just tailoring the PUS subservice entity providers but by specifying at system level the PUS service needs, implying what they expect from the subservice entity users (each user able to interact with many providers of the same subservice). recall discussions with ESOC operators related to Generic OIRD.
Jean-Loup and ESOC operators are in line: ESOC wish a single generic OIRD (tailoring the PUS). Jean-Loup SAVOIR group wish a generic on-board reference architecture.

## Slide 355: PUS Foundation – Instruction ≈ Request
t3  executing the schedule, the time-based schedule service generates the “on/off device command” instruction (request)
APID B
S18 ObcpM
APID A
S6 RDMM
ground application process
Space Segment
Ground Segment
subservice
provider
S6 RDMM
subservice
user
S6 RDMM
S18 ObcpM
OBCP
service
Memory
Management
Service
Raw Data
Memory
Management
subservice
OBCP Management Subservice